## Slide 1: Pattern making

## Slide 3: Pattern make - Set in B Modify from the pattern of Set in A (001)
Make the pattern of Set in A (001) and copy front and back body pattern. Modify them to Set in B.
Flip/Mirror Reverse back body.

## Slide 4
Merge/Line

## Slide 5
Delete seam allowances of both patterns ? = OK
Just in case seam allowance is already made.

## Slide 6
Input Guide Point for "Dropped Back Shoulder Placement" in measurement table.
Guide point/Perimeter
Draw an assist line from the neck point to the guide point.

## Slide 7
Divide/Line
Press "EXEC." on sub keyboard for execution.

## Slide 8
Rotate/Pattern/Horizontal
Pattern will be set upside down according to the angle of the pattern.
In this case, select the pattern by clicking it and press F3 key on sub keyboard or keyboard to turn back to the original angle.
The angle for F3 key is set to 180° in "Set/System Setting/Function Setting."

## Slide 9
When the shoulder line is not horizontally straight, it can be fixed by moving the point at corner.
Point/Move/"Horizontal/Vertical“

## Slide 10
It is required to keep same width for front and back on shoulder for better linking condition. * It is one example. Each company has their own way.

## Slide 11
Measure each width.
The measurement on front is wider by 2.9cm in this example.
Input guide point at 2.9cm to the left from shoulder point.
Pattern Line/Modify/Redraw Line
Modify the line considering the continuance between front and back body.
Delete unnecessary assist line.

## Slide 12
Measure the perimeter of sleeve cap and armhole then modify line to match the length if necessary.
Copy the sleeve then Flip/Mirror.
Merge/line
Delete center assist line if necessary.

## Slide 13
Cross Mark/Perimeter
Input 4.5cm which is the value of "Dropped Back Shoulder Placement" in measurement table. This position may be varied according to the measurement of armhole or sleeve cap after modification.

## Slide 14: Practice - Pattern make of Set in B Modify from the pattern of Set in A

## Slide 16
Make Set in A referring to size table002 and grading for all sizes then modify the pattern of Set in B.

## Slide 17
For this pattern there are two measurements for creating Set in B. One guide point (1.5 cm) will be input on the neck line.
The other guide point (3cm) will be input on the armhole on the back body.

## Slide 18: Yarn simulation

## Slide 19: Yarn sample

## Slide 20
Компьютер дээр бэлэн байгаа утасны загвараас сонгож сүлжих машин болон гейчийг тохируулан симуляци хийнэ.

## Slide 21
Симуляци урд ба ардаас харагдах ба бодитоор сүлжсэнтэй адил үр дүнтэй.

## Slide 22
Хэрэв өөрт байгаа утсаараа симуляци хийж үзэх бол утсаа эхлээд скайнердана. Скайнер болон зориулалтын утас тогтоогч, ар талын фон хэрэглэгдэнэ.

## Slide 23
Ар талын фон хар ба цагаан өнгөтэй байх ба утасны өнгөөс хамаарч ялгагдах талаар нь тохируулан тавьна.

## Slide 25: Scan
Normal image 200-300 dpi
Slub yarn 400 dpi
Slub yarn 400 dpi
Lame 400 dpi
Chenille 500 dpi
Twist mélange 500 dpi
Mohair 700 dpi
Thin yarn 800-1000 dpi
Cannot scan nep/space dyed yarn

## Slide 26
Скайнердсаны дараа цэвэрлэж арын фоноос салгана.

## Slide 29
References
https://www.shimaseiki.com
Shimaseiki training guide