## Slide 3: System Configuration
Body
Monitor
Sub-keyboard
Digitizer
Stylus pen

## Slide 4: Stylus Pen / Digitizer
The stylus pen can be used on the digitizer.
When the desk is a digitizer-built-in type, the pen stroke is recognized in the area outlined by the dotted red line.

## Slide 5: Sub-keyboard

## Slide 6: Sub-keyboard
Frequently-used functions are duplicated. A trackball can move and scroll the image easily. Refer to the final page
For maximum productivity, users can work with both hands. One hand can use the pen or mouse, and the other hand can use the sub-keyboard.

## Slide 7: Stylus pen

## Slide 8: Eye-ONE2
This is the color reader that can pick up colors directly from color samples.
To read a color, select "Reader" in the color menu.
Press the color reader's head onto the color sample and then click the black button located on the side of the color reader.

## Slide 9: Design software-Standard Screen

## Slide 10: Page list
A page is an opened window of an image file.
Even if many image files are opened, Page List allows users to switch pages easily, just like turning the pages of a book.
To display/hide the menu, select the bottom left corner of the screen.

## Slide 11: Color menu
The color value can be switched between RGB, CMY, and HLS in the pulldown menu

## Slide 12: Brush Menu
Set the drawing mode, brush type, width, and density.
Frequently-used Brush Types...
Dot: Paints only the selected color without any blur
Paint: Paints smoothly with a blurred edge
Air Brush: Paints with small particles, like mist

## Slide 13: Colorway
Only a single sample is needed to develop a full range of high-quality colorway simulations that maintain the original sense of texture and material.

## Slide 14: Layer Menu
Layers are like multiple sheets that create a complete image when combined.
Each layer can be edited individually.
Move / Copy / Size Change / Rotate / Color Change / Transparency etc.

## Slide 15: Stencil
Generally, a stencil refers to a sheet with a design cut out j of it.
In the Design software, the Stencil tool is used to mask an area that users do not want to display when making a layer.
In the example, a stencil is drawn on the background of the image to cut out the model from the background.
Image resolution describes the detail an image holds. The unit is dpi (dot per inch).
The higher the image resolution, the higher the quality, and the larger the file size.
The standard resolution in Design is 200 dpi.
Resolution

## Slide 16: Save and Transfer Data
Data is saved in Shima Seiki format, such as Colorway, Knit, Textile, Layer, etc.
Users can transfer the created data to a normal PC as a I general image format, like JPEG.
Local Disk (C): Only for programs *DO NOT USE
Local Disk (D)
Local Disk (E)
Removable Disk (G): USB plug-in device (e.g., digital camera)
Drive to Save Data

## Slide 17: Assistant Menu
This menu is the operation manual of the Design software.
Design functions, including descriptions with visual contents, are introduced to beginners.
To display/hide the Assistant Menu, select the
Select a category from the list on the left side of the Assistant Menu, and choose the work you desire.
Users can work while following the Assistant Menu displayed on the right side of the screen.

## Slide 18: Assistant Menu

## Slide 19: Work Menu
This menu provides the necessary functions of Design arranged according to the workflow.
Although there are no visual contents like the Assistant Menu, it is unnecessary to switch pages during one Design subject.
This menu allows users quick access to the desired function.
To display/hide the Work Menu, click the Work Menu
located in the bottom right corner of the screen.
Users can choose their work from the Work Menu List, and then follow the Work Menu displayed on the right side of the screen.

## Slide 20: O Convert to Stitch
Illustrations and photographs can be converted into stitches according to gauge. Taking into account the vertical to horizontal ratio of knitted loops, accurate evaluation can be made of the final product size.

## Slide 21
Data downloaded from staf can be used to create and edit stripe sequence, weave structure and colorway using APEX3.
Data can be converted to high-resolution textile simulation images and super realistic weave simulations to output for instruction sheets.
You can output textile planning paper based on design data.

## Slide 22: Troubleshooting HELP Menu
Design HELP describes each function in detail.
To open the HELP menu, click F1 directly on top of any function to see a detailed explanation.

## Slide 23: The Cursor is Frozen
The Cursor is Frozen * Force quit the Design software
Press the keys Ctrl +Alt + Delete together.
Select Task Manager from the menu.
Select SDS-ONE Design from the application list.
Click End Task twice and then select End now

## Slide 24: The Cursor is Frozen
The Cursor is Frozen Force quit Windows
If you cannot force quit the Design software as described above, push the Reset button on the hardware to restart Windows.
This process may take a minute.
After restarting and opening the Design software, the data will be restored.
Data may not be restored depending on the condition.

## Slide 25: Design video

## Slide 26: Design video

## Slide 27
References
https://www.shimaseiki.com
Shimaseiki training guide