## Slide 1
Lecture – 5 (Week 5)
FUNDAMENTAL OF THERMODYNAMICS AND HEAT TRANSFER
Dr. Lila Raj Koirala
Kathmandu Engineering College
Course Title:
Properties of Pure Working Substances

## Slide 2
Learning Objective of Lecture:
To impart a great deal of knowledge to undergraduate students on the following topics:
Pure Working Substances
Phase Change Terminologies and Definitions
P – T Diagram of a Pure Substance
Saturation Curve on P – v Diagram
Saturation Curve on T – v Diagram
Two Phase Systems
Ideal Gases and Ideal Gas Relations
State Postulate

## Slide 3: Working Substance:
A substance used in any thermodynamic system (device) with the help of which energy is transported between the system and its surroundings.
It serves as a medium for the transfer of energy to produce certain useful effect in all thermodynamic applications.

## Slide 4
Moreover, fluids can be easily transported from one place to another through pipes.
For examples, fuel air mixture in heat engine, refrigerants (e.g. ammonia) in heat pumps and refrigerators etc.
Working Substance:
It is the fluid that can be conveniently made to absorb, store and release energy.

## Slide 5
For most of the thermodynamic analysis, we assume the working substance as a pure substance.
Pure Substance:
A system is said to be composed of pure substance if it is [1]
III. invariable in chemical aggregation
II. homogeneous in chemical aggregation (combination),
I. homogeneous in composition (relative proportion)

## Slide 6
single elements and compounds are both examples of pure substances. A mixture of various chemical elements or compounds also qualifies as a pure substance as long as the mixture is homogeneous.
Pure Substance:
(i)
(ii)
(iii)

## Slide 7
State Postulate or Two Property Rule:
Experiments on a pure substance show that if the values of any two independent thermodynamic properties are known, all other thermodynamic properties can be determined for a state of a system composed of a pure substance.
This special feature of a pure substance for a state of a system is known as state postulate or two property rule.

## Slide 8
Two independent thermodynamic properties are sufficient to establish a stable thermodynamic state of a system composed of a pure substance [2].
It can be stated as
State Postulate or Two Property Rule:

## Slide 9: Ideal Gas:
A gas having no forces of molecular attraction.
At low pressures and high temperatures the molecules are far apart to each other due to which the forces of molecular attraction tend to be negligibly small [3].
Real gases tend to obey at low pressures or high temperature or at both.
No such gas existing in nature.

## Slide 10
The volume of a given mass of an ideal gas is inversely proportional to the pressure if the temperature remains constant. i.e.
PV = Constant
Ideal Gas Relations:
    Boyle's Law:

## Slide 11
It is also called Gay-Lussac's law, and can be stated in two parts:
The pressure of a given mass of an ideal gas varies directly with the absolute temperature if the volume is held constant. i.e.
    Charle’s Law:
The volume of a given mass of an ideal gas varies directly with the absolute temperature if the pressure is held constant. i.e.

## Slide 12
A relationship between all three common thermodynamic properties namely pressure, temperature and specific volume for a particular state of a system (ideal gas).
Equation of state:
It can be derived by combining Boyle's law and Charles' law. Consider unit mass of an ideal gas undergoing an isobaric process and an isothermal process in series.

## Slide 13
Applying Charle's law for the isobaric process 1 - A:
Using Boyle's law for the isothermal process
Equation of state:

## Slide 14
Equating these two relations we get:
where R is known as the particular or characteristic gas constant.
Equation of state:

## Slide 15
Two Phase (Liquid and Vapor) Systems:
A system is said to be in two phases when it exists as a mixture of two phases during phase change, e.g. a mixture of solid and vapor, solid and liquid, liquid and vapor.
Working substance in the form of mixture of liquid and vapor are used in many thermodynamic systems to transport energy.
For example, liquid and vapor phases of water and refrigerants as the working substances are used in power plants, refrigerators, heat pumps, air conditionings and many thermal distribution systems.

## Slide 16
Saturation Curve on T-v Diagram (P = Constant):
Constant pressure heating of water

## Slide 18
vcr = 0.003106 m3/kg
Tcr = 373.95C
T – v diagram for constant pressure heating of a pure substance (e.g. water) at various pressures:

## Slide 19
Saturation curve for two-phase mixture on T – v diagram:
Source: [3]

## Slide 20
Saturation Curve on P  v Diagram (T = Constant):
Constant temperature expansion of water

## Slide 21
P – v diagram for expansion of water at different temperatures:

## Slide 22
Saturation curve for two-phase mixture on P – v diagram:
Source: [3]

## Slide 23
P – T Diagram of a Pure Substance:
For water, the triple point temperature and pressure are 0.01°C and 0.6117 kPa.
Source: [4]

## Slide 24
Saturation Temperature:
For a given pressure, the temperature at which phase change (liquid to vapor or vapor to liquid) occurs.
For example, if we heat water at 1atm, evaporation takes place at 1000C, i.e., saturation temperature for 1 atm is 1000C.
Saturation Pressure:
For a given temperature, the pressure at which phase change (liquid to vapor or vapor to liquid) occurs.
For example, if we expand water at 1000C, evaporation takes place at 1 atm, i.e., saturation pressure for 1000C is 1 atm.
Phase Change Terminologies and Definitions:

## Slide 25
Saturated Liquid:
The state of a substance at which evaporation just starts (during heating) or condensation just completes (during cooling).
Saturated Vapor:
The state of a substance at which evaporation just completes (during heating) or condensation just starts (during cooling).
Compressed Liquid or Subcooled Liquid:
When saturated liquid is further cooled or compressed, it is called a compressed liquid or subcooled liquid.

## Slide 26
Superheated Vapor:
When saturated vapor is further heated or expanded, it is called a superheated vapor.
The state of a substance at which saturated liquid and saturated vapor have identical properties.
Critical Point:
The pressure and temperature corresponding to critical point are called critical pressure and critical temperature respectively. For H2O, critical pressure and temperature are 22.055 MPa and 373.950C respectively.

## Slide 27
Degree of Superheat:
The difference in temperature of a superheated vapor and the corresponding saturation temperature.
Hence, the degree of superheat of a super-heated vapor at state A is
.

## Slide 28
Hence, the degree of sub-cooling of a sub-cooled or compressed liquid at state B is
.
Degree of Sub-cooling:
The difference in the corresponding saturation temperature and the temperature of a sub-cooled or compressed liquid.

## Slide 29
The triple point of a pure substance exists at a definite pressure and temperature. For water, the pressure and the temperature at the triple point are 0.6117 kPa and 0.01C respectively.
The point at which all the three phases of the pure substance namely solid, liquid and vapor coexist in equilibrium.
A point at which the sublimation, fusion and vaporization lines meet to each other.
Triple Point:

## Slide 30
Sensible Heat:
It is the quantity of heat (or enthalpy) required to raise the temperature of 1 kg of water from 0C to its boiling point (saturation temperature) at a given pressure.
Hence, there is a change in the temperature in sensible heating process. Sensible heat increases as the pressure increases.

## Slide 31
Latent (Hidden) Heat:
There are two types of latent heat namely.
Latent heat of fusion is defined as the quantity of heat required to convert 1 kg of ice into water at constant temperature of 0C.
Latent heat of fusion
Latent heat of vaporization

## Slide 32
Latent het of vaporization is defined as the quantity of heat required to convert 1 kg of water at saturation temperature for a given pressure into its vapor at the same temperature and pressure.
Hence, there is no change in the temperature for a given pressure in latent heating process. Latent heat decreases as the pressure increases.
Latent (Hidden) Heat:

## Slide 33
[1] A Textbook of Engineering Thermodynamics: Rajput R. K., Laxmi Publications Pvt. Ltd. 113, Golden House, Daryaganj, New Delhi – 110002, India, 2010.
[2] Fundamentals of Engineering Thermodynamics: Howell J. R. and Buckius R. O., McGraw-Hill, New York, 1992.
References:

## Slide 34
[4] Thermodynamics: An Engineering Approach: Cengel Y. A. and Boles M. A., McGraw-Hill Education, New York, 2018.
[3] Fundamentals of Thermodynamics & Heat Transfer: Luintel M.C., Heritage Publishers & Distributors Pvt. Ltd., Kathmandu, Nepal, 2016.
References: