## Slide 1
Lecture – 8 (Week 8)
FUNDAMENTAL OF THERMODYNAMICS AND
HEAT TRANSFER
Dr. Lila Raj Koirala
Kathmandu Engineering College
Course Title:
First Law of Thermodynamics

## Slide 2
Learning Objective of Lecture:
To impart a great deal of knowledge to undergraduate students on the following topics:
Conservation Principle of Energy for a Control Volume
Conservation Principle of Mass for a Control Volume
First Law of Thermodynamics for a Control Volume
Expression for Mass Flow Rate

## Slide 3
Control Volume Analysis
Example Illustrating Use of First Law of Thermodynamics for a Control Volume
Steady State Analysis
Unsteady State Analysis
Learning Objective of Lecture:

## Slide 4
First Law of Thermodynamics for a Control Volume:
Conservation of Mass for a Control Volume:
Any control volume (open system) can interact with its surroundings by energy transfer as well as mass transfer.

## Slide 5
The change in mass within a control volume is equal to the mass entering into the control volume minus the mass leaving the control volume [1].
Conservation of mass for a control volume can be stated as
Conservation of Mass for a Control Volume:

## Slide 6
where,
On a rate basis,
Conservation of Mass for a Control Volume:

## Slide 7
Expression for Mass Flow Rate:
Total mass of the fluid crossing the section of length L is given by

## Slide 8
The mass flow rate is then given by
where is the volumetric flow rate of the fluid.
Conservation of mass can be expressed as
Expression for Mass Flow Rate:

## Slide 9
Conservation of Energy for a Control Volume:
Along with heat transfer and work transfer, mass transfer also affects the total energy of a control volume.
Mass entering into the control volume increases the total energy of the system where as mass leaving from the control volume decreases the total energy of the system.

## Slide 10
Following three conditions are possible in mass flow:
Ein < Eout  E of system decreases.
Ein > Eout  E of system increases.
Ein = Eout  E of system remains constant.

## Slide 11
All three conditions can be expressed as:
The change in total energy of the control volume can be caused due to net energy of mass flow and energy interactions through the boundary, i.e.
Conservation of Energy for a Control Volume:

## Slide 12
The change in total energy of a control volume is equal to the net energy transported by the fluid into the control volume plus the heat transferred to the control volume minus the work done by the control volume [1].
Conservation of energy for a control volume can be stated as:
Conservation of Energy for a Control Volume:

## Slide 13
where
On rate basis,
Heat transfer always occurs due to the difference in temperature between the system and the surroundings whether it’s a control mass or control volume, i.e.,
Conservation of Energy for a Control Volume:

## Slide 14
But the total work transfer associated with a control volume includes various modes of work transfer such as flow work, shaft work, expansion/ compression work, etc, i.e.,
Work transfer is composed of flow work due to flow of fluid at inlets/outlets and real boundary works,
Conservation of Energy for a Control Volume:

## Slide 15
Energy (work) required for the displacement of the fluid is given as
Conservation of Energy for a Control Volume:

## Slide 16
Therefore, the rate of flow work is evaluated as
Specific flow work or flow work per unit mass of the fluid is
Now, the total flow work for the control volume is the sum of the flow work at the inlets and the flow work at the outlets with consideration of sign convention, i.e.
Conservation of Energy for a Control Volume:

## Slide 17
Then, general expression for total work transfer is given by
where
Then general energy equation for control volume reduces to
Conservation of Energy for a Control Volume:

## Slide 18
Substituting,
h = u + Pv
Conservation of Energy for a Control Volume:

## Slide 19
Control Volume Analysis:

## Slide 20
Steady state system: the properties of the system at a particular point do not vary with time.
Uniform system: the properties of the system at a particular instant of time do not vary with space.
Unsteady state system: the properties of the system at a particular point vary with time.
Non-uniform system: the properties of the system at a particular instant of time vary with space.
Control Volume Analysis:

## Slide 21
Steady State Analysis:
Properties (total mass and total energy) of the control volume should not change with time.
Analysis of the long-term operation of a control volume where no mass or energy accumulates or dissipates within the control volume.
For example, uniform motion of a fan at a constant velocity.

## Slide 22
For devices having single inlet and single outlet,
Mathematically,
Steady State Analysis:

## Slide 23
Steady State Analysis:

## Slide 24
For devices having single inlet and single outlet, energy equation reduces to

Steady State Analysis:

## Slide 25
Unsteady State Analysis:
Properties (total mass and total energy) change with time, i.e., total mass and total energy of the system is function of time.
Analysis of the control volume when there is an accumulation (storage) or dissipation of the mass or energy within the control volume and their time variations at the inlets and outlets.
For examples, filling and discharging of a gas cylinder, start-up and shut-down period of a device such as of a fan.

## Slide 26
Integrating mass conservation equation
Unsteady State Analysis:

## Slide 27
Integrating energy conservation equation
Unsteady State Analysis:

## Slide 28
Example: Application of First Law of Thermodynamics for a Control Volume:
Steam is leaving a 4-L pressure cooker whose operating pressure is 150 kPa. It is observed that the amount of liquid in the cooker has decreased by 0.6 L in 40 min after the steady operating conditions are established, and the cross-sectional area of the exit opening is 8 mm2. Determine
Source: [2]
Energy Transport by Mass:

## Slide 29
(i) the mass flow rate of the steam and the exit velocity,
(iii) the rate at which energy leaves the cooker by steam [2].
(ii) the total and flow energies of the steam per unit mass,
Energy Transport by Mass:

## Slide 30
Solution:
Assumptions:
1. The flow is steady, and the initial start-up period is disregarded.
2. The kinetic and potential energies are negligible and thus they are not considered.
Given:
Operating pressure, P = 150 kPa
Change of volume of liquid, ∆Vl = 0.6 L
Time, ∆t = 40 min
Area of exit, A = 8 mm2

## Slide 31
Properties:
From the steam table the properties of the saturated liquid and saturated vapor at pressure 150 kPa are:
vl = 0.001053 m3/kg
vg = 1.1595 m3/kg
ug = 2519.4 kJ/kg
hg = 2693.4 kJ/kg
3. Saturation conditions exist within the cooker at all times so that steam leaves the cooker as a saturated vapor at the cooker pressure.
Assumptions:

## Slide 32
Saturation conditions exist in a pressure cooker at all times after the steady operating conditions are established.
Analysis:
Hence, the liquid has the properties of saturated liquid and the exiting steam has the properties of saturated vapor at the operating pressure.
The evaporated mass of liquid,
= 0.5698 kg

## Slide 33
= 34.41 m/s
= 2693.4 – 2519.4 = 174 kJ/kg
As h = u + Pv
(ii) The flow energy per unit mass,
and the exit velocity,
Kg/s
(i) The mass flow rate of the exiting steam,

## Slide 34
(iii) Now, the rate at which energy is leaving the cooker by steam is given by
= 0.64 kW
e = hg + ke + pe = hg = 2693.4 kJ/kg
and the total energy per unit mass,
As the kinetic and potential energies are neglected.

## Slide 35
The numerical value of the energy leaving the cooker with steam alone does not mean much since this value depends on the reference point selected for enthalpy (it could even be negative).
Discussion:
The significant quantity is the difference between the enthalpies of the exiting vapor and the liquid inside (i.e. hlg = hg – hl) since it relates directly to the amount of energy supplied to the cooker.

## Slide 36
[2] Introduction to Thermodynamics and Heat Transfer: Cengel Y. A., McGraw-Hill Companies, ISBN: 0 – 390 - 86122-7, 2008.
[1] Fundamentals of Thermodynamics & Heat Transfer: Luintel M.C., Heritage Publishers & Distributors Pvt. Ltd., Kathmandu, Nepal, 2016.
References:

## Slide 37
Thank You