## Slide 1
Lecture – 12 (Week 12)
FUNDAMENTAL OF THERMODYNAMICS AND
HEAT TRANSFER
Dr. Lila Raj Koirala
Kathmandu Engineering College
Course Title:
Second Law of Thermodynamics

## Slide 2
Learning Objective of Lecture:
To impart a great deal of knowledge to undergraduate students on the following topics:
Carnot cycle and Heat engine
Heat pump and Refrigerator
Kelvin – Planck and Clausius statements and their equivalence
Clausius inequality
Example illustrating the use of a heat pump for heating a house

## Slide 3
Carnot Cycle:
It is an ideal cycle devised by Carnot which will have efficiency equal to that of a reversible cycle (theoretical maximum).
However, it is used as a reference standard for the comparison of different practical cycles.
This cycle is not practically possible.

## Slide 4
All the four processes have to be reversible. This needs that there should not involve any kind of frictions within the system (between working fluid particles) as well as between the piston and cylinder walls.
The reversible heat addition and rejection have to take place with infinitesimal temperature differences. However, the smaller the temperature difference between two systems, the smaller the heat transfer rate will be.
Carnot cycle is practically impossible, because…….

## Slide 5
For achieving isothermal heat transfer, the piston movement is required to be very slow. However, the piston must move fast for the adiabatic process so that there is less time available for the heat transfer. A variation in the speed of the piston during different processes of a cycle is rather impossible [1].
Hence, any significant heat transfer through a small temperature difference requires a very large surface area of the cylinder and a very long time which is impractical and not economically feasible.
because…….

## Slide 6
Carnot cycle consists of the following processes in series as shown in Cycle Diagram below.
Thermal efficiency of a Carton cycle or Carnot engine is given by

## Slide 7
Source: [2]

## Slide 8
Reversible Isothermal Heat Addition (Process 1 – 2)
During process 1 – 2, heat is added to the working substance inside the cylinder from a high temperature source having a temperature of TH and the working substance undergoes an isothermal expansion.
During the isothermal expansion, pressure of the substance decreases, its volume increases, its temperature remains constant and the entropy increases.

## Slide 9
Reversible Adiabatic (Isentropic) Expansion (Process 2 – 3)
During process 2 – 3, working substance undergoes an isentropic expansion during which its pressure further decreases and its volume further increases.
Hence, during the isentropic expansion process, entropy of the system remains constant and its temperature decreases.
During isentropic expansion process no heat is supplied to the system and hence, it produces work due to expense of its internal energy.

## Slide 10
During process 3 – 4, heat is transferred from the working substance inside the cylinder to a low temperature sink having a temperature of TL and the working substance undergoes an isothermal compression.
Reversible Isothermal Heat Rejection (Process 3 – 4)
During the isothermal compression, pressure of the substance increases, its volume decreases, its temperature remains constant and the entropy decreases.

## Slide 11
Reversible Adiabatic (Isentropic) Compression (Process 4 – 1)
During process 4 – 1, working substance is further compressed under isentropic condition such that its initial state is restored during which its pressure further increases and its volume further decreases.
Hence, during this process entropy of the system remains constant and its temperature increases.
During isentropic compression process work supplied to the system increases its internal energy because there is no heat loss from the system.

## Slide 13
Heat Engine:
Device which operates on a cyclic process and converts heat energy into mechanical work is called a heat engine.
Source: [3]

## Slide 14
Performance of a heat engine is measured by its efficiency, which is defined as the ratio of net work output and the heat supplied, i.e.
Figure shows a schematic representation of a heat engine which takes QH amount of heat from a high temperature reservoir at TH (source) converts some part of it into work (W) and rejects remaining part QL to a low temperature reservoir at TL (sink).

## Slide 15
Applying first law of thermodynamics for a cyclic process,
The thermal efficiency of heat engine can be expressed as
Applying second law for cyclic process,

## Slide 16
For a reversible heat engine,
Now, thermal efficiency of a reversible heat engine which is also called the Carnot efficiency can be expressed as

## Slide 17
Heat Pump:
Device which is operating on a cyclic process, and takes heat from a low temperature reservoir at TL (surroundings) and delivers it to a high temperature TH (desired space) with the help of external work.
Source: [3]

## Slide 18
Performance of a heat pump is measured by its coefficient of performance, which is defined as the ratio of desired effect and the work supplied,
In case of heat pump, desired effect is the amount of heat supplied to the desired space (QH), hence
Heat pump maintains the temperature of a desired space higher than that of the surroundings.

## Slide 19
Using first law of thermodynamics for the heat pump,
Now, the COP of a heat pump can be expressed as
Applying second law for cyclic process,

## Slide 20
For a reversible heat pump,
COP for a reversible heat pump can be expressed as:

## Slide 21
Refrigerator:
Device which is operating on a cyclic process, and takes heat from a low temperature reservoir at TL (desired space) and delivers it to a high temperature TH (surroundings) with the help of external work.
Source: [3]

## Slide 22
Performance of a refrigerator is also measured by its coefficient of performance, and in case of refrigerator, desired effect is the amount of heat taken out from the desired space (QL), i.e.
It maintains the temperature of a desired space lower than that of the surroundings.

## Slide 23
Using first law of thermodynamics for the refrigerator,
The COP of a refrigerator can be expressed as
Applying second law for cyclic process,

## Slide 24
For a reversible refrigerator,
COP for a reversible refrigerator can be expressed as

## Slide 25
Clausius Inequality:
From the second of thermodynamics the change in entropy for a control mass with a single heat transfer reservoir as its surroundings is given by
As
This equation is known as Clausius inequality.
Taking cyclic integral for a complete cycle,

## Slide 26
the cycle is irreversible
the cycle is reversible
the cycle is impossible
For any cycle if

## Slide 27
Kelvin – Planck and Clausius Statements of Second Law of Thermodynamics :
The possible direction of a process can also be defined by some popular statements without using the system property entropy.
I. Kelvin - Planck Statement:
It is impossible to construct a device that operates on a cycle to convert all the heat supplied to it into an equivalent amount of work [2].

## Slide 28
Impossible device (heat engine) as defined by Kelvin Planck
Source: [3]

## Slide 29
This statement can also be expressed as:
“no heat engine can have a thermal efficiency of 100 percent”.
II. Clausius Statement:
It is impossible to construct a device that operates in a cycle and produces no effect other than the transfer of heat from a lower-temperature system to a higher-temperature system [2].

## Slide 30
Impossible device (heat pump or refrigerator) as defined by Clausius
Source: [3]

## Slide 31
Equivalence of Kelvin-Planck and Clausius Statements:
These two statements are equivalent in their consequences, and either statement can be used as the expression of the second law of thermodynamics.
Any device that violates the Kelvin–Planck statement also violates the Clausius statement, and vice versa.

## Slide 32
Violation of Kelvin-Planck Statement Resulting in Violation of Clausius Statement:
Source: [3]

## Slide 33
Violation of Clausius Statement Resulting in Violation of Kelvin-Planck Statement:
Source: [3]

## Slide 34
A heat pump is used to meet the heating requirements of a house and maintain it at 20ºC. On a day when the outdoor air temperature drops to −2ºC, the house is estimated to lose heat at a rate of 80,000 kJ/h. If the heat pump under these conditions has a COP of 2.5, determine
EXAMPLE: Heating a House by a Heat Pump
(ii) the rate at which heat is absorbed from the cold outdoor air [3].
(i) the power consumed by the heat pump

## Slide 35
Source: [3]

## Slide 36
Steady state operating conditions exist.
Assumptions:
(i) The power consumed by this heat pump is determined from the definition of the coefficient of performance to be
Solution: Given,
Analysis:
kJ/h
= 8.9 kW
TL = −2ºC = 271 K
TH = 20ºC = 293 K
kJ/h
COPHP = 2.5

## Slide 37
(ii) The house is losing heat at a rate of 80,000 kJ/h. If the house is to be maintained at a constant temperature of 20ºC, the heat pump must deliver heat to the house at the same rate, that is, at a rate of 80,000 kJ/h. Then the rate of heat transfer from the outdoor becomes
= 80000 − 32000 = 48000 kJ/h
= 13.3 kW

## Slide 38
Note that 48,000 of the 80,000 kJ/h heat delivered to the house is actually extracted from the cold outdoor air.
Discussion:
Therefore, we are paying only for the 32,000 kJ/h energy that is supplied as electrical work to the heat pump.
If we were to use an electric resistance heater instead, we would have to supply the entire 80,000 kJ/h to the resistance heater as electric energy.

## Slide 39
This would mean a heating bill that is 2.5 times higher.
This explains the popularity of heat pumps as heating systems and why they are preferred to simple electric resistance heaters despite their considerably higher initial cost.

## Slide 40
[2] Fundamentals of Thermodynamics & Heat Transfer: Luintel M.C., Heritage Publishers & Distributors Pvt. Ltd., Kathmandu, Nepal, 2016.
References:
[1] Thermal Science and Engineering: Dr. Kumar D.S., S. K. Kataria & Sons, India, 2009.
[3] Thermodynamics: An Engineering Approach: Cengel Y. A. and Boles M. A., McGraw-Hill Education, New York, 2018.

## Slide 41
Thank you