## Slide 1
Lecture – 14 (Week 14)
FUNDAMENTAL OF THERMODYNAMICS AND
HEAT TRANSFER
Dr. Lila Raj Koirala
Kathmandu Engineering College
Course Title:
Thermodynamic Cycles

## Slide 2
Learning Objective of Lecture:
To impart a great deal of knowledge to undergraduate students on the following topics:
Air Standard Analysis
Air Standard Otto Cycle
Vapor Compression Refrigeration Cycle
Air Standard Diesel Cycle

## Slide 3
Air Standard Analysis:
During the normal operation of the petrol and diesel engines, the mass of the fuel per unit mass of air i.e. fuel-air ratio, is very small (0.08 to 0.025) and therefore the properties of the fuel air mixture before combustion approximates closely to those of air [1].
The properties of the products of combustion also do not differ much from those of pure air.

## Slide 4
Therefore, simplified analysis of such cycles can be carried out by considering only air as its working substance.
The idealized analysis of the cycle considering only air as the working substance is called an air standard analysis. Efficiency resulting from such analysis is called an air standard efficiency.
Air Standard Analysis:

## Slide 5
Assumptions of Air Standard Analysis:
The cycle consists of fixed mass of air.
The expansion and compression processes are isentropic.
The combustion process is replaced by an equivalent heat addition process from an external source.
The exhaust process is replaced by an equivalent heat rejection process to an external sink.
The properties of air (cp, cv. R, etc.) remains constant.

## Slide 6
Air Standard Otto Cycle:
An idealized model for the operation of petrol engines.
Consists of two isentropic and two isochoric processes.
Although the air standard analysis differs from the actual operation, it gives basic idea about the variation of efficiency of the cycle with different parameters.

## Slide 7
At the beginning of compression, piston will be at the BDC and the cylinder contains the mixture of air and petrol.
Process 1 - 2 (Isentropic Compression)
During the isentropic compression:
 pressure and temperature of the system increase,
 volume decreases and entropy remains constant.
When the piston travels from BDC to TDC, the mixture inside the cylinder is compressed under isentropic condition.

## Slide 9
Process 2 - 3 (Isochoric Heat Addition)
At the end of the compression stroke, spark plug provides an electric spark and petrol gets burn instantaneously.
During the heat addition process:
pressure, temperature and entropy of the system increases.
Therefore, heat addition for an ideal Otto cycle is considered as an isochoric process.

## Slide 11
Process 3 - 4 (Isentropic Expansion)
Due to the impact of burning, piston gets expanded from TDC to BDC and the process is assumed to be an isentropic expansion.
During the expansion process:
 volume increases and entropy remains constant.
 pressure and temperature of the system decreases,

## Slide 13
Process 4 - 1 (Isochoric Heat Rejection)
Heat is rejected by the system to the surroundings through the exhaust gas and this process is replaced by an equivalent constant volume heat rejection process to complete the cycle.
During isochoric heat rejection process:
temperature, pressure and entropy of the system decrease.

## Slide 15
Efficiency of an Air Standard Otto Cycle:
Efficiency of internal combustion cycle can be determined as
Heat rejected and heat added during the cycle are given as
and

## Slide 16
Substituting qL and qH
This equation requires temperatures of each state to determine the efficiency of the cycle.
We can further simplify it to reduce the number of required variables.

## Slide 17
Applying temperature – volume relationship for isentropic compression process 1 - 2 and isentropic expansion 3 - 4 process,
Equating these two equations,
or,
and

## Slide 18
Now, using componendo and dividendo,
Efficiency is then given as
We can express efficiency in terms of volume ratio as
where r = V1/V2, is called compression ratio.

## Slide 19
Although high compression ratio is desirable for high efficiency but in reality high pressure ratio causes high temperature and there is a limitation to which a real engine cylinder can withstand maximum temperature or pressure [1].
In real petrol engine cycle compression ratio is usually between 8 to 12 [1].

## Slide 20
Source: [2]

## Slide 21
Source: [3]

## Slide 22
Expression for Compression Ratio:
The stroke volume is given by
Substituting expression for stroke volume, we get an expression for compression ratio in terms of engine dimensions as

## Slide 24
Air Standard Diesel Cycle:
An idealized model for the operation of diesel engines.
Consists of isentropic compression, isobaric heat addition, isentropic expansion and isochoric heat rejection.
Process 1-2 (Isentropic Compression)
At the beginning of compression, piston will be at the BDC and the cylinder contains air.

## Slide 25
When the piston travels from BDC to TDC, the air inside the cylinder is compressed under isentropic condition.
During the isentropic compression:
entropy remains constant.
volume decreases and
 pressure and temperature of the system increase,

## Slide 27
Process 2 - 3 (Isobaric Heat Addition)
At the end of compression stroke, the temperature of the air reaches greater than the self ignition temperature of diesel.
At this state, fuel injector nozzle supplies diesel into the cylinder and the diesel get self burnt.

## Slide 28
During the constant pressure heat addition process:
volume, temperature and entropy of the system increase.
Therefore, heat addition is modeled as an isobaric process.
The combustion of the diesel cannot complete instantaneously and the piston move from TDC to towards the BDC simultaneously with heat addition.

## Slide 30
Process 3 - 4 (Isentropic Expansion)
Due to the impact of burning, piston gets further expansion in isentropic condition.
During the isentropic expansion process:
 entropy remains constant.
 volume increases and
 pressure and temperature of the system decrease,

## Slide 32
Process 4 - 1 (Isochoric Heat Rejection)
Heat is rejected by the system to the surroundings through the exhaust gas.
During isochoric heat rejection process:
temperature, pressure and entropy of the system decrease.
This process is replaced by an equivalent constant volume heat rejection process to complete the cycle.

## Slide 34
Efficiency of an Air Standard Diesel Cycle:
Efficiency of an ideal diesel cycle is given as
Heat rejected by the system during constant volume process 4 - 1 is given by

## Slide 35
Heat added to the system during constant pressure process 2 - 3 is given by
Substituting qL and qH

## Slide 36
Applying temperature – volume relationship for isentropic compression process 1 - 2
where r = V1/V2, is called compression ratio.
Applying temperature – volume relationship for isobaric heat addition process 2 - 3
where  = V3/V2, is called cut off ratio.

## Slide 37
Applying temperature – volume relationship for isentropic expansion process 3 - 4
Substituting V4 = V1,

## Slide 38
Multiplying temperature ratios,
Expression for the efficiency of diesel cycle can be given as

## Slide 39
Source: [3]

## Slide 40
Vapor Compression Refrigeration Cycle:
The most widely used cycle for heating and cooling of the desired space.
Working substance used to run the cycle is called refrigerant.
Consists of isentropic compression, isobaric heat rejection, isenthalpic expansion (throttling) and isobaric heat addition.

## Slide 41
Source: [1]

## Slide 42
Exit saturated vapor from the evaporator is supplied to the compressor, where it is compressed with the help of work input usually provided by the electricity.
Isentropic Compression Process 1 – 2
During compression process:
 pressure, temperature and enthalpy of the refrigerant increases,
The compression process is assumed to be an isentropic process,
 entropy remains constant.

## Slide 44
The high pressure and temperature superheated refrigerant from the compressor outlet is delivered to the condenser.
Isobaric Heat Rejection Process 2 - 3
Condensation process occurs at constant pressure, during which entropy and enthalpy of the refrigerant decrease.
While rejecting heat, superheated vapor at the condenser inlet gets condensed into saturated liquid.
Condenser can interact with its surroundings and the high temperature refrigerant rejects heat to the surroundings.

## Slide 46
The high pressure saturated liquid at the exit of the condenser is delivered to the expansion (throttling) valve.
Isenthalpic Expansion (Throttling) Process 3 - 4
During the throttling process (isenthalpic process):
entropy increases.
pressure and temperature decreases and
enthalpy of the refrigerant remains constant,

## Slide 48
The low pressure and low temperature refrigerant (two phase mixture) from the throttling valve enters into the evaporator.
Isobaric Heat Addition Process 4 - 1
Evaporation takes place at constant pressure during which entropy and enthalpy of the refrigerant increase.
During the absorption of heat refrigerant gets evaporated.
The low temperature refrigerant inside the evaporator can take heat from its surroundings.

## Slide 50
If the cycle is used for the heating of a desired space then its COP is given as
If the cycle is used for the cooling of a desired space then its COP is given as
Coefficient of Performance (COP) of the Cycle:

## Slide 51
[1] Fundamentals of Thermodynamics & Heat Transfer: Luintel M.C., Heritage Publishers & Distributors Pvt. Ltd., Kathmandu, Nepal, 2016.
References:
[2] Thermal Science and Engineering: Dr. Kumar D.S., S. K. Kataria & Sons, India, 2009.
[3] Thermodynamics: An Engineering Approach: Cengel Y. A. and Boles M. A., McGraw-Hill Education, New York, 2018.

## Slide 52
Thank You