## Slide 1: Course: Building Services III
Lecture 9: Energy, energy planning and energy auditing
Lecturer: Manchan Tiwari

## Slide 2: Introduction
Energy is the capacity to do work. Energy is vital for each activity in our day-to-day life. Energy is required to fulfill every basic need of human beings.
At larger scale, energy consumption of a country or civilizations depicts the extent of development or prosperity of the nation. All the technological advances in the world are possible due to the improvement in quality of various types of energy.
Earliest form of energy used were work done by human and animals along with wind and water available in nature. The development of human civilization has been directly related with the amount and form of energy consumed.
The energy sources consumed before the Industrial revolution had low energy density and were not dependable (Singal, 2011). However, the sources were renewable and available for free.
With the growth in population and various inventions, the use of energy shifted to conventional fossil fuels. The high energy density of the fuels resulted in efficient conversion to useful work.
Due to environmental impact of the conventional fuels, the focus has been shifted to traditional or renewable energy sources. The majority of renewable energy sources are focused towards electricity generation.

## Slide 3: Energy Characteristics
Use of energy can be evident in very simple form as of daily work done by human beings or in rather complex form as power produced from a Solar Photo-voltaic panel. However, the basic concepts and characteristics for all the kind of energy sources and forms are fundamentally similar. Some of the characteristics are:
Energy can neither be created nor be destroyed
Energy can exist and can be transformed from one form to another
Energy can be stored in proper devices and equipment
The general unit of energy is N-m or Joule.
The value of energy is measured with reference to a datum. The commonly used datum or reference are ground level, atmospheric pressure and temperature at 0 K. Which means that the heat energy at 0 K is considered zero. The potential energy at ground level is considered zero.
The natural flow of energy takes place from higher energy to lower energy (Singal, 2011)

## Slide 4: Forms of Energy
Energy are available in various forms. Some of them are
Mechanical Energy
Electrical Energy
Chemical Energy
Nuclear Energy
Heat Energy

## Slide 5: Mechanical Energy
    Kinetic Energy
Kinetic Energy is the result of energy possessed by a body due to the virtue of its mass and motion or velocity. The kinetic energy of a body can also be understood by the amount of work required to move the body at the given velocity from the position of rest.
Kinetic Energy (KE) can be expressed by the following relation
    Potential Energy
It is defined as the energy possessed by a body due to its position with respect to a relative datum or ground. It represents the energy a body has when it is raised to certain height above the ground and due to which it falls and gains kinetic energy.

## Slide 6: Flow Energy
When a water body is flowing in a pressurized conduit, it is important to consider the pressure energy the fluid possess along with the kinetic energy. The energy is known as flow energy or pressure energy

## Slide 7: Shaft Energy
Generally, the potential energy or kinetic energy of a fluid is converted to rotation energy of a shaft which in turn rotates a generator or drive system to which it is coupled to produce the necessary power.

## Slide 8: Electrical Energy
Wind or hydro power plants along with other major power plants transform the mechanical energy produced by turbines into electrical energy.
Electrical energy is clean form of energy which can be easily transported by the means of transmission lines.
Also, fuel cells convert the chemical energy of a fuel to electrical energy. In most of the case, the end targeted end product of all energy sources in Electrical Energy.

## Slide 9: Chemical Energy
Chemical energy is the energy possessed by a either solids, liquids or gases (hydrocarbons) which gets released upon the chemical reaction. Generally, the fuel such as coal, wood, gasoline combine with oxygen to release byproducts and heat in an exothermic reaction.
The heat that one kg of such substances is able to produce during combustion is called calorific value. The unit of calorific value is kJ/kg.
Fuel cell is also a device which directly converts the fuel to electrical energy by the virtue of chemical energy present in the fuel.

## Slide 10: Energy Classification
Commercial and Non-commercial energy resources
Renewable and Non-renewable energy resources
Conventional and Non-conventional energy resources

## Slide 11: Energy Classification
  Commercial and Non-commercial energy resources
Commercial energy resources are also known as primary energy resources. These are generally available in raw form in nature eg. coal, natural gas, wind and water etc. Non-commercial energy resources are those which are available freely in nature such as solar energy, agricultural waste.
  Renewable and Non-renewable energy resources
Renewable energy sources are those which do not deplete upon continuous use and can be reused continuously such as solar energy, wind energy, geothermal energy, tidal energy etc.
Non renewable energy sources are those which deplete upon use and can get exhausted upon use for a limited period of time such as coal, oil, gas etc. Dependency on non-renewable energy sources can contribute to fuel crisis in future as the supply cannot be adjusted according to the demand (Sharma & Hasan, 2009).

## Slide 12: Energy Classification
  Conventional and Non-conventional energy resources
Conventional energy sources are those which are being used orthodoxly in the world today. Coal, oil and gas are commonly known as conventional energy resources. Conventional energy sources get depleted and are non-renewable. Solar energy, wind energy, agricultural waste etc. are classified as the non-conventional energy resources.

## Slide 13: Renewable energy sources
Renewable energy sources are often non-conventional energy sources. The various types of renewable energy sources are
  Solar Energy
  Wind Energy
  Geothermal Energy
  Biomass
  Ocean Energy and Tidal Energy
  Micro-hydro Projects

## Slide 14: Solar energy
Solar energy is continuously incident on the earth in form of electromagnetic radiation at the rate if around 1,7 x 1017 W (Singal, 2011).
If a person would require 10 kW of energy for sustaining life, then a population of 10 billion will require around 1011 which is much less than the solar energy incident on the earth.
So, theoretically solar energy is sufficient to fulfill all the energy requirement of the people of earth.

## Slide 15: Solar energy
However, there are limitations which restrict the actual usage of solar energy such as solar energy is very diffuse, cyclic and often undependable.
However, much of the limitations have been addressed by modern energy conversion devices which either convert solar energy to heat or directly generate electricity in reliable manner.

## Slide 16: Solar energy applications
Conversion to electricity (Solar PV)
Conversion to thermal energy (Solar Thermal)

## Slide 17: Solar energy applications
The main applications of solar energy are:
Heating of buildings
Cooling of buildings
AC and refrigeration
Solar cookers
Solar water heaters
Solar air heaters
Solar water pumping devices
Building integrated solar photovoltaic
Community based solar photovoltaic system
Standalone solar PV power systems
Solar water heating
Solar drying of agricultural and animal products
Solar distillation on a small community scale
Salt production by evaporation of seawater or inland brines
Solar engines from water pumping
Bio conversion and wind energy which are indirect sources of solar energy
Solar furnace
Solar electric power generation
Solar pond
Steam generation heated by rotating reflectors
Solar PV cells

## Slide 18: Wind energy
Sunlight has to travel varying distance to reach the surface of the earth depending on its latitude.
That is, sunlight reaches perpendicularly at tropical region and becomes more oblique in high latitude region.
This results in uneven heating of the earth’s surface which results in tropical region being hotter than the polar regions.

## Slide 19: Wind energy
This results in variation of atmospheric pressure at different regions which results in movement of air from high pressure to low pressure regions.
This phenomenon is the principal cause of Earth’s wind system (Boyle, 2013).
This wind energy is dependent mainly on the velocity at which the wind travels and can be harnessed by using different form of wind turbines.

## Slide 20: Wind energy
The kinetic energy of the wind is governed by simple equation represented as follows:
Where,
  KE = Kinetic energy posses by wind(Joule)
  m = mass of air (kg)
  V = velocity of the wind (m/s)

## Slide 21: Wind energy
Generally rotor diameter of 50m and heights of 100m are typical dimensions for a wind turbine which can produce appreciable amount of power (Singal, 2011).
The large variability of wind has resulted in unreliable power production in wind energy.
Figure: Wind Turbine (Source: IEA 2022)

## Slide 22: Geothermal energy
Earth is composed of inner core, outer core, lower mantle, upper mantle and crust.
The depth of crust is about 40 kms.
The temperature is highest at earth’s core.
At the base of the crust the temperature ranges from 200 to 100 degree Celsius.
Due to various faults and fractures in earth’s surface (due to earthquakes or surface movement), rain water can seep down such faults for miles.
After being heated it can return to the surface as steam or hot water. Geothermal springs can reach temperature of 370 degree Celsius (Singal, 2011).
The heat stored beneath the earth’s crust can be used for various purpose such as space heating, electricity generation, cooking and medicinal purposes.

## Slide 23: Biomass
Biomass are basically the organic matter derived from various plant and animal sources. Energy derived from such biomass is known as biomass energy.
Biomass is also indirect manifestation of solar energy as the solar energy received by the plants converts carbon dioxide present in the atmosphere to carbohydrates which forms the basis of much complex molecules.
In developing countries, biomass (or in form of biofuels) are the major source of energy.

## Slide 24: Biomass
Gaseous and liquid fuels derived from biomass are significant source of power in some countries (Boyle, 2013).
However, biomass or biofuels are considered renewable source of energy only when the rate at which they are consumed is less than the rate at which new plants are regrown which is unfortunately, is often not the case (Boyle, 2013).
Inefficient combustion of biomass can result in significant amount of green house gases to be released in to atmosphere.

## Slide 25: Micro hydro power
Micro hydropower is considered renewable energy source even though large hydropower plants are generally not categorized as renewable energy due to its considerable environmental impact.
In context of Nepal, micro hydropower is defined as hydro plants of capacity less than 100 kW.
Hydropower plant is an energy system which derives its power from the flowing river system.
The water is either stored in a reservoir or blocked by weir/dam from where the water is diverted through canal and/or penstock pipe to rotate a turbine in powerhouse.
The rotating turbine drives generators that produce electricity. The amount of water which flows in the river and the height from which it falls (head) is directly proportional to the power capacity of hydropower.
Basically in a hydropower the potential energy of the water is converted to kinetic energy in the nozzle which is then converted to mechanical energy in turbine. The mechanical energy of the turbine is converted to electrical energy by generator.

## Slide 26: Advantages of renewable energy sources
Renewable in nature and inexhaustible
No operating cost for fuel
Are site specific, lesser need for transmission and distribution.
Renewable energy sources have negligible or no contribution to the pollution and hence are considered as clean energy sources
Most devices or technology used for conversion of renewable energy sources are simple in nature and can be fabricated easily locally.
Renewable technology can serve rural areas better with locally available source of renewable energy.

## Slide 27: Solar radiation
Solar radiation is the primary natural energy source of the Earth (other natural sources are: geothermal heat, natural terrestrial radioactivity, cosmic radiation, tidal energy due to gravitational pull).
Solar radiation mainly reaches the earth as electromagnetic radiation from the surface of the sun.
The radiation is originated due to high temperature of sun which is a result of several nuclear fusion processes occurring in the interior of the sun.
Sun is the most prominent feature in our solar system
The sun is an enormous nuclear fusion reactor, which causes four hydrogen nuclei to fuse together and form helium nucleus.

## Slide 28: Solar radiation
The difference in the mass of helium is 0.7% less than that of four hydrogen nuclei.
This difference in mass is expelled in form of energy and radiated from the surface of the Sun (S. Hasan & Sharma, 2009).
It radiates energy by virtue of its high surface temperature around 6000 ⁰C.
Only small part of energy radiated from sun reaches to the earth.
Almost one third of the radiation incident on Earth is simply reflected back.
Even though we perceive solar radiation as white light, in fact it spreads over a wide spectrum of wavelengths, from short-wave infrared to ultraviolet.

## Slide 29: Solar radiation
Sun Statistics
Mass (kg) : 1.98 x 1030
Equatorial radius : 695000
Mean Density : 1.41 gm/cm3
Mean Surface Temperature : 6000 C
Hydrogen : 92.1%
Helium : 7.8%

## Slide 30: Solar radiation
Solar radiation is the electromagnetic radiation emitted by the sun which can be converted to useful forms of energy such as heat and electricity by using various technologies
The electromagnetic radiation emitted by the sun shows a wide range of wavelengths.
It can be divided into following major regions
  Ionizing radiation (x-rays and gamma rays)
  Non ionizing radiation (UVR, Visible and infrared radiations)
The highly injurious ionizing radiation does not penetrate the earth’s atmosphere
The wavelength distribution of solar radiation consists of short wave as well as long wave radiations.
The different region of solar spectrum has varying wavelengths
The region of the spectrum that is visible to human has wavelengths around 400 to 700 nm.
Visible range of the electromagnetic radiation is practically useful for us.
Short wavelength radiation has higher energy level that the long wavelength radiation.

## Slide 31: Solar radiation
The sunlight while it passes through the earth’s atmosphere, some of its part is absorbed and reflected by air molecule, water vapors, clouds, dust and pollutants.
The radiation which have been reflected is known as Diffused radiation. The diffused radiation does not have a particular path.
The solar radiation other than diffused radiation which reaches the earth’s surface without being scattered is known as Direct radiation. The sum of the direct and diffused radiation is called global radiation.

## Slide 32: Energy Management
Energy management refers to the strategic and systematic oversight of the way energy is used and controlled within an organization, facility, or system. It involves the efficient utilization, conservation, and optimization of energy resources to minimize energy consumption, reduce costs, and mitigate environmental impact.
Key aspects of energy management include:
Monitoring and Analysis: Regular monitoring, measurement, and analysis of energy consumption patterns and energy efficiency to identify areas for improvement.
Efficiency Improvements: Implementing measures and technologies to improve energy efficiency, such as upgrading equipment, improving insulation, using energy-efficient lighting, or optimizing processes to reduce energy waste.
Renewable Energy Integration: Introducing renewable energy sources like solar, wind, or hydro power to reduce reliance on non-renewable resources and lower the carbon footprint.

## Slide 33: Energy Management
Behavioral Changes: Educating and engaging employees or users to adopt energy-saving practices and promoting a culture of energy consciousness.
Regulatory Compliance: Adhering to energy-related regulations and standards to ensure legal compliance and potentially benefit from incentives or rebates.
Cost Reduction: Managing energy consumption to reduce operational costs, which can significantly impact the bottom line of businesses or households.
Environmental Impact: Mitigating the environmental impact of energy use by reducing carbon emissions and other pollutants associated with energy production and consumption.
Effective energy management practices are essential for sustainability, cost savings, and reducing the carbon footprint. It involves a combination of technological upgrades, behavioral changes, and continuous improvement initiatives to achieve the goal of using energy in the most efficient and sustainable manner possible.

## Slide 34: Energy Auditing
Energy auditing in the context of buildings involves a systematic process of assessing and evaluating the energy usage and efficiency of a structure to identify opportunities for energy conservation and cost savings. It aims to analyze the energy consumption patterns within a building, recommending improvements to enhance energy efficiency and reduce overall energy costs.
Key points about energy auditing in buildings include:
Assessment of Energy Use: Energy auditors evaluate the overall energy consumption patterns of a building by examining factors like heating, cooling, lighting, appliances, insulation, and ventilation systems. They collect data to understand how energy is used throughout the building.
Identification of Inefficiencies: Through detailed analysis, auditors identify areas where energy is being wasted or used inefficiently. This could include outdated equipment, poor insulation, air leaks, or inefficient lighting systems.

## Slide 35: Energy Auditing
Recommendation of Improvements: Energy auditors provide recommendations for improvements aimed at enhancing energy efficiency. These suggestions may include upgrading to energy-efficient appliances, improving insulation, optimizing HVAC systems, installing energy-efficient lighting, or adopting renewable energy sources.
Cost-Benefit Analysis: Auditors often conduct a cost-benefit analysis of the recommended improvements to help building owners understand the potential return on investment for various energy-saving measures.
Customized Solutions: Energy audits are tailored to the specific needs and characteristics of a building. They consider factors like the size, function, age, and structure of the building in providing energy-saving solutions.
Compliance and Standards: Energy audits may also ensure compliance with local energy efficiency standards and regulations, enabling buildings to meet certification requirements such as LEED (Leadership in Energy and Environmental Design) or Energy Star ratings.

## Slide 36: Energy Auditing
Environmental Impact: Improving energy efficiency in buildings reduces greenhouse gas emissions and lessens the environmental impact associated with energy consumption.
Energy auditing is a crucial step in achieving energy efficiency and sustainability in buildings. By identifying areas for improvement and recommending solutions, these audits empower building owners and managers to make informed decisions that can lead to significant energy and cost savings, as well as environmental benefits.

## Slide 37: Steps of Energy Auditing
An energy audit for buildings involves a systematic process to evaluate energy usage, identify inefficiencies, and recommend improvements to enhance energy efficiency. Here are the typical steps involved in an energy auditing process for buildings:
Gather Information: Collect historical energy bills, building plans, occupancy schedules, and any other relevant data to understand the building's energy usage patterns.
Preliminary Assessment: Conduct a walkthrough of the building to identify potential energy wastage, such as air leaks, inefficient equipment, lighting, insulation, etc.
Utility Analysis: Analyze historical energy bills to understand usage patterns, peak demand, and cost breakdowns for various energy systems in the building.
Energy Modeling and Simulation: Use specialized software to create a detailed model of the building to simulate energy usage and identify areas where improvements can be made.

## Slide 38: Steps of Energy Auditing
Building Systems Inspection: Evaluate the performance of various building systems including HVAC (heating, ventilation, and air conditioning), lighting, water heating, insulation, etc. Check for maintenance issues and assess the condition and efficiency of the systems.
Data Logging and Monitoring: Install data loggers or monitoring equipment to collect real-time data on energy consumption and usage patterns to better understand peak loads and when and where energy is being used most.
Identify Energy Conservation Measures (ECMs): Analyze the data collected and observations made to identify potential energy-saving opportunities such as upgrading equipment, improving insulation, optimizing lighting, implementing renewable energy sources, etc.
Cost-Benefit Analysis: Evaluate the costs associated with potential improvements and weigh them against the estimated energy savings and payback period to prioritize the most cost-effective measures.

## Slide 39: Steps of Energy Auditing
Recommendation and Report: Prepare a comprehensive report detailing the findings, potential energy-saving measures, cost estimates, and the expected return on investment. This report may also include a prioritized list of recommendations.
Implementation Plan: Develop a plan that outlines the steps required to implement the recommended energy-saving measures. This may include project timelines, procurement of materials, hiring contractors, and more.
Monitoring and Verification: After implementing the energy-saving measures, continue to monitor energy consumption to verify that the changes made have resulted in the expected energy savings.
Continuous Improvement: Energy audits are not a one-time event. Regular audits, continuous monitoring, and ongoing improvements are essential to maintain and enhance a building's energy efficiency over time.
Each building is unique, so the steps might vary depending on the specific requirements and complexities of the structure being audited. The goal is to identify opportunities to reduce energy usage, lower costs, and improve the overall environmental impact of the building.

## Slide 40: References
Boyle, G. (2013). Renewable Energy Power For A Sustainable Future (Vol. Third Edition). Oxford: Oxford University Press.
Elprocus. (2022). Retrieved October 9, 2022, from https://www.elprocus.com/what-is-pyranometer-construction-types-applications/
IEA. (2022). Retrieved October 9, 2022, from https://www.iea.org/reports/offshore-wind-outlook-2019
Koirala, D. R. (2019). Principals of Engineering Thermodynamics and Heat Transfer. Kathmandu: Shree Chandeswori Publication Pvt. Ltd. .
S. Hasan, S., & Sharma, D. (2009). Non-Conventional Energy Resources. Delhi: S. K. Kataria and Sons.
Sharma, D., & Hasan, S. (2009). Non-Conventional Energy Sources (Second Edition ed.). Delhi: S.K. Kataria and Sons.
Singal, R. (2011). Non-Conventional Energy Resources (Vol. Third Edition). Delhi: S. K. Kataria and Sons.