## Slide 1: Power Systems Operation and Control
Lecture 15
Project assignments and Assessments
Lecturer: Teshome Goa (Assist. Prof.)
Final exam on Power Systems Operation and Control
The exam contains Three parts:
Part I:Multiple choice, Part II: True-False and Part III: Subjective questions
The total Mark is : 100% Time allowed: 1:30 hrs
Name:_____________________ ID no:_____________

## Slide 2: Instruction I: Multiple choice questions
For the questions, Question number one up to question number 30 choose the correct answer from the given multiple choices and circle the right answer.
Each question weights : 2 marks .

## Slide 3: Question number one and two
An electric power system that supplies power to homes and industries for a sizeable region is called
a. Generator
b. Grid
c. Transmission Line
d. Compensator
2. The main components of System are
Generation System
Transmission System and Distribution Systems
The Load
All

## Slide 4
3. All of the following are Renewable energy resource except
Solar power plant
Hydro power plant
Thermal power plant
wind Power plant
4. The knowledge of --------------needed for power flow analysis
a. Bus admittance matrix
b. Types of bus
c. The topology of network
d. All
Question number Three and Four

## Slide 5: Question number Five and Six
5. Which one of the following is used for the economic operation of power system .
Unit commitment
Economic load dispatch
Optimal power flow .
All
6. Which one of the following is not true about Unit commitment
a. Sharing the demand among all generation unit
b. Minimizing the startup cost of some of the power plant while starting quick starting power units
c. Sharing the demand among only the started generation but not for all units
d. Hydro power plant is used over thermal for peak demand supplying

## Slide 6
Question number seven and eight
7. The following statement describes the control variables of thermal power plant except
a. Real power generation
b. Reactive power generation
c. Bus voltage magnitude
d. A and C
8. Which one of the following is true about the economic operation of thermal power plant
a. Minimizing the operational cost of the plant is main objective
b. Power generations are quadratic function
c. Marinating generation limit is one of the constraint's
d. All

## Slide 7: Question number nine and ten
9. which, one of the following is the importance of ELD with the transmission line loss consideration
a. Minimizing the overall cost
b. Improving system efficiency
c. Maintaining stability
d. all
Which one of the following is not true about unit commitment
a. Checking the Power plant start-up and shutdown costs.
b. Determining the Operating expenses all base-case generation units
c. Evaluating the Ramp rates of units
d. Schedules for maintenance.

## Slide 8: Question number eleven and twelve
11. One of the following not true about the equality constraints of optimal power flow
a. Operation cost minimization
b. Reducing emission
c. Checking the power transfer capability of lines
d. VAR investment reduction
12. The following is true about Stochastic OPF except
a. Addresses uncertainties by optimizing the worst-case scenario
Incorporates uncertainties in load
Considers generation uncertainty
Consider the market prices change

## Slide 9: Question number 13 and 14
13. One of the following not true about hydrothermal scheduling
a. Hydro starts during peak load case
b. Large thermal unit can easily starts to supply the peak load compared to hydro
c. The objective function is to minimize the operating fuel cost thermal plants while maintaining water volume of hydro
d. it’s one of conventional power plant scheduling
14. One of the following is not true about hydrothermal-RE scheduling
a. Increase the grid mix opportunities
b. RE is the most regular and efficient power plant compared to hydro
c. Wind and solar power is affected by environmental conditions
d. The mix of hydro-thermal with RE reduces the emission

## Slide 10: Question number 15 and 16
15. The following are the common decision variable of hydro-thermal plants except
Market Pricing, pricing decisions based on supply and demand.
Emissions Levels
Investment Decisions
None.
16. The primary objectives of power system control include
a. Ensuring the system remains stable under normal and abnormal conditions
b. Automatic generation control
c. Maintaining stability
d. All

## Slide 11: Question number 17 and 18
17. which one of the following is not true about primary control of power system
a. provides a longer-term correction to restore system frequency and voltage
b. provides immediate response to changes in system conditions
c. primarily focusing on maintaining stability
d. none
18. One of the following is not true
a. For centralized control, the entire power system is monitored and controlled by a single central controller
b. Distributed control makes use of several local controllers
c. Hierarchical Management is possible in centralized control
d. All

## Slide 12: Question number 19 and 20
19. One of the following is not fundamental components while modeling the system for load frequency control
a. Modeling governor system
b. Turbine modeling
c. Generator modeling
d. None
20. Which one is not true for load frequency control
a. The generation frequency increases when load reduces
b. Generation scheduling is one of the most common techniques in load frequency control
c. The reference setting of power is one of the frequency control
d. Derivative control can minimize the error up to zero

## Slide 13: Question number 21 and 22
,
21. One of the following is the frequency dependent load
a. Motor load
b. Lighting load
c. Heating load
d. B and c
22. If the generation is not adequate enough to balance the load demand & loss, the most effective solution is
a. Starting thermal power plants
b. Load shedding
c. Generation rescheduling
d. None

## Slide 14: Question number 23 and 24
23. Which one of the following is as free governor operation
a. Changing the reference power
b. Changing the load
c. Changing both the load and reference power
d. A and c
24. Which one of the following is not true about the Tie-line Power
a. AC-Tie line is very good for long transmission line
b. DC Tie-line needs converter stations
c. Multi-tie line enable for larger-scale power transfers and facilitate complex power trading agreements
d. All

## Slide 15
25. One of the following is true about reactive power compensation
a. Maintain the bus voltage within the limit
b. maintain acceptable voltage at the receiving end during no-load and loaded condition
c. Capacitor generates reactive
d. All
26. One of the following is not true about power factor :
a. As power factor increases the system efficiency increase
b. The power factor is unity at industrial load
c. Capacitor boosts power factor
d. A and c
Question number 25 and 26

## Slide 16
Question number 27 and 28
27. Which one of the following is not true about Uncompensated transmission lines' characteristics
a. Improved line loss
b. Poor voltage regulation
c. Good stability
d. High efficiency
28. The following is true about voltage control methods except
a. AVR Control
Transformer Tap changing
Synchronous Condensers
All

## Slide 17
29. Which one of the following is the most common recent excitation system to control the voltage
a. DC excitation system
b. Ac excitation system .
c. Brushless AC excitation
d. None
30. Which one of the following is not true about Multiple Contingencies
a. Outage of two or more generation units at a time
b. N-1 Contingency
c. N-2 contingency
d. All
Question number 29 and 30

## Slide 18: II. For the following question (questions from 1-to 10) say True if the statement is correct and say False if it’s incorrect
Balancing demand across various loads to prevent overloading and ensure efficient one of essence of economic operation of power system.
For automatic non-economic regulation, the output level of power plants changes around a base setting as area control error is fixed
For economic operation of power system, The incremental production cost, is made up of incremental fuel cost plus the incremental cost of labor, water, maintenance etc
Unit commitment involves determining which generating units to turn ON or OFF over a specific time horizon to meet electricity demand reliably and cost-effectively
Optimal power flow typically focuses on none -real-time operation
Total mark= 20% Each question weights 2 marks

## Slide 19: Cont.…
6. The optimal scheduling problem in a hydro-thermal system can be stated as to minimize the fuel cost of thermal plants under the constraint of water availability for hydro-generation
7. Electric power must always be produced at a rate equal to its consumption because it cannot be stored in vast quantities
8. In load frequency control, the Fly-balls moves downward when speed increases
9. In central load frequency control of a given control area, the change (error) in frequency is known as Area Control Error (ACE).
10. AGC systems respond to variations in frequency or load by automatically modifying the output of generating units

## Slide 20
Instruction III. Answer the following four questions as per the Request in space provided
Total mark= 20% Each question weights five marks

## Slide 21
    31. The four basic components needs to be modeled for load frequency control are:
    ____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________
Question number 31

## Slide 22: Question number 32
32. The four components model needed for AVR control are :
__________________________________________________________________________________
__________________________________________________________________________________
__________________________________________________________________________________
__________________________________________________________________________________

## Slide 23: Question number 33
33. The difference and similarity between single area and Tie Line frequency control are? Mention at least four
______________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 24: Question number 34
34. What are the main economic operation methods of power systems?
____________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 25: Answer Q. 1- Q.30
Instruction I:
1 B
2. D
3. C
4. D
5. D
6. A
7. C
8. D
9. D
10. B
11. C
12. A
13. B
14. B
15. D
16. D
17. A
18. C
19. D
20. D
21. A
22. B
23. B
24. A
25. D
26. B
27. A
28. D
29 C
30. C

## Slide 26: Answer For True-False Questions Q. 1- Q.10
True
False
True
True
False
True
True
False
True
True

## Slide 27: Answer Q. 31
31.
Governor system .
Turbine system
Generator system.
Load system (Frequency dependent and Frequency independent ).

## Slide 28
Answer Q. 32
32.
Voltage transformer or VT model
Amplifier model .
Excitation system model
Generator model

## Slide 29: Answer Q. 33
33.
Both single area and Tie-line controls the frequency with respect of load change either by generation rescheduling or load shading emergency case)
The single area control only focuses on controlling a given area frequency based on the load change within the area
Whereas, the tie-line frequency control should responds to the change in load from two or more interconnected area
The Tie-line control also focuses on controlling the line power flow through interconnected network

## Slide 30: Answer Q. 34
34.
Economic load dispatch
Unit commitment
Optimal power flow
Hydro-thermal and hydro-thermal , and RE schedulings
.

## Slide 31: Project Assignment
1. If three generators are interconnected into a grid is required to supply a maximum demand of 1200 MW. Determine the ED of the generators neglecting transmission losses using Lagrange multiplier based on their input cost function as given below. See lecture 3 and lecture four for your reference while answering it.

## Slide 32
Thank you !