## Slide 1
Biometrics
Lecture 8
Multimodal Biometrics
Lecturer: Dr. Joshua Okemwa

## Slide 2: Expected learning outcomes
At the end of the lecture you will be able to:
Understanding multimodal systems.
Discuss the importance of multimodal systems.
Evaluate the challenges, recent developments and future trends of multimodal systems .

## Slide 3: Areas of focus
The main areas of focus in this presentation include:
Overview of multimodal systems
System demonstration
Multimodal vs unimodal systems
Application of multimodal system.

## Slide 4: Introduction
Multimodal biometrics integrates multiple biometric traits, such as fingerprints, facial recognition, iris scans, and voice recognition, into a single system.
This combination enhances the system's robustness and
reduces the chances of false positives and false negatives.

## Slide 5: purpose of multimodal biometrics
The integration of multiple biometric modalities addresses the limitations of unimodal systems, such as susceptibility to spoofing, low recognition accuracy under varying conditions, and higher error rates.

## Slide 6: Unimodal biometrics
Unimodal biometrics has several problems such as noisy data, intra class variation, inter class similarities, non universality and spoofing which cause this system less accurate and secure.
To overcome these problems and to increase level of security multimodal biometrics is used.

## Slide 7: cont…
Multimodal biometrics makes the use of multiple source of information for personal authentication.
Multimodal biometrics has becoming very popular now days since it is at the frontier of unimodal biometrics.

## Slide 8: unimodal vs multimodal
Unimodal biometrics approach is simpler and more cost-effective, making it easier to design, implement, and maintan.
However, unimodal systems can be less reliable and more
susceptible to spoofing, environmental limitations, and higher
false acceptance or rejection rates.

## Slide 9: Cont…
In contrast, multimodal biometrics leverages multiple biometric traits, like combining fingerprint, face, and voice recognition. This increases accuracy, security, and flexibility by compensating for the weaknesses of individual modalities. While multimodal systems are more complex and costly to deploy and maintain, they provide a more robust and reliable means of authentication by integrating various biometric sources reliable means of authentication by integrating various biometric sources.

## Slide 10: System demonstration
Source: Journal (SIPIJ)
Author:P. S. Sanjekar

## Slide 11: Explanation
Multimodal biometric system can operate in serial mode or parallel mode. In serial mode of operation, the system processes one biometric modality at a time. Each modality's output helps refine or limit the pool of potential identities before moving to the next modality. This can reduce the overall recognition time.

## Slide 12: Cont…
In parallel mode, all selected biometric modalities are captured and processed simultaneously. This method increases the chances of accurate identification since it analyzes multiple data points at once, though it can require more computational resources. In parallel mode of operation, information from different modalities is used simultaneously.

## Slide 13: Cont…
In case of multimodal biometric system decision can be made at various levels of fusion like Feature level fusion, Matching score level fusion and Decision level fusion.

## Slide 14: note
Choosing between serial and parallel modes depends on the specific needs of the application. Serial mode is ideal for systems prioritizing resource efficiency and lower processing costs, while parallel mode suits environments where high accuracy and speed are essential, even with higher operational costs.

## Slide 15: advantages
Improved Accuracy: Combining multiple data sources increases the probability of correct identification and reduces false acceptance and rejection rates.
Enhanced Security: Multimodal systems are more resilient against spoofing and fraudulent access since replicating multiple biometric traits is more challenging.

## Slide 16: cont…
Adaptability to Different Environments: Multimodal biometrics can adapt to various environmental conditions. For instance, if face recognition is less reliable in poor lighting, the system can prioritize fingerprint or voice recognition.
Improved User Experience: Users have multiple ways to authenticate themselves. If one biometric modality fails (e.g., due to a bandaged finger or noisy background affecting voice), other modalities can still confirm identity, allowing for smoother interactions.

## Slide 17: cont…
Enhanced Verification for Sensitive Applications: In high-security environments (e.g., government facilities, banking, or military applications), the layered approach of multimodal biometrics meets stricter security requirements.
Supports Multiple Authentication Scenarios: Multimodal systems can tailor the modalities required based on the risk level.

## Slide 18: disadvantages
High Implementation Costs: Multimodal systems require additional hardware and software to capture, process, and integrate data from multiple biometric sources. This makes the setup and maintenance more expensive than single-modal systems.
Complex System Architecture: Integrating multiple biometrics requires advanced data fusion algorithms, making system design, configuration, and troubleshooting more complex.

## Slide 19: cont…
Greater Processing Power Needed: Multimodal systems need significant processing resources to handle multiple biometric data streams and algorithms in real time, especially in high-traffic environments.
Increased Storage Demand: Since multiple biometric templates (e.g., voice, fingerprint, and face data) need to be stored for each user, the system requires substantial storage capacity, which can be costly.

## Slide 20: cont…
Complexity in Data Fusion: Combining biometric data from different sources can lead to higher error rates if the data fusion isn’t well-optimized, especially if one modality produces inaccurate results.
Error Propagation: If an error occurs in one modality, it may affect the accuracy of the entire system, especially if that modality’s data heavily influences the final decision.

## Slide 21: fusion levels in multimodal biometrics
Generally there are three fusion levels in multimodal biometrics: feature level fusion, matching score level fusion and decision level fusion respectively. It is generally believed that a combination scheme applied as early as possible in the recognition system is more effective

## Slide 22: explanation
Feature Level Fusion is a method in multimodal biometric systems where the feature sets extracted from different biometric modalities are combined into a single, unified feature set before making a classification or identification decision.
This approach is where raw or processed data from each biometric source are merged a representation of the individual’s identity.

## Slide 23: cont…
Matching Score Level Fusion is a technique used in multimodal biometric systems where each biometric modality (e.g., fingerprint, face, voice) independently produces a score that represents the likelihood of a match. These scores are then combined to make a final decision about identity verification or recognition.

## Slide 24: cont…
Decision Level Fusion in multimodal biometric systems is a technique where each biometric modality independently makes its own decision about a match (e.g., "accept" or "reject") before a final decision is made by combining these individual outputs.
This method is typically used when individual biometric systems are separate and each can independently perform identification or verification.

## Slide 25: challenges& Concerns
Complexity and Cost: Implementing and maintaining a multimodal system is more resource-intensive than a single-modal one.
Data Fusion: Combining data from multiple modalities (data fusion) can be technically challenging and requires sophisticated algorithms.
Privacy and Data Security: Storing and processing multiple types of sensitive data raises concerns about privacy and the potential for breaches.

## Slide 26: Application
Financial Services: Used in banking for secure transactions, with multimodal verification adding extra layers of security.
Healthcare: Ensures secure patient identification and access to medical records.
Border Security: Airports and border control use multimodal biometrics to enhance security and manage identity verification efficiently.
Corporate Security: High-security facilities often require multimodal biometrics to control access.

## Slide 27: Future directions
AI and Machine Learning: These technologies are improving multimodal biometric systems by enhancing pattern recognition and data fusion techniques.
Mobile Multimodal Biometrics: Growing in mobile and wearable devices, integrating sensors for face, voice, fingerprint, and even gait recognition.

## Slide 28: Future directions
Privacy-Preserving Techniques: Differential privacy and encryption methods are being explored to secure biometric data while respecting user privacy.
Increased Use in Consumer Devices: Mobile phones, smartwatches, and other wearables are beginning to use multiple biometric sensors, such as face, voice, and even gait recognition. These multimodal systems provide secure, convenient, and seamless authentication options on personal devices.

## Slide 29: Review questions
1. Explain the purpose of multimodal biometrics?
2. Elaborate how multimodal biometrics improve security?
3. Highlight challenges in implementing multimodal biometrics?
4. Explain how multimodal biometrics handle variations in user appearance?
5. Discuss some of the applications of multimodal biometrics?
6. Compare to single-modal biometrics in terms of user convenience?

## Slide 30: References
Zhang, D. (2013). Multimodal biometrics: Theory and practice. Springer Science & Business Media.
V. Mane and D. Jadhav, “Review of Multimodal Biometrics: Applications, Challenges and Research Areas,” International Journal of Biometrics and Bioinformatics (IJBB), vol. 3, no. 5, pp. 90-95, 2009. Signal & Image Processing : An International Journal (SIPIJ) Vol.4, No.1, February 2013
F. Yang and Baofeng M. A, “Two Models Multimodal Biometric Fusion Based on Fingerprint, Palm-Print and Hand-Geometry,” in Proc. of 1st International Conference on Bioinformatics and Biomedical Engineering (ICBBE), Wuhan, pp. 498-501, 6-8 July 2007.