## Slide 1: Engineering Thermodynamics I
Lecture 11
Gas Power Cycles
Lecturer: Dr. Melaku Desta

## Slide 2: Lecture learning outcomes:
At the end of this lecture, you will be able to:
Understand air standard assumptions to recognize the simplifications made in the analysis of thermodynamic cycles
Analyze internal combustion cycles and compare and contrast the air-standard Otto and Diesel cycles, focusing on efficiency, compression ratios, and thermodynamic processes.
Examine gas-turbine power cycles and understand the Brayton cycle as the fundamental thermodynamic model for gas turbines, and assess modifications such as the gas turbine cycle with regeneration.
Apply thermodynamic concepts to practical systems
to evaluate performance enhancements in power cycles,
such as regeneration.

## Slide 3: Content
Fundamental Aspects of Power Cycle Analysis
The Carnot Cycle and its Value in Engineering
Air Standard Assumptions
Air-Standard Otto Cycle
Air-Standard Diesel Cycle
Brayton Cycle: The Ideal Cycle for Gas-Turbine Engines
Gas-Turbine Cycle with Regenerator
Summary
References

## Slide 4: 1. Fundamental Aspects of Power Cycle Analysis
Thermodynamic Cycles can be grouped into:
    Power cycles
    Refrigeration cycles
Engines - devices or systems used to produce a net power output – the thermodynamic cycles they operate on are called Power Cycles.
Refrigerators/Air Conditioners/Heat Pumps- devices or systems to produce a refrigeration effect- the thermodynamic cycles they
operate on are called Refrigeration Cycles.

## Slide 5: 1. Fundamental Aspects of Power Cycle Analysis Cont…
Thermodynamic Cycles
  Closed cycles - the working fluid is returned to the initial state at the end of the cycle and is recirculated.
  Open cycles - the working fluid is renewed at the end of each cycle instead of being recirculated.
Heat Engines
  Internal Combustion Engines
  External Combustion Engine

## Slide 6: 1. Fundamental Aspects of Power Cycle Analysis Cont…
In actual devices, thermodynamic cycles (such as those in engines, refrigerators, or power plants) deviate significantly from idealized cycles due to real-world complications.
Two major factors that make these cycles difficult to analyze are:
  Friction and other irreversibilities
  Lack of equilibrium conditions
    Finite time processes
    Dynamic effects
    Chemical non-equilibrium

## Slide 7: 1. Fundamental Aspects of Power Cycle Analysis Cont…
  These irreversibilities mean that real cycles cannot achieve the theoretical maximum efficiency predicted by idealized models (e.g., Carnot efficiency).
Figure 1: P-v diagrams of Actual and Ideal Cycles
url: https://slideplayer.com/slide/7656651/25/images/3/BASIC+CONSIDERATIONS+IN+THE+ANALYSIS+OF+POWER+CYCLES.jpg

## Slide 8: 1. Fundamental Aspects of Power Cycle Analysis Cont…
Heat engines are designed for the purpose of converting other forms of energy (usually in the form of heat) to work, and the thermal efficiency is:
              or
No body can develop a cycle more efficient than the Carnot cycle [1].
Idealizations and simplifications – for analysis of power cycles
  Cycle does not involve any friction
  Expansion and compression processes –quasi-equilibrium
  Pipes are well-insulated
  Changes in kinetic and potential energy could be neglected

## Slide 9: 2. The Carnot Cycle and its Value in Engineering
The Carnot cycle provides a fundamental guideline for energy efficiency.
Though impractical, it inspires modern engineering innovations.
Engineers strive to approach Carnot efficiency in practical designs.
The Carnot cycle consists of four reversible processes:
  Isothermal Expansion: Heat absorption at constant temperature
  Adiabatic Expansion: Cooling without heat exchange.
  Isothermal Compression: Heat rejection at constant
  temperature
  4. Adiabatic Compression: Heating without heat
  exchange.

## Slide 10: 2. The Carnot Cycle and its Value in Engineering Cont…
Limitations of the Carnot Cycle
  Idealized assumptions make it impractical for real-world use.
  Requires perfectly reversible processes, which are impossible to achieve.
  Only applicable between two temperature reservoirs.
Figure 2: P-v and T-s diagrams of a Carnot Cycle
url: https://www.mechanicaltutorial.com/pictures/content_picture/carnot_cycle/carnot_cycle_graph.png

## Slide 11: 3. Air Standard Assumptions
In gas power cycles working fluid remains a gas throughout the entire cycle.
Examples of devices operating on gas power cycles
  Spark-ignition automobile engines.
  Diesel engines
  Conventional gas turbines
Because of the combustion process, the composition of the working fluid changes from air and fuel to combustion products during the course of the cycle.
The actual gas power cycles are rather complex.
To reduce the analysis to a manageable level, we utilize
the air-standard assumptions.

## Slide 12: 3. Air Standard Assumptions Cont…
Air standard assumptions are simplifications used in thermodynamic analysis to make the study of internal combustion engines and gas power cycles more manageable without dealing with the complexities of real-world combustion and fluid behavior [2].
The following are Air Standard Assumptions:
  The working fluid is air
  Constant specific heats
  Internally reversible processes
  Heat addition and rejection
  No chemical reactions
  No exhaust losses
Figure 3: Air Standard Assumptions
url: https://slideplayer.com/slide/5179287/16/images/11/Air+Standard+Assumptions.jpg

## Slide 13
4. Air Standard Otto Cycle
An overview of reciprocating Engines
A reciprocating engine is a type of internal combustion engine that converts chemical energy from fuel into mechanical work using reciprocating (back-and-forth) motion [3].
These engines are widely used in transportation, power generation, and industrial applications.
The reciprocating engine is the powerhouse of:
  The vast majority of automobiles
  Trucks,
  Light aircraft
  Ships, and
  Electric power generators

## Slide 14
4. Air Standard Otto Cycle Cont…
Top Dead Center (TDC)- the position of the piston when it forms the smallest volume in the cylinder.
Bottom Dead Center (BDC)-The position of the piston when it forms the largest volume in the cylinder
Stroke of the engine- the distance between TDC and BDC- the largest distance that the piston can travel in one direction.
Bore –the diameter of the piston
Intake Valve- The air or air-fuel mixture is drawn into the
cylinder through.
Exhaust Valve- The combustion products are expelled from the cylinder through.
Figure 4: Components of a reciprocating engine
url: https://encrypted-tbn3.gstatic.com/images?q=tbn:ANd9GcSmKi70cK9tml9x4x-OLmfw1EnF8ekc6GxQBILLnTbyVILYmsf7

## Slide 15
4. Air Standard Otto Cycle Cont…
The minimum volume formed in the cylinder when the piston is at TDC is called the clearance volume.
The volume displaced by the piston as it moves between TDC and BDC is called the displacement volume.
The ratio of the maximum volume formed in the cylinder to the minimum (clearance) volume is called the compression ratio r of the engine:
Figure 5: Displacement and Clearance Volume
url: https://encrypted-tbn0.gstatic.com/images?q=tbn:ANd9GcRwAlkUCQSXi0rsP0By7zgzPG-oGADb6sU8PA&s

## Slide 16
4. Air Standard Otto Cycle Cont…
The Mean Effective Pressure (MEP): it is a fictitious pressure that, if it acted on the piston during the entire power stroke, would produce the same amount of net work as that produced during the actual cycle.
The Mean Effective Pressure can be used as a parameter to compare the performance of reciprocating engines of equal size.
The engine with a larger value of MEP will deliver more net work per cycle and thus will perform better.

## Slide 17
4. Air Standard Otto Cycle Cont…
Figure 6: Mean Effective Pressure
url: https://www.engineersedge.com/graphics/chap8-5.png

## Slide 18
4. Air Standard Otto Cycle Cont…
The Air Standard Otto Cycle is a theoretical model that approximates the behavior of a spark-ignition internal combustion engine, commonly found in gasoline-powered vehicles [3].
The Otto cycle is the ideal cycle for spark-ignition reciprocating engines.
In most spark-ignition engines, the piston executes four complete strokes (two mechanical cycles) within the cylinder, and the crankshaft completes two revolutions for each thermodynamic cycle.
It consists of four distinct processes that occur in a closed system, assuming air as the working fluid and neglecting any real-world complexities
like friction or heat losses.
These engines are called four-stroke internal combustion engines.

## Slide 19
4. Air Standard Otto Cycle Cont…
The working Principle of Air Standard Otto Cycle
Figure 7: Working principle of Air Standard Otto Cycle
url: http://sounak4u.weebly.com/uploads/1/2/7/0/12702026/9860058_orig.png

## Slide 20
4. Air Standard Otto Cycle Cont…
Initially, both the intake and the exhaust valves are closed, and the piston is at its lowest position (BDC).
During the compression stroke, the piston reaches its highest position (TDC).
The spark plug fires and the mixture ignites, increasing the pressure and temperature of the system.
The high pressure gases force the piston down, which in turn forces the crankshaft to rotate, producing a useful work output during the expansion or power stroke.

## Slide 21
4. Air Standard Otto Cycle Cont…
At the end of this stroke, the piston is at its lowest position (the completion of the first mechanical cycle), and the cylinder is filled with combustion products.
Now the piston moves upward one more time, purging the exhaust gases through the exhaust valve (the exhaust stroke), and down a second time, drawing in fresh air-fuel mixture through the intake valve (the intake stroke).
Notice that the pressure in the cylinder is slightly below during the intake stroke.

## Slide 22
4. Air Standard Otto Cycle Cont…
The thermodynamic analysis of the actual four-stroke or two-stroke cycles can be simplified significantly if the air-standard assumptions are utilized.
The resulting cycle, which closely resembles the actual operating conditions, is the ideal Otto cycle.
It consists of four internally reversible processes:
    1-2 Isentropic compression
    2-3 Constant volume heat addition
    3-4 Isentropic expansion
    4-1 Constant volume heat rejection

## Slide 23
4. Air Standard Otto Cycle Cont…
The P-v and T-s diagram of an Otto Cycle
Figure 8: P-v and T-s diagram of an Otto Cycle
url: https://4.bp.blogspot.com/-5myRAsvqta0/WeYIGLbIAMI/AAAAAAAAIi8/TBrB9BCohcoeXY_z8agJRo5jzNnXp5zxgCEwYBhgL/s1600/P-V%2Band%2BT-S%2BDiagram%2Bof%2BOtto%2BCycle%2Bwith%2BP%252C%2BV%252C%2BT%2Band%2BS.png

## Slide 24
4. Air Standard Otto Cycle Cont…
The Otto cycle is executed in a closed system, and disregarding the changes in kinetic and potential energies, the 1st law relation for any of the processes is expressed, on a unit-mass basis, as
No work is involved during the two heat transfer
processes since both take place at constant volume.

## Slide 25
4. Air Standard Otto Cycle Cont…
Then, the thermal efficiency of the ideal Otto cycle under the cold air standard assumptions becomes:
Processes 1-2 and 3-4 are isentropic, and

## Slide 26
4. Air Standard Otto Cycle Cont…
Example:
The compression ratio of an air-standard Otto cycle is 9.5. Prior to the isentropic compression process, the air is at 100 kPa, 35°C, and 600 cm³. The temperature at the end of the isentropic expansion process is 800 K. Using specific heat values at room temperature, determine:
  The highest temperature and pressure in the cycle,
  The amount of heat transferred in (in kJ),
  The thermal efficiency, and
  The mean effective pressure (MEP).
,

## Slide 27
4. Air Standard Otto Cycle Cont…
Solution:
For the Isentropic Compression:
and,
The highest temperature occurs at state 3:
Given

## Slide 28
4. Air Standard Otto Cycle Cont…
The highest pressure is found using the ideal gas law:
Heat addition occurs during The mass of air is determined:
Heat added:

## Slide 29
4. Air Standard Otto Cycle Cont…
The thermal efficiency:
It is dependent on the compression ratio:
Mean Effective Pressure (MEP) is defined as:
And, the net work output:
Displacement Volume:

## Slide 30
4. Air Standard Diesel Cycle Cont…
The Diesel cycle is the ideal cycle for the compressed ignition (CI) reciprocating engines.
In spark-ignition engines (also known as gasoline engines), the air-fuel mixture is compressed to a temperature that is below the auto ignition temperature of the fuel, the combustion process is initiated by firing a spark plug [4].
In CI engines (also known as diesel engines), the air is compressed to a temperature that is above the auto ignition temperature of the fuel, and combustion starts on contact as the fuel is injected into this hot air.
Therefore, the spark plug and carburetor are replaced
by a fuel injector in diesel engines.

## Slide 31
4. Air Standard Diesel Cycle Cont…
The working principle is:
The fuel injection process in diesel engines starts when the piston approaches TDC and continues during the first part of the power stroke.
Because of this longer duration, the combustion process in the ideal Diesel cycle is approximated as a constant-pressure heat-addition process.
This is the only process where the Otto and the Diesel cycles differ.
The remaining three processes are the same for both ideal cycles.
  Process 1-2 : Isentropic compression
  Process 2-3 : Constant pressure heat addition
  Process 3-4 : Isentropic expansion
  Process 4-1 : Constant-volume heat rejection

## Slide 32
4. Air Standard Diesel Cycle Cont…
The Diesel cycle is the ideal cycle for the compressed ignition (CI) reciprocating engines.
Figure 9: P-v and T-s diagram of Diesel Cycle
url: https://mechanicalbooster.com/wp-content/uploads/2017/10/Dieselcycleworkingprocess-e1591892297266.png

## Slide 33
4. Air Standard Diesel Cycle Cont…
Noting that the Diesel cycle is executed in a piston-cylinder device, which forms a closed system, the amount of heat transferred to the working fluid at constant pressure and rejected from it at constant volume can be expressed as:
The thermal efficiency of the ideal Diesel cycle under the cold-air-standard assumption becomes:
)

## Slide 34
4. Air Standard Diesel Cycle Cont…
We now define a new quantity, the cutoff ratio as the ratio of the cylinder volumes after and before the combustion process:
Utilizing this definition and the isentropic ideal-gas relations for processes 1-2 and 3-4, we see that the thermal efficiency relation reduces to:

## Slide 35
4. Air Standard Diesel Cycle Cont…
Example:
An ideal Diesel engine has a compression ratio of 18 and uses air as the working fluid. The state of air at the beginning of the compression process is 100 kPa and 25°C. If the maximum temperature in the cycle is not to exceed 2100 K, determine:
  The thermal efficiency of the cycle.
  The mean effective pressure (MEP).
Assume constant specific heats for air at room temperature.

## Slide 36
4. Air Standard Diesel Cycle Cont…
Solution:
Let’s determine and for isentropic compression:
For the constant pressure heat addition:
=

## Slide 37
4. Air Standard Diesel Cycle Cont…
Calculate Heat Input and Heat Rejected:
Heat Input
Heat Rejected
Thermal efficiency
Alternatively, using Diesel efficiency formula
)
)

## Slide 38
4. Air Standard Diesel Cycle Cont…
Mean Effective Pressure (MEP)
Net Work Output
Displacement Volume
First, find specific volume at State 1:
Therefore,

## Slide 39: 6. Brayton Cycle
Brayton cycle is used for gas turbines only where both the compression and expansion processes take place in rotating machinery.
Gas turbines usually operate on an open cycle.
Fresh air at ambient conditions is drawn into the compressor, where its temperature and pressure are raised.
The high-pressure air proceeds into the combustion chamber, where the fuel is burned at constant pressure.
Figure 10: An Open Cycle Gas Turbine Cycle
url: https://ars.els-cdn.com/content/image/3-s2.0-B9780323995603000065-f07-04-9780323995603.jpg

## Slide 40: 6. Brayton Cycle Cont…
The resulting high-temperature gases then enter the turbine, where they expand to the atmospheric pressure, producing power.
The exhaust gases leaving the turbine are thrown out (not recirculated), causing the cycle to be classified as an open cycle.
The open gas-turbine cycle can be modeled as a closed cycle, by utilizing the air-standard assumptions.

## Slide 41: 6. Brayton Cycle Cont…
Brayton cycle: the compression and expansion processes remain the same, but the combustion process is replaced by a constant-pressure heat-addition process from an external source, and the exhaust process is replaced by a constant-pressure heat-rejection process to the ambient air.
The ideal cycle that the working fluid undergoes in this closed loop is the Brayton cycle, which is made up of four reversible processes:
  1-2: Isentropic compression (in a compressor)
  2-3: Constant pressure heat addition
  3-4: Isentropic expansion (in a turbine)
  4-1: Constant pressure heat rejection
Figure 11: A Closed Cycle Gas Turbine Cycle
url: https://blogmedia.testbook.com/blog/wp-content/uploads/2023/09/closed-cycle-gas-turbine-1e9a752b.png

## Slide 42: 6. Brayton Cycle Cont…
All four processes of the Brayton cycle are executed in steady-flow devices; thus, they should be analyzed as steady-flow processes.
When the changes in kinetic and potential energies are neglected, the energy balance for a steady-flow process can be expressed as:
Heat transfers to and from the working fluid are:
Figure 12: T-s and P-v diagrams of a simple Brayton Cycle
url: https://www.engineersedge.com/graphics/chap11-4.png

## Slide 43: 6. Brayton Cycle Cont…
The thermal efficiency of the ideal Brayton cycle under the cold air standard assumptions becomes:
Or,
Process 1-2 and 3-4 are isentropic and
Substituting these equations into the thermal efficiency relation and simplifying:
Where,

## Slide 44: 6. Brayton Cycle Cont…
Deviation of Actual Gas-Turbine Cycles from Idealized Ones is due to:
  Pressure drop
  Irreversibilities
The deviation of actual compressor and turbine behavior from the idealized isentropic behavior can be accurately accounted for by utilizing the adiabatic efficiencies of the turbine and compressor, defined as:
Figure 13: Deviation of Actual Gas Turbine with the Idealized ones
url: https://figures.academia-assets.com/51221247/figure_001.jpg

## Slide 45: 7. Gas-Turbine Cycle with Regenerator
In gas-turbine engines, the temperature of the exhaust gas leaving the turbine is often considerably higher than the temperature of the air leaving the compressor [5].
The high-pressure air leaving the compressor can be heated by transferring heat to it from the hot exhaust gases in a counter-flow heat exchanger, which is also known as a regenerator.
Figure 14: Gas Turbine Cycle with Regenerator
url: https://energy.sdsu.edu/testhome/introModule/introimages/TESTcalcrias/gasturbine4.gif

## Slide 46: 7. Gas-Turbine Cycle with Regenerator Cont…
Assuming the regenerator to be well insulated and any changes in kinetic and potential energies to be negligible,
he actual and maximum heat transfers from the exhaust gases to the air can be expressed as:
For ideal regeneration,
Figure 15: T-s diagram of Gas Turbine Cycle with Regenerator
url: https://media.cheggcdn.com/media/04f/04fdf153-51c2-4070-a2e3-e571da50da45/phpC5REzG

## Slide 47: Summary
Power cycles convert heat energy into mechanical work, forming the basis of engines and turbines.
The Carnot cycle represents the idealized thermodynamic cycle with maximum efficiency, serving as a benchmark for real-world power systems.
Air Standard Assumptions simplify thermodynamic analysis by treating the working fluid as air with ideal gas properties, neglecting combustion and heat losses.
Air-Standard Otto Cycle models gasoline engines, consisting of two isentropic and two constant-volume processes.
Air-Standard Diesel Cycle is used for diesel engines, this cycle differs from the Otto cycle by having constant-pressure heat addition, improving efficiency at higher compression ratios.
The Brayton cycle describes gas-turbine engines, vital in
aviation and power generation. Regenerators enhance
thermal efficiency by recycling exhaust heat.

## Slide 48: References
[1]. Thermodynamics – An Engineering Approach, Cengel Y A.,Bole M A., McGraw-Hill Education, 8th edition 2015.
[2]. Fundamentals of engineering thermodynamics, Moran, M. J., Shapiro, H. N., Boettner, D. D., & Bailey, M. B. (2018). (9th ed.). Wiley.
[3]. Internal Combustion Engine Fundamentals, John B. Heywood, 2nd ed. McGraw-Hill, 2020.
[4]. Introduction to Internal Combustion Engines, R. Stone, 4th ed. London, U.K.: Palgrave Macmillan, 2012.
[5]. Gas Turbine Combustion: Alternative Fuels and Emissions, A. H. Lefebvre and D. R. Ballal, 3rd ed. Boca Raton, FL, USA: CRC Press, 2010.
,

## Slide 49
Thank you !