## Slide 1
Chemical Reaction Engineering II- Reactor Design (ChEg 4101)
Prerequisite: Chemical Reaction Engineering I-Reaction Kinetics (ChEg3104)
Lecture 4: Design of Semi-batch Reactor
Week 4
Lecturer: Adamu Esubalew (PhD, ChEg)
Addis Ababa, Ethiopia

## Slide 2
At the end of the lecture, you will be able to:
describe the characteristics of semi-batch batch reactor,
identify the reasons why semi-batch reactor is preferred, and
design semi-batch batch reactor using materials and energy balance equations.
Lecture learning outcomes

## Slide 3
Presentation outlines
Introduction to semi-batch reactor
The reasons of semi-batch reactor preference
Semi-batch batch reactor design equations
Summary

## Slide 4: 4.1. Introduction to semi-batch reactor
Semi-batch reactor: It is a type of chemical reactor that combines features of both batch and continuous reactors.
It is particularly useful for processes that require the addition of reactants during the reaction.
For batch component, the reactor can be operated with a fixed volume of liquid (or solid) phase, and reactants are added at the beginning.
For continuous component, gaseous reactants can be fed continuously during chemical reactions.
4

## Slide 5: Cont’d
Semi-batch reactor is operated at unsteady state .
Semi-batch occurs when some reactants are charged into the reactor at time zero, while other reactants are added during the reaction.
The operation of a simi-batch reactor is one reactant or a product either batch or continuous.
Figure 4.1 demonstrates various forms of semi-batch reactors (Levenspiel, 2011, pg. 84).
Figure 4.1 Various forms of semi-batch reactors
5

## Slide 6: Cont’d
The reactants can be added at different stages of the reaction, which allows for better control over reaction rates and conversion.
It is beneficial for controlling exothermic reactions or for preventing the formation of unwanted by-products.
Semi-batch reactor often has mixing mechanisms to ensure uniform distribution of reactants and temperature throughout the reactor.
Uniform mixing is essential for achieving consistent reaction conditions and maximizing yield.
6

## Slide 7: Cont’d
The semi-batch reactor is a flexible system but is more difficult to analyze than the other reactor types.
It offers good control of reaction speed because the reaction proceeds as reactants are added.
Such reactors are used in a variety of applications from the calorimetric titrations in the laboratory to the large open-hearth furnaces for steel production.
7

## Slide 8: 4.2. The reasons of semi-batch reactor preference
Semi-batch reactor is preferred for the following reasons:
to control highly exothermic reaction,
to react a gas with a liquid,
to remove one of the products to increase the equilibrium of the reaction, and
to minimize unwanted side products by maintaining low concentration of one of the reactants. i.e. enhance selectivity.
8

## Slide 9: Cont’d
Consider the following stochiometric reaction.
(4.1)
Where: A is liquid reactant, B is gas reactant, P is a product, and k is rate constant.
If a liquid reactant A and a gas reactant B to be reacted to form a product P, then semi batch reactor can be preferred to conduct the reaction. Similarly, if the following stochiometric reaction is exothermic, semi-batch reactor will be preferred to carry out the reaction.
C (4.2)
Where: C and D are reactants, R is product, and k is rate constant.
9

## Slide 10: Cont’d
One of the best reasons to use semi-batch reactors is to enhance selectivity in liquid-phase reactions.
For example, consider the following two simultaneous reactions:
(4.3)
(4.4)
One reaction produces the desired product D, and the other reaction produces an undesired product U.
10

## Slide 11: Cont’d
The rate law for the desired reaction (desired product formation, D) is given by:
(4.5)
The rate law for the undesired reaction (undesired product formation, U) is given by:
(4.6)
The instantaneous selectivity SD/U is the ratio of these two rates ( desired/ undesired).
(4.7)
Large selectivity is required to maximize desired product and suppress undesired one.
11

## Slide 12: Cont’d
The selectivity ratio guides us how to produce the most amount of our desired product and the least amount of our undesired product.
The instantaneous selectivity confirms that the formation of desired product (D) can be increased and the formation of undesired product (U) can be decreased by keeping the concentration of A is high and the concentration of B is low.
This result can be achieved through the use of the semi-batch reactor, which is charged with pure A and to which B is fed slowly to A in the reactor.
12

## Slide 13: Cont’d
Semi-batch reactor offers a versatile platform for conducting chemical reactions with improved control over various parameters, making them valuable in both research and industrial applications.
Designing a semi-batch reactor involves several considerations to ensure efficient and safe operations. reactor volume, feed system, mixing mechanism, and temperature control system.
It is required to determine the reactor volume based on the desired production rate, reaction kinetics, and the amounts of reactants to be used.
13

## Slide 14: 4.3. Semi-batch reactor design equations
Consider the following two reactions:
A+B-------->C (4.8)
A+B-------->C+D (4.9)
For semi-batch reactor, the following three possible cases can be occurred.
Case 1: Reactant A and product C are batch, and reactant B is semi-batch (Figure 4.2).
Figure 4.2 Semi-batch reactor
(Fogler, 2015, pg. 228)
14

## Slide 15: Cont’d
Case 2: Reactant B and product C are batch, and reactant A is semi-batch (Figure 4.3).
Figure 4.3 Semi-batch reactor
15

## Slide 16: Cont’d
Case 3: Reactants A & B, product D are batch and product C is semi-batch (Figure 4.4).
Figure 4.4 Semi-batch reactor
16

## Slide 17: 4.3.1. Materials balance equation
Case 1: The species A and C are batch and B is semi-batch (Figure 4.2).
I
Material balance on species A:
(4.10)
Since species A is batch, (4.11)
Figure 4.2 Semi-batch reactor
17

## Slide 18: Cont’d
For species A of batch reaction, the material balance equation is given by:
- (4.12)
Where: V is volume of a mixture, NA is moles of species A at any time t, rA is reaction rate of species A, and t is reaction time.
Number of moles of species, i = (concentration of species, i) * (volume of mixtures)
(4.13)
18

## Slide 19: Cont’d
By substituting equation (4.13) into equation (4.12), you get:
(4.14)
The term dV/ dt in equation (4.14) shows that the volume of the mixtures varies with time.
To find the volume of mixtures variation, let’s consider the over all material balance of all species, and correlate with density of mixtures.
(4.15)
19

## Slide 20: Cont’d
For constant density
(4.16)
For constant volumetric flow rate, volume of reacting mixture varies with time.
The integration of equation (4.16) becomes:
(4.17)
This shows that the volume of a mixture in the reactor increases with time.
Where: V is volume of a mixture at any time t, Vo is initial volume of a mixture, vo is volumetric flow rate, and t is reaction time.
20

## Slide 21: Cont’d
By substituting equation (4.16) into equation (4.14), you get:
(4.18)
By re-arranging equation (4.18) and solve for concentration of reactant A, you get:
(4.19)
This is a material balance equation for species A as batch in semi-batch reactor.
Where: CA is concentration of species A, rA is reaction rate of species A, V is volume of a mixture at any time t, vo is volumetric flow rate, and t is reaction time.
21

## Slide 22: Cont’d
Material balance on species B:
Species B is semi-batch, and the material balance equation is given by:
(4.20)
(4.21)
By differentiate equation (4.21) with respect to time, you get:
(4.22)
Where: NB is moles of species B, FBo is molar flow rate of species B in the feed, V is volume of a mixture at any time t, CB is concentration of species B, rB is reaction rate of species B, and t is reaction time.
22

## Slide 23: Cont’d
Substituting equation (4.22) into equation(4.20), you get:
(4.23)
The term dV/dt= vo, which is volumetric flow rate.
(4.24)
By substituting equation( 4.24) into equation (4.23), and solve for the concentration of species B, you get:
(4.25)
This is a material balance equation for species B as semi-batch feed in semi-batch reactor.
Where: CB is concentration of species B at any time t, CBo is initial concentration of species B vo is volumetric flow rate, V is volume of a mixture at any time t, rB is reaction rate of species B, and t is reaction time.
23

## Slide 24: Cont’d
Material balance on species C:
The martials balance for species C as batch is given by:
(4.26)
NC= CCV (4.27)
By differentiating equation (4.27), you get:
(4.28)
By substituting equation (4.28) into equation (4.26), you get:
(4.29)
24

## Slide 25: Cont’d
The term dV/dt=vo, which is the volumetric flow rate.
By re-arranging equation (4.29) and solve for concentration of species C, you get:
(4.30)
This is a material balance equation for species C as batch fin semi-batch reactor.
Where: CC is concentration of species C at any time t, vo is volumetric flow rate, V is volume of a mixture at any time t, rC is reaction rate of species C, and t is reaction time.
25

## Slide 26: Cont’d
Observations on equations (4.19, 4.25 & 4.30):
If the reaction order is zero, first order and isothermal, the equations can be solved by analytical techniques to determine the conversion/concentration as function of time.
However, if the reaction is not zero order, first order and isothermal, then use numerical techniques to determine the conversion/concentration as function of time.
26

## Slide 27: Cont’d
Case 2: The species A is semi-batch, and species B and C are batch (Figure 4.3).
I
Material balance on species A:
Species A is semi-batch, and the material balance equation is given by:
(4.31)
Figure 4.3 Semi-batch reactor
27

## Slide 28: Cont’d
(4.32)
For constant density, = o (4.33)
By differentiate equation (4.32) with respect to time, you get:
(4.34)
Where: NA is moles of species A, FAo is molar flow rate of species A in the feed, V is volume of a mixture at any time t, CA is concentration of species A, rA is reaction rate of species A, and t is reaction time.
28

## Slide 29: Cont’d
Substituting equation (4.34) into equation(4.31), you get:
(4.35)
The term dV/dt= vo, which is volumetric flow rate.
(4.36)
By substituting equation( 4.36) into equation (4.35), and solve for the concentration of species A, you get:
(4.37)
This is a material balance equation for species A as semi-batch feed in semi-batch reactor.
Where: CA is concentration of species A at any time t, CAo is initial concentration of species A, vo is volumetric flow rate, V is volume of a mixture at any time t, rA is reaction rate of species A, and t is reaction time.
29

## Slide 30: Cont’d
Material balance on species B:
For species B of batch reaction, the material balance equation is given by:
- (4.38)
Where: V is volume of a mixture, NB is moles of species B at any time t, rB is reaction rate of species B, and t is reaction time.
Number of moles of species, i = (concentration of species, i) * (volume of mixtures)
(4.39)
30

## Slide 31: Cont’d
The term dV/ dt=vo, which volumetric flow rate.
By substituting equation (4.39) into equation (4.38) and solve for concentration of reactant B, you get:
(4.40)
This is a material balance equation for species B as batch in semi-batch reactor.
Where: CB is concentration of species B, rB is reaction rate of species B, V is volume of a mixture at any time t, vo is volumetric flow rate, and t is reaction time.
31

## Slide 32: Cont’d
Material balance on species C:
The martials balance for species C as batch is given by:
(4.41)
NC= CCV (4.42)
By differentiating equation (4.42), you get:
(4.43)
By substituting equation ( 4.43) into equation (4.41), you get:
(4.44)
32

## Slide 33: Cont’d
The term dV/dt=vo, which is the volumetric flow rate.
By re-arranging equation ( 4.44) and solve for concentration of species C, you get:
(4.45)
This is a material balance equation for species C as batch in semi-batch reactor.
Where: CC is concentration of species C at any time t, vo is volumetric flow rate, V is volume of a mixture at any time t, rC is reaction rate of species C, and t is reaction time.
33

## Slide 34: Cont’d
Observations on equations (4.37, 4.40 & 4.45):
If the reaction order is zero, first order and isothermal, the equations can be solved by analytical techniques to determine the conversion/concentration as function of time.
However, if the reaction is not zero order, first order and isothermal, then use numerical techniques to determine the conversion/concentration as function of time.
34

## Slide 35: Cont’d
Case 3: The species A, B & D are batch and Species C is semi-batch (Figure 4.4).
Material balance for species A:
Species A is batch; hence, the material balance equation is given by:
- (4.46)
NA= CAV (4.47)
By differentiating equation (4.47) with respect to time, you get:
(4.48)
35
Figure 4.4 Semi-batch reactor

## Slide 36: Cont’d
By substituting equation (4.48) into equation (4.46), you get:
(4.49)
In this case the volume of the mixture decreases since species C is discharged as product.
The over all material balance of all species is given by:
(4.50)
For constant density
(4.51)
For constant volumetric flow rate, volume of reacting mixture decreases with time.
36

## Slide 37: Cont’d
(4.52)
This describes that the volume of a mixture decreases with reaction time.
Where: V is volume of a mixture at any time t, Vo is initial volume of a mixture, vf is volumetric flow rate of outgoing stream, t is reaction time.
By substituting equation (4.51) into equation (4.49) and solve for concentration of the species A, you get:
(4.53)
This is a material balance equation for species A as batch in semi-batch reactor.
Where: CA is concentration of species A, rA is reaction rate of species A, V is volume of a mixture at any time t, vf is volumetric flow rate in the outgoing stream, and t is reaction time.
37

## Slide 38: Cont’d
Material balance on species B: Species B is batch; the material balance equation is given by:
(4.54)
NB= CBV (4.55)
By differentiating equation (4.55) with respect to time, you get:
(4.56)
The term dV/dt=-vf, which is outgoing volumetric flow rate.
By substituting equation (4.56) into equation (4.54) and solve for concentration of species B, you get:
(4.57)
This is a material balance equation for species B as batch in semi-batch reactor.
Where: CB is concentration of species B, rB is reaction rate of species B, V is volume of a mixture at any time t, vf is volumetric flow rate in the outgoing stream, and t is reaction time.
38

## Slide 39: Cont’d
Material balance on species C: Species C is semi-batch; the material balance equation is given by:
0 (4.58)
NC= CCV (4.59)
By differentiating equation (4.59) with respect to time, you get:
(4.60)
The term dV/dt=-vf, which is outgoing volumetric flow rate.
By substituting equation (4.60) into equation (4.58) and solve for concentration of species C, you get:
; FC= CC*vf (4.61)
This is a material balance equation for species C as semi-batch discharge in semi-batch reactor.
Where: CC is concentration of species C, rC is reaction rate of species C, V is volume of a mixture at any time t, vf is volumetric flow rate in the outgoing stream, and t is reaction time.
39

## Slide 40: Cont’d
Material balance on species D: Species D is batch; the material balance equation is given by:
0 (4.62)
ND= CDV (4.63)
By differentiating equation (4.63) with respect to time, you get:
(4.64)
The term dV/dt=-vf, which is outgoing volumetric flow rate.
By substituting equation (4.64) into equation (4.62) and solve for concentration of species D, you get:
(4.65)
This is a material balance equation for species D as batch in semi-batch reactor.
Where: CD is concentration of species D, rD is reaction rate of species D, V is volume of a mixture at any time t, vf is volumetric flow rate in the outgoing stream, and t is reaction time.
40

## Slide 41: Activity 4.1
Consider the following elementary chemical reaction of reactants A and B is conducted in isothermal semi-batch reactor to form product C. The species A is semi-batch and species B and C are batch. The initial concentrations of reactant A and reactant B are 2 kmol/m3 and 4 kmol/m3, respectively. The reactor volume is 0.2 m3. The volumetric flow rate and molar flow rate of the continuous feed are 0.02 m3/min and 0.003 kmol/min, respectively. The reaction rate constant is 0.004 m3/kmol.min.
Based on the given data, determine (a) concentrations of species and (b) the conversions as a function of time when the reaction time is reached to 48 min.
A+B-----------> C
Given: A+B-----------> C, Elementary chemical reaction
-rA=-rB=rC= kCACB
CA0=2 kmol/m3, CB0= 4 kmol/m3, V= 0.2 m3, V0=0.02 m3/min
FA0= 0.003 kmol/min, k= 0.004 m3/ kmol. min
41

## Slide 42: Cont’d
Solution:
Reactant A is semi-batch, and reactant B and product C are batch (Case 2).
The material balance equation for the three species A, B & C, respectively, are given by:
; FAo= CAo*v0 (4.37)
This is a material balance equation for species A as semi-batch feed in semi-batch reactor.
(4.40)
This is a material balance equation for species B as batch in semi-batch reactor.
(4.45)
This is a material balance equation for species C as batch in semi-batch reactor.
The reaction is second order reaction, which shows that we can’t solve the above three equations using analytical technique.
Hence, numerical method is required. i.e use polymath program to simulate the results.
42

## Slide 43: Cont’d
(a). Polymath program to plot concentrations of species A, B& C as a function of reaction time.
d(CA) / d(t) = (FAo-CA*vo)/V+k*CA*CB # A+B-------------> C Elementary chemical reaction.
CA(0) = 2 # kmol/m3
d(CB) / d(t) = -(CB*vo)/V+k*CA*CB #Rate of B, kmol/m3.min
CB(0) = 4 #kmol/m3
d(CC) / d(t) = -(CC*vo/V)+k*CA*CB #Rate of C formation, Kmol/m3.min
CC(0) =0 # kmol/m3
FAo=0.003 # kmol/min
vo=0.02 #m3/min
V=0.2 #m3
k=0.004 #m3/ kmol. min
t(0)=0 # min
t(f) =48 # min
43

## Slide 44: Cont’d
Simulation results:
The concentrations of species A and B are deceased, and concentration of species C ( product) is increased with reaction time up to 24 min, then after, the concentrations of all species A, B & C are remains stagnant (Figure 4.5).
44
Figure 4.5. Concentrations (species A, B & C) as a function of reaction time

## Slide 45: Cont’d
(b). Polymath program to plot conversion of species A& B as a function of reaction time.
A+B-------------> C : Elementary chemical reaction; CA= CAo * (1-XA); CB= CBo* (1-XB)
d(XA) / d(t) =(CA0*(1-XA)*vo-FAo)/(V*CA0)-k*2*(1-XA)*CB0*(1-XB) # Conversion of species A
XA(0) = 0
CA(0) = 2 # kmol/m3
d(XB) / d(t) = (CB0*(1-XB)*vo)/(V*CB0)-k*CA0*(1-XA)*CB0*(1-XB) # Conversion of species B
XB(0) = 0
CB(0) = 4 #kmol/m3
FAo=0.003 # kmol/min
vo=0.02 #m3/min
V=0.2 #m3
k=0.004 #m3/ kmol. min
t(0)=0 # min
t(f) =48 # min
45

## Slide 46: Cont’d
Simulation results:
The conversions of species A and B are exponentially increased with reaction time up to 24 min, then after, conversions are increased slowly (Figure 4.6).
46
Figure 4.6. Conversions of species A & B as a function of reaction time

## Slide 47: 4.3.2. Energy balance equation
Energy balance for semi-batch reactor
For isothermal single reaction, the energy balance equation for species i is given by:
0 (4.66)
For isothermal multiple reactions, the energy balance equation for species i is given by:
0 (4.67)
where q = no of reaction, m = no of species
Where: Q is rate of heat addition, Ws is work done, rA is rate of species A (limiting reactant), V is volume of a mixture, HRx is heat of reaction, Fio/oj is molar flow rate of species i/j, Cpi/j is specific heat capacity of species i/j, Ni/j is moles of species i/j, T is final reaction temperature, and To is initial temperature.
47

## Slide 48
For non–isothermal single reaction, the energy balance equation for species i is given by:
(4.68)
For non-isothermal multiple reactions, the energy balance equation for species j is given by:
(4.69)
where q = no of reaction, m = no of species
Where: Q is rate of heat addition, Ws is work done, rA is rate of species A (limiting reactant), V is volume of a mixture, HRx is heat of reaction, Fio/oj is molar flow rate of species i/j, Cpi/j is specific heat capacity of species i/j, Ni/j is moles of species i/j, T is final reaction temperature, To is initial temperature, t is reaction time.
Cont’d
48

## Slide 49
Consider the following elementary chemical reaction of reactants A and B is conducted in non-isothermal semi-batch reactor to form product C. The species A is semi-batch and species B is batch. The initial concentrations of reactant A and reactant B are 2 kmol/m3 and 4 kmol/m3, respectively. The reactor volume is 0.2 m3. The volumetric flow rate and molar flow rate of the continuous feed are 0.02 m3/min and 0.003 kmol/min, respectively. The reaction rate constant at reference temperature is 0.004 m3/kmol.min.
Based on the given data, determine (a) concentrations of species A & B, (b) the reaction temperature, and (c) the conversions of species A & B as a function of time when the reaction time is reached to 48 min.
A+B-----------> C
Activity 4.2
49

## Slide 50
Additional design data (Activity4.2)
CA0=2 kmol/m3, CB0= 4 kmol/m3, V= 0.2 m3, V0=0.02 m3/min, FA0= 0.003 kmol/min, k=0.004*exp(-95/R*T) m3/ kmol. min, Q= 10 kJ/min, Ws=6 kJ/min, HRx= 15 kJ/kmol, CpA= 10 kJ/kmol.K, CpB=12 kJ/kmol.K, R=8.314,kJ/kmol.K To=308 K
Given: A+B-----------> C, Elementary chemical reaction
-rA=-rB= kCACB
Species A is semi-batch and species B is batch.
The reaction time is reached to 48 min.
Cont’d
50
Figure 4.3 Semi-batch reactor

## Slide 51: Cont’d
Materials and energy balance equations for activity 4.2
(4.37)
(4.40)
i for species (4.68)
The above three equations must be solved simultaneously.
Let's apply polymath program to solve the equations to find concentrations of species, temperature and conversion as a function of time.
51

## Slide 52: Cont’d
Polymath program for concentrations of species A & B, and temperature as a function of time.
d(CA) / d(t) = (FAo-CA*vo)/V+k*CA*CB # Rate of A, kmol/m3. min
CA(0) = 2 # kmol/m3
d(CB) / d(t) = -(CB*vo)/V+k*CA*CB #Rate of B, kmol/m3. min
CB(0) = 4 # kmol/m3
d(T) / d(t) = (Q-Ws+ (-rA*V)*HRx-(FAo*CpA*(T-T0)))/(NA*CpA+NB*CpB) # K/min
T(0) = 308# K, Q=10 #kJ/min, Ws=6 # kJ/min, HRx= 15 # kJ/kmol
-rA=k*CA*CB # reaction rate # kmol/ m3.min
CpA= 10 # kJ/kmol.K, CpB=12 # kJ/kmol.K, NA=V*CA # kmol, NB=V*CB # kmol
FAo=0.003 # kmol/min, vo=0.02# m3/min, V=0.2 # m3, k=0.004*exp(-95/R*T) # m3/ kmol.min
R=8.314 # kJ/ kmol.K
t(0)=0 # min
t(f) =48# min
52

## Slide 53: Cont’d
Simulation results:
Concentrations of species A & B are decreased with reaction time exponentially (Figure 4..7).
After 28 min, concentration of species A is stagnant.
53
Figure 4.7. Concentrations of species A & B as a function of reaction time

## Slide 54: Cont’d
Simulation results:
The reaction temperature is increased with reaction time (Figure 4.8)
54
Figure 4.8. Reaction temperature as a function of reaction time

## Slide 55: Cont’d
Polymath program of conversions of species A& B as a function of time.
d(XA) / d(t) =(CA0*(1-XA)*vo-FAo)/(V*CA0)-k*2*(1-XA)*CB0*(1-XB) #Conversion of A
XA(0) = 0
CB0=4 # kmol/m3, CA0=2 # kmol/m3
d(XB) / d(t) = (CB0*(1-XB)*vo)/(V*CB0)-k*CA0*(1-XA)*CB0*(1-XB) # Conversion of B
XB(0) = 0
d(T) / d(t) = (Q-Ws+ (-rA*V)*HRx-(FAo*CpA*(T-T0)))/(NA*CpA+NB*CpB) #
T(0) = 308# K, Q= 10# kJ/min, Ws=6 # kJ/min, HRx= 15# kJ/kmol
rA=-k*CA0*(1-XA)*CB0*(1-XB) # kmol/m3. min
CpA= 10# kJ/kmol.K, CpB=12 # kJ/kmol.K, NA=V*CA0*(1-XA) # kmol, NB=V*CB0*(1-XB)# kmol
FAo=0.003 # kmol/min, vo=0.02# m3/min, V=0.2 # m3, k=0.004*exp(-95/R*T) # m3/ kmol.min
R=8.314 # kJ/ kmol.K
t(0)=0 # min
t(f) =48# min
55

## Slide 56: Cont’d
Simulation results:
Conversions of species A and B are increased with reaction time exponentially (Figure 4.9).
56
Figure 4.9. Conversion as a function of reaction time

## Slide 57: 4.4. Summary
Semi-batch reactor a type of chemical reactor that combines features of both batch and continuous reactors.
Semi-batch reactor is operated at unsteady state.
The reactants can be added at different stages of the reaction, which allows for better control over reaction rates and conversion.
Semi-batch reactor is preferred for the following reasons:
  to control highly exothermic reaction,
  to react a gas with a liquid,
  to remove one of the products to increase equilibrium of the reaction, and
  to minimize unwanted side products. i.e. enhance selectivity.
For non-isothermal semi-batch reactor, both materials and energy balance equations should be solved simultaneously using numerical techniques.
57

## Slide 58: References
Chemical Reaction Engineering, Levenspiel, O John Wiely& Sons, 3rd edition, 2011.
Elements of Chemical Engineering, Fogler, HS Prentice- Hall Inc Prentice- Hall Inc, 5th edition, 2015.
58
Thank you!