## Slide 1: Power Plant Engineering
Lecture 12
Miscellaneous Topics
Lecturer: Dr. Melaku Desta

## Slide 2: Lecture learning outcomes:
At the end of this lecture, you will be able to:
Explain the basic principles, sources, and conversion technologies involved in biomass power generation.
Describe the working principles and safety aspects of nuclear power plants and their role in global energy supply.
Analyze the causes and consequences of the greenhouse effect and its impact on climate change.
Identify major types and sources of pollution resulting from energy
production and industrial activities.
Discuss various pollution control methods and sustainable
practices to reduce environmental impacts.

## Slide 3: Content
Biomass Power Generation
Nuclear Power Generation
Greenhouse Effect
Pollution and Its Control
Summary
References

## Slide 4: 1. Biomass Power Generation
Introduction to Biomass Energy
Biomass energy refers to energy derived from organic materials — living or recently living plants, animals, and waste — that can be used as fuel to produce heat, electricity, or biofuels [1].
It is a form of stored solar energy, as plants capture solar energy through photosynthesis, converting carbon dioxide and water into carbohydrates.
When biomass is used for energy, this stored energy is released.
It is considered a renewable source of energy because plants
absorb CO₂ during growth, which offsets the CO₂ released
when the biomass is burned or converted.

## Slide 5: 1. Biomass Power Generation
Biomass provides about 9–14% of the world’s primary energy supply, mostly in developing countries [1].
It supports rural development and waste management while contributing to energy diversification.
Plays a vital role in achieving net-zero carbon emissions and energy security goals.
Biomass is the oldest source of energy for humanity, but its modern application for large-scale power generation is crucial for several reasons [2]:
  Renewability: Biomass can be replenished on a human
  timescale through sustainable management.

## Slide 6: 1. Biomass Power Generation
  Energy Security: It reduces dependence on imported fossil fuels by utilizing domestic resources.
  Waste Management: It offers a productive way to dispose of agricultural, urban, and industrial waste, reducing landfill use and methane emissions from decomposition.
  Baseload Power: Unlike intermittent sources like solar and wind, biomass plants can provide a consistent, dispatchable supply of electricity.

## Slide 7: 1. Biomass Power Generation Cont…
Sources of Biomass
Wood and Agricultural Products
  Virgin wood: Logging residues, wood chips, sawdust from forestry operations.
  Energy crops: Fast-growing trees (e.g., willow, poplar) and grasses (e.g., miscanthus, switchgrass) cultivated specifically for energy production.
  Agricultural residues: Straw, husks, shells, and bagasse (the fibrous residue from crushed sugarcane).
Animal Waste
  Manure from poultry, cattle, and swine operations.
  This is a potent source of methane when processed
  anaerobically.

## Slide 8: 1. Biomass Power Generation Cont…
Municipal and Industrial Waste
  Municipal solid waste: The organic fraction of household garbage (food scraps, yard waste, paper, wood).
  Industrial waste: By-products from food processing, such as nut shells, olive pits, and wastewater sludge.
Biomass Conversion Technologies
There are several technological pathways to convert the
chemical energy in biomass into electricity.
They can be broadly categorized into thermochemical
and biochemical processes.

## Slide 9: 1. Biomass Power Generation Cont…
Thermochemical Conversion (Using Heat)
Direct Combustion
  Biomass is burned directly in a boiler to produce high-pressure steam.
  The heat is used to produce steam, which drives a steam turbine to generate electricity.
  The simplest and most common method.
  Example: Wood-fired steam power plants.
  Key reactions:

## Slide 10: 1. Biomass Power Generation Cont…
Gasification
Converts solid biomass into producer gas (syngas) — a mixture of CO, H₂, CH₄, and CO₂ — by partial oxidation at high temperatures (800–1000°C) with limited air or oxygen.
Syngas can be used in:
  Gas turbines,
  Internal combustion engines, or
  As feedstock for chemical synthesis (methanol, hydrogen).
  Main reactions:

## Slide 11: 1. Biomass Power Generation Cont…
Pyrolysis
Thermal decomposition of biomass in absence of oxygen (400–600°C).
Produces:
  Bio-oil (liquid fuel),
  Syngas, and
  Biochar (solid carbon residue).
Fast pyrolysis produces mainly liquid fuels suitable for upgrading
to transportation fuels.

## Slide 12: 1. Biomass Power Generation Cont…
Biochemical Conversion (Using Microorganisms)
Anaerobic Digestion
Biochemical process using microorganisms to break down organic matter (animal waste, sewage, food waste) in oxygen-free conditions.
Produces biogas (CH₄ + CO₂), which can be used for:
  Electricity generation,
  Heating, or
  Upgraded to biomethane for transport.
The residue (digestate) is a useful biofertilizer.
Ideal for high-moisture content feedstocks like wet waste.

## Slide 13: 1. Biomass Power Generation Cont…
Biomass Power Plant Components and Working Principles
Let's take a direct combustion plant as a representative model.
Feedstock Preparation
Biomass must be collected, transported, and processed to ensure uniform size and moisture content.
Common preparation steps:
  Drying (to reduce moisture < 15–20%),
  Chipping or shredding, and
  Pelletizing for uniform combustion.

## Slide 14: 1. Biomass Power Generation Cont…
Boiler or Reactor
  Combustion boiler: Burns biomass to generate high-pressure steam.
  Gasifier or pyrolyzer: Converts biomass to gas or oil intermediates for combustion or upgrading.
Turbine-Generator System
  Steam from the boiler drives a steam turbine, which rotates a generator to produce electricity.
  In gasification-based systems, syngas may be burned in a
  gas turbine or engine.

## Slide 15: 1. Biomass Power Generation Cont…
Emission Control Systems: Include:
  Cyclones or bag filters – remove particulates.
  Scrubbers – reduce SOx, NOx, and acid gases.
  Electrostatic precipitators – capture fine ash.
Modern plants meet strict environmental standards for air quality.
Condenser and Cooling System:
  After passing through the turbine, the low-pressure steam is condensed back into water in a condenser and pumped back to the boiler to
  begin the cycle again.
Simplified Process Flow:
Feedstock → Combustion/Gasification → Steam/Syngas →
Turbine → Generator → Electricity

## Slide 16: 1. Biomass Power Generation Cont…
Advantages and Limitations of Biomass Energy
Advantages
Renewable and sustainable – Biomass can be continuously replenished through responsible forestry and agriculture.
Carbon neutral – CO₂ released during combustion is balanced by CO₂ absorbed during plant growth.
Waste utilization – Converts agricultural, animal, and municipal wastes into useful energy.
Energy security – Reduces dependence on imported
fossil fuels.
Rural development – Creates local employment and
economic growth.

## Slide 17: 1. Biomass Power Generation Cont…
Limitations
Feedstock logistics – Collection, transportation, and storage can be costly and complex.
Low energy density – Biomass has lower calorific value compared to fossil fuels.
Land-use issues – Large-scale cultivation of energy crops may compete with food production.
Seasonal availability – Biomass feedstock supply may vary by
season.
Air emissions – Though cleaner than coal, biomass
combustion still emits particulates and NOx.

## Slide 18: 1. Biomass Power Generation Cont…
Environmental and Economic Impacts
Environmental Impacts
Lifecycle Emissions
  Biomass emits CO₂ when burned, but if sourced sustainably, net emissions are near zero.
  Unsustainable practices (deforestation, transport, fertilizer use) increase emissions.
Biodiversity and Soil Health
  Energy crop monocultures may affect biodiversity and soil
  nutrients.
Air Pollution
  Particulate matter, CO, and volatile organic compounds
  (VOCs) can be emitted if combustion is inefficient.

## Slide 19: 1. Biomass Power Generation Cont…
Economic Impacts
Capital and Operating Costs
  Higher initial costs than fossil-fuel plants, but lower fuel costs in the long term.
Job Creation
  Provides employment in feedstock supply chains, plant operation, and maintenance.
Energy Pricing
  Can stabilize local energy costs by reducing reliance on
  imported fuels.
Sustainability and Incentives
  Many governments provide feed-in tariffs, carbon credits,
  or tax incentives to encourage biomass use.

## Slide 20: 2. Nuclear Power Generation
Fundamentals of Nuclear Energy and Radioactive Decay
Nuclear energy is the energy released from the nucleus of an atom through nuclear reactions—either fission (splitting of heavy nuclei) or fusion (combining of light nuclei) [3].
In power generation, fission is primarily used.
Basic Atomic Structure:
  Atom: Consists of protons and neutrons (nucleus) and electrons
  orbiting around it.
  Isotopes: Atoms of the same element with different numbers
  of neutrons (e.g., Uranium-235 and Uranium-238).

## Slide 21: 2. Nuclear Power Generation Cont…
Radioactive Decay
Radioactive isotopes spontaneously transform into more stable forms by emitting radiation:
  Alpha decay (α): Emission of helium nuclei (2 protons, 2 neutrons).
  Beta decay (β): Conversion of a neutron into a proton with emission of an electron.
  Gamma decay (γ): Release of high-energy electromagnetic radiation.
Binding Energy
The energy that holds the nucleus together.
According to Einstein’s equation:

## Slide 22: 2. Nuclear Power Generation Cont…
A small loss of mass during nuclear reactions converts to a large amount of energy.
Energy Density:
  1 kg of Uranium-235 releases ≈ 8 × 10¹³ J of energy.
  Equivalent to burning about 3,000 tons of coal.
Nuclear Fission Process and Chain Reaction Control
Nuclear Fission
Nuclear fission is the process of splitting a heavy, unstable
atomic nucleus into two or more lighter nuclei.
This process releases a tremendous amount of energy
because the resulting lighter nuclei have a higher binding
energy per nucleon.

## Slide 23: 2. Nuclear Power Generation Cont…
Chain Reaction
  Each fission event releases neutrons that can cause further fissions.
    Controlled chain reaction → steady energy release (power plant).
    Uncontrolled chain reaction → explosion (atomic bomb).
Control mechanisms for the chain reaction:
Control Rods: Made of neutron-absorbing materials (cadmium, boron, hafnium) to regulate the number of free neutrons.
Moderator: Slows down fast neutrons to thermal energies for
efficient fission (materials: water, heavy water, graphite).
Coolant: Removes heat from the reactor core (water, gas, or
liquid metal).
Reactor Geometry: Maintains optimal neutron flux and reactivity.

## Slide 24: 2. Nuclear Power Generation Cont…
Criticality Conditions
  Subcritical: Chain reaction dies out.
  Critical: Steady-state reaction (desired).
  Supercritical: Exponential growth (unsafe).
Components and Operation of a Nuclear Power Plant
Reactor Core:
  Contains fuel rods (U-235 or Plutonium-239 (Pu-239)).
  Moderator slows down neutrons.
  Control rods adjust reactivity.
Coolant System:
  Circulates coolant to remove heat from the core.
  Transfers heat to a secondary loop to generate steam.

## Slide 25: 2. Nuclear Power Generation Cont…
Steam Generator
  Converts feedwater to steam using reactor heat (in pressurized systems).
Turbine-Generator
  Steam drives the turbine, converting thermal energy to mechanical energy.
  Generator converts mechanical energy into electrical energy.
Condenser
  Cools exhaust steam from the turbine back into water.
Containment Structure
  Reinforced concrete dome enclosing the reactor to prevent
  radiation leakage.
Safety Systems
  Emergency cooling, shutdown systems, and containment
  isolation.

## Slide 26: 2. Nuclear Power Generation Cont…
The operation principle is:
Nuclear fission in the reactor core produces heat → coolant absorbs heat → steam generated → drives turbine → electricity produced → steam condensed and recycled.
The typical efficiency is 30–35% [2].
Types of Nuclear Reactors
Pressurized Water Reactor (PWR)
Uses ordinary (light) water as coolant and moderator.
Water in the reactor is kept under high pressure (≈15 MPa)
to prevent boiling.
Heat is transferred to a secondary loop through a
steam generator.

## Slide 27: 2. Nuclear Power Generation Cont…
Boiling Water Reactor (BWR)
  Water acts as both coolant and moderator.
  Water boils directly in the reactor core, producing steam that drives the turbine.
  Simpler design but with radioactive steam path.
Pressurized Heavy Water Reactor (PHWR)
  Uses heavy water (D₂O) (deuterium, a heavier isotope of hydrogen) as moderator and coolant.
  Can use natural uranium as fuel.
  Allows refueling during operation.

## Slide 28: 2. Nuclear Power Generation Cont…
Gas-Cooled Reactors (AGR, HTGR)
  Uses carbon dioxide or helium as coolant and graphite as moderator.
  Operates at high temperatures for improved efficiency.
Fast Breeder Reactor (FBR)
  No moderator; uses fast neutrons.
  Fuel: plutonium-239 or uranium-238.
  Breeds more fissile material (Pu-239) from U-238.
  Coolant: liquid sodium.
Advanced and Next-Generation Reactors
  Small Modular Reactors (SMRs): Compact, safer, and easier
  to deploy.
  Generation IV Reactors: Focus on safety, sustainability, and
  waste minimization (e.g., molten salt reactors, gas-cooled
  fast reactors).

## Slide 29: 2. Nuclear Power Generation Cont…
Nuclear Waste Management, Safety, and Future Trends
Nuclear Waste Types
  Low-level waste: Lab clothing, tools (short-lived radioactivity).
  Intermediate-level waste: Reactor components, chemical sludge.
  High-level waste: Spent fuel rods and reprocessing waste (highly radioactive, long-lived).
Waste Management Techniques
  Short-term storage: Cooling pools at reactor sites (5–10 years).
  Interim storage: Dry casks in shielded facilities.
  Long-term disposal: Deep geological repositories
  (hundreds of meters underground).
  Reprocessing: Recovery of usable uranium and plutonium
  from spent fuel.

## Slide 30: 2. Nuclear Power Generation Cont…
Safety Systems and Standards
  Defense-in-depth: Multiple layers of protection.
  Emergency Core Cooling System (ECCS): Prevents meltdown.
  Containment Integrity: Prevents radiation leakage.
  International Oversight: IAEA safety standards and inspections.
Accidents and Lessons
  Three Mile Island (1979) (USA) – Partial meltdown, no fatalities.
  Chernobyl (1986) (Ukraine)– Reactor explosion due to design flaws and operator error.
  Fukushima Daiichi (2011) (Japan) – Tsunami-induced power loss
  leading to core meltdowns.
  → Lesson: Redundant safety systems and emergency
  preparedness are critical.

## Slide 31: 3. Greenhouse Effect
The Greenhouse Effect is a natural process where certain gases in the Earth's atmosphere trap heat from the sun, preventing it from escaping back into space, thus keeping our planet warm enough for life to exist [4].
When the Sun’s energy reaches the Earth’s atmosphere, some of it is reflected back to space while the rest is absorbed and re-radiated by greenhouse gases.
This process maintains the Earth’s average temperature at about 15°C, making it suitable for life.
Without it, the average surface temperature would be around
–18°C, too cold for most living organisms.

## Slide 32: 3. Greenhouse Effect Cont…
However, human activities, particularly the burning of fossil fuels and deforestation, have enhanced this effect, leading to global warming and climate change.
Mechanism of the Greenhouse Effect
Incoming Solar Radiation
  The Sun emits shortwave radiation (mainly visible and ultraviolet light). About 30% of this radiation is reflected back by clouds, aerosols, and the Earth’s surface (albedo effect).
Absorption by the Earth’s Surface
  The remaining 70% is absorbed by the land and oceans,
  warming the planet.

## Slide 33: 3. Greenhouse Effect Cont…
Re-radiation of Infrared Energy
  The warmed surface emits longwave infrared radiation back toward space.
Absorption and Re-emission by Greenhouse Gases
  Greenhouse gases (GHGs) absorb part of this outgoing infrared radiation and re-radiate it in all directions — including back toward the Earth’s surface.
The Net-Effect
  This process traps heat in the lower atmosphere, maintaining
  a stable and life-supporting temperature — known as the
  greenhouse effect.

## Slide 34: 3. Greenhouse Effect Cont…
Major Greenhouse Gases and Their Sources
Not all greenhouse gases are created equal.
They differ in their effectiveness at trapping heat (Global Warming Potential - GWP) and their lifetime in the atmosphere.
  CO₂ is the most abundant anthropogenic greenhouse gas and contributes most to global warming.
  Methane has a higher warming potential but shorter atmospheric
  lifetime (~12 years).
  Fluorinated gases are potent but released in small quantities.

## Slide 35: 3. Greenhouse Effect Cont…
Role of Human Activities in Enhancing the Greenhouse Effect
The natural greenhouse effect is life-sustaining.
The problem we face today is the enhanced greenhouse effect, also known as anthropogenic global warming.
Human activities, particularly since the Industrial Revolution, have drastically increased the concentration of GHGs in the atmosphere.
The primary mechanism is the disruption of the global carbon cycle.
The enhanced greenhouse effect refers to the strengthening
of the natural greenhouse effect due to human-induced increases
in greenhouse gases.

## Slide 36: 3. Greenhouse Effect Cont…
Key Human Activities
Burning of Fossil Fuels
  Major source of CO₂ emissions.
  Power generation, transport, industry, and heating contribute heavily.
Deforestation and Land Use Change
  Trees act as carbon sinks; cutting them down reduces CO₂ absorption.
  Burning forests releases stored carbon.
Agricultural Practices
  Rice paddies and ruminant livestock emit large amounts of CH₄.
  Fertilizer use increases N₂O emissions.

## Slide 37: 3. Greenhouse Effect Cont…
Industrial Activities
  Cement production, chemical manufacturing, and refrigeration release CO₂ and fluorinated gases.
Waste Management
  Decomposing organic waste in landfills emits methane.
  Poor waste burning adds CO₂ and black carbon.

## Slide 38: 3. Greenhouse Effect Cont…
Environmental and Climatic Consequences of Global Warming
The enhanced greenhouse effect leads to global warming, which in turn causes major environmental, climatic, and social consequences.
Climatic Consequences
  Increase in global average temperature (~1.2 rise since pre-industrial times).
  Melting of glaciers and polar ice caps → rise in sea levels.
  Changes in precipitation patterns → floods, droughts, and storms.
  Ocean warming and acidification → coral bleaching, marine
  ecosystem disruption.
  Increased frequency of extreme weather events —
  hurricanes, heatwaves, wildfires.

## Slide 39: 3. Greenhouse Effect Cont…
  Environmental and Ecological Effects
    Loss of biodiversity — species migration or extinction due to habitat shifts.
    Desertification — expansion of arid zones and soil degradation.
    Forest dieback — especially in tropical regions.
  Socioeconomic Impacts
    Threats to food security — crop yield reductions.
    Water scarcity — altered hydrological cycles.
    Health problems — heat stress, spread of vector-borne
    diseases.
    Displacement — “climate refugees” from flood-prone or
    drought-hit areas.

## Slide 40: 3. Greenhouse Effect Cont…
  Mitigation and Adaptation Strategies for Reducing Greenhouse Gas Emissions
  Mitigation Strategies
Mitigation aims to reduce or prevent the emission of greenhouse gases and enhance natural sinks.
  Transition to renewable energy
  Energy efficiency
  Carbon capture and storage
  Reforestation and afforestation
  Sustainable agriculture and waste management
  Policy and international agreements

## Slide 41: 3. Greenhouse Effect Cont…
Adaptation Strategies
Adaptation involves adjusting human and natural systems to minimize damage from climate impacts.
Examples:
  Building sea walls and flood defenses in coastal areas.
  Developing drought-resistant crops and improving irrigation.
  Enhancing disaster preparedness and early warning systems.
  Promoting water conservation and efficient resource
  management.
  Urban planning that includes green spaces and heat
  management systems.

## Slide 42: 4. Pollution and Its Control
Pollution is the introduction of harmful substances or energy into the environment, resulting in adverse effects on living organisms and ecosystems [5].
These harmful agents are called pollutants, which may be solids, liquids, gases, noise, heat, or radiation.
Classification of Pollution
Pollution can be classified based on the medium affected:
Air Pollution
  Contamination of the atmosphere by gaseous, liquid, or solid
  wastes that alter its natural composition.
  Major air pollutants: CO, CO₂, SO₂, NOx, hydrocarbons (HC),
  particulate matter (PM₂.₅, PM₁₀), lead, ozone.

## Slide 43: 4. Pollution and Its Control Cont…
Water Pollution
  It is the introduction of harmful substances into rivers, lakes, oceans, or groundwater, degrading water quality.
  Water pollutants include organic waste, chemicals, heavy metals (Mercury (Hg), Lead (Pb), Cadmium (Cd)), oil, fertilizers, pathogens.
Soil Pollution
  It is the degradation of the earth’s surface due to the presence of chemicals or waste materials.
  Soil pollutants includes pesticides, herbicides, heavy metals,
  plastics, industrial waste, solid waste.

## Slide 44: 4. Pollution and Its Control Cont…
Air Pollution Control Methods
Air pollution control involves capturing, removing, or reducing pollutants from emissions before they enter the atmosphere.
Filtration - Mechanical separation of particulate matter from gas streams using porous media.
Scrubbing - Polluted gas comes into contact with a liquid (usually water) that absorbs or neutralizes pollutants.
Electrostatic Precipitation - Uses electric fields to charge
dust particles, which are then attracted to oppositely charged
plates.

## Slide 45: 4. Pollution and Its Control Cont…
Policies, Standards, and Sustainable Pollution Control Strategies
Environmental Policies and Regulations
Example: Global Initiatives such as:
  Paris Agreement (2015): Reduce greenhouse gas emissions.
  Basel Convention (1992): Controls transboundary movement of hazardous waste.
  Montreal Protocol (1989): Controls ozone-depleting substances.
Sustainable Pollution Control Strategies
  Cleaner production: Minimizing waste at the source by
  efficient process design.

## Slide 46: 4. Pollution and Its Control Cont…
  Green technologies: Renewable energy adoption, low-emission fuels.
  Waste minimization and recycling: Circular economy approaches.
  Afforestation and urban green spaces: Natural air purification and noise reduction.
  Public awareness and environmental education: Promoting behavioral change and responsible consumption.

## Slide 47: Summary
Biomass power generation utilizes organic materials like crop residues, wood, and waste to produce renewable energy through combustion, gasification, or anaerobic digestion.
Nuclear power generation generates electricity from controlled nuclear fission reactions within reactors, offering high energy output with low greenhouse gas emissions.
Greenhouse effect describes how greenhouse gases trap heat in the Earth’s atmosphere, influencing global temperatures and driving climate change.
Pollution and its control examines sources and types of pollution (air, water, soil, noise) and their harmful effects on ecosystems and human health.
Integrating clean and efficient energy systems with pollution
control is key to reducing environmental impact and ensuring
long-term ecological balance.

## Slide 48: References
[1]. Biomass Power for the World: Transformations to Effective Use. Wim P. M. van Swaaij, Sascha R. A. Kersten & Wolfgang Palz (eds). Jenny Stanford Publishing, 2015.
[2]. Biomass Production and Efficient Utilization for Energy Generation. N. S. Rathore & N. L. Panwar. CRC Press, 2022.
[3]. A Global Review of PWR Nuclear Power Plants. R. L. Íñiguez‑de Onzoño, J. C. Crespo‑Cárdenas, J. M. Castro‑Ruiz, et al. Applied Sciences (MDPI AG), 2020.
[4]. Ahmed, I. Greenhouse gas emissions reduction for electric power generation: integrating renewable energy with traditional thermal plants. Nature (Scientific Reports), 2022.
[5]. Energy, power, and greenhouse gas emissions for future global electric energy growth scenarios (2020‑2050); L. Battisti; Energy Policy, 2023.

## Slide 49
Thank you !