## Slide 1: Power Plant Engineering
Week 14
Assessments
Final Exam
Lecturer: Dr. Melaku Desta

## Slide 2: This exam contains two parts:
  Multiple Choice Questions (40 Questions_2 marks each)
  Short Answer Questions (4 Questions_ 5 marks each)
  Total marks = 100
  Attempt all questions
  Time allotted: 90 minutes

## Slide 3: Multiple Choice Questions
Which of the following is an example of a raw energy resource?
  A. Electric energy
  B. Solar radiation
  C. Compressed air energy storage
  D. Battery energy
In a direct energy conversion system, energy is converted from one form to another without____.
  A. Using a mechanical intermediary
  B. Requiring any energy source
  C. Generating heat as an intermediate form
  D. Involving electromagnetic fields

## Slide 4: Multiple Choice Questions
Which of the following devices is an example of a direct energy conversion system?
  A. Steam turbine
  B. Gas turbine
  C. Fuel cell
  D. Diesel engine
In indirect energy conversion power plants, the primary energy is first converted into____.
  A. Electrical energy directly
  B. Thermal energy or mechanical energy
  C. Nuclear energy
  D. Gravitational potential energy

## Slide 5: Multiple Choice Questions
Which of the following correctly matches the power plant with its energy conversion type?
  A. Photovoltaic system – Indirect conversion
  B. Steam power plant – Direct conversion
  C. Fuel cell – Indirect conversion
  D. Gas turbine plant – Indirect conversion
The basic power cycle used in steam power plants is the____.
  A. Otto cycle
  B. Brayton cycle
  C. Rankine cycle
  D. Diesel cycle

## Slide 6: Multiple Choice Questions
The main purpose of the reheat cycle in steam power plants is to____.
  A. Increase boiler pressure
  B. Improve thermal efficiency and reduce moisture at turbine exhaust
  C. Decrease condenser pressure
  D. Increase mass flow rate of steam
The regenerative cycle improves thermal efficiency primarily by____.
  A. Superheating steam to a higher temperature
  B. Using part of the turbine steam to preheat the feedwater
  C. Operating at higher condenser pressures
  D. Reducing the number of turbine stages

## Slide 7: Multiple Choice Questions
The reheat–regenerative cycle combines the advantages of____.
  A. Rankine and Otto cycles
  B. Reheat and regenerative cycles
  C. Carnot and Brayton cycles
  D. Open and closed cycle
10. In a binary vapor cycle, two working fluids are used primarily to____.
  A. Increase the compressor work
  B. Utilize low-temperature heat sources more efficiently
  C. Reduce the mass flow rate of steam
  D. Operate the plant at a higher pressure

## Slide 8: Multiple Choice Questions
11. Fuels are broadly classified based on their physical state as____.
  A. Organic and inorganic fuels
  B. Natural and artificial fuels
  C. Solid, liquid, and gaseous fuels
  D. Renewable and non-renewable fuels
The proximate analysis of coal gives information about____.
  A. Carbon, hydrogen, and oxygen content
  B. Moisture, volatile matter, ash, and fixed carbon
  C. Calorific value and sulfur content
  D. Ultimate composition and heating value

## Slide 9: Multiple Choice Questions
13. Combustion stoichiometry deals with____.
  A. Measurement of calorific value of fuels
  B. Estimation of air required for complete combustion
  C. Determination of ash content in coal
  D. Analysis of products of incomplete combustion only
14. The adiabatic flame temperature of a fuel–air mixture depends primarily on____.
  A. The calorific value and excess air used
  B. The moisture content of fuel only
  C. The ambient pressure alone
  D. The rate of combustion only

## Slide 10: Multiple Choice Questions
The bomb calorimeter is used for____.
  A. Determining the ultimate analysis of fuel
  B. Measuring the adiabatic flame temperature
  C. Experimental determination of heating value of a fuel
  D. Estimating air-fuel ratio for combustion
16. Boilers are generally classified according to____.
  A. Fuel used, position of furnace, and method of water circulation
  B. Type of turbine connected
  C. Size of chimney
  D. Efficiency of the condenser

## Slide 11: Multiple Choice Questions
17. In a water-tube boiler____.
  A. Hot gases pass through tubes and water surrounds them
  B. Water flows inside tubes and hot gases flow outside the tubes
  C. Both water and steam are mixed in the same chamber
  D. Combustion takes place inside the tubes
18. Which of the following is a boiler mounting (essential fitting)?
  A. Economizer
  B. Superheater
  C. Safety valve
  D. Air preheater

## Slide 12: Multiple Choice Questions
The boiler efficiency is defined as____.
  A. Ratio of feedwater mass to steam mass
  B. Ratio of heat supplied to the fuel to heat absorbed by steam
  C. Ratio of heat absorbed by steam to heat supplied by fuel
  D. Ratio of power output to fuel input
20. The boiler draught is primarily used to____.
  A. Regulate the flow of water into the boiler
  B. Maintain steam pressure in the boiler drum
  C. Supply required air for combustion and remove flue gases
  D. Measure the amount of fuel burned

## Slide 13: Multiple Choice Questions
21. In fuel-bed combustion, the fuel____.
  A. Is suspended and burned in a stream of air
  B. Burns while resting on a grate with air supplied from below
  C. Is completely mixed with air before ignition
  D. Is atomized before entering the furnace
22. The main purpose of using a mechanical stoker in a boiler is to____.
  A. Atomize liquid fuels for complete combustion
  B. Feed solid fuel automatically and uniformly to the furnace
  C. Supply secondary air to the combustion chamber
  D. Increase the boiler pressure

## Slide 14: Multiple Choice Questions
23. In pulverized coal firing, the coal is____.
  A. Burned in lump form on a grate
  B. Mixed with oil and sprayed into the furnace
  C. Ground into fine particles and blown into the combustion chamber with air
  D. Fed by mechanical stokers onto the fuel bed
24. In an impulse turbine, the steam expands—
  A. In both fixed and moving blades
  B. Only in the moving blades
  C. Only in the nozzle before striking the blades
  D. In the condenser after leaving the blades

## Slide 15: Multiple Choice Questions
25. In a reaction turbine, the pressure drop of steam occurs____.
  A. Only in the nozzle
  B. Only in the moving blades
  C. Partly in the fixed and partly in the moving blades
  D. Only in the condenser
26. The blade or diagram efficiency of an impulse turbine is maximum when the ratio of blade speed to steam velocity (u/V₁) is approximately____.
  A. 0.25
  B. 0.5
  C. 0.75
  D. 1.0

## Slide 16: Multiple Choice Questions
The axial thrust on the rotor of a reaction turbine is primarily due to____.
  A. Change in steam velocity
  B. Pressure difference across the moving blades
  C. Friction losses in bearings
  D. Centrifugal force on rotating blades
28. The governing of a steam turbine is necessary to____.
  A. Maintain constant boiler pressure
  B. Control the speed of the turbine under varying load
  C. Improve the quality of exhaust steam
  D. Reduce friction losses in bearings

## Slide 17: Multiple Choice Questions
29. In a diesel engine, combustion of fuel takes place____.
  A. At constant volume
  B. At constant pressure
  C. At constant temperature
  D. During both compression and expansion
30. The main advantage of an internal combustion engine power plant over a steam power plant is____.
  A. Lower fuel cost
  B. Higher overall efficiency and quicker starting
  C. Lower maintenance requirements
  D. Capability to use low-grade fuels

## Slide 18: Multiple Choice Questions
31. Supercharging in diesel engines is used to____.
  A. Reduce exhaust emissions
  B. Increase the mass of air supplied per cycle to improve power output
  C. Decrease the compression ratio
  D. Cool the engine cylinder
A regenerative gas turbine cycle differs from a simple gas turbine cycle by____.
  A. Using intercooling between compressors
  B. Reheating the air after combustion
  C. Using exhaust gases to preheat the compressed air before combustion
  D. Expanding the gases in multiple turbines

## Slide 19: Multiple Choice Questions
33. In a photovoltaic (PV) power generation system, solar energy is directly converted into____.
  A. Chemical energy
  B. Thermal energy
  C. Electrical energy
  D. Mechanical energy
In hydro-power generation, the primary energy conversion process involves____.
  A. Chemical energy to electrical energy
  B. Mechanical energy of falling water to electrical energy
  C. Thermal energy to mechanical energy
  D. Potential energy to chemical energy

## Slide 20: Multiple Choice Questions
The main source of energy in geothermal power generation is____.
  A. Solar radiation
  B. Heat from nuclear fission reactions
  C. Heat from within the Earth’s crust
  D. Ocean tidal energy
The power output of a wind turbine depends most strongly on____.
  A. Wind speed
  B. Air temperature
  C. Tower height only
  D. Rotor color and material

## Slide 21: Multiple Choice Questions
In biomass power generation, the main source of energy is____.
  A. Mechanical energy from tides
  B. Chemical energy stored in organic matter
  C. Solar radiation directly
  D. Nuclear decay of plant materials
The greenhouse effect in power generation refers to____.
  A. The heating of plant buildings by solar collectors
  B. The trapping of heat in the atmosphere due to gases like CO₂ and CH₄
  C. The rise in boiler temperature due to improper insulation
  D. A method of reducing thermal pollution in lakes

## Slide 22: Multiple Choice Questions
The primary purpose of applying engineering economy principles in power plant projects is to—
  A. Increase the thermal efficiency of the plant
  B. Evaluate the economic feasibility and optimize resource allocation
  C. Improve environmental compliance
  D. Reduce the size of the plant
Which of the following is a key financial indicator used to assess the performance of a power plant?
  A. Adiabatic flame temperature
  B. Net Present Value (NPV)
  C. Steam turbine blade efficiency
  D. Boiler draught

## Slide 23: Short Answer Questions
Compare and contrast the environmental impacts of renewable and non-renewable power generation systems. How can modern power plants minimize greenhouse gas emissions and pollution while maintaining high efficiency?__________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________.
Explain how the efficiency and sustainability of power generation can be improved through advanced cycle modifications and hybrid systems (e.g., combined cycle plants, reheat-regenerative steam cycles, or solar-assisted thermal systems).____________________________________________________________________________________________________________________________________________________________________________________________________________________.

## Slide 24: Short Answer Questions
Explain the principles of engineering economy and their application in evaluating the economic feasibility of power plants. How do these principles help in decision-making for power generation projects?”_________________________________________________________________________________________________________________________________________________________________________________________________________________________________.
Discuss the key financial indicators used to assess the performance of power plants. How can these indicators be used to optimize the economics of power generation?”________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________.

## Slide 25
Thank you !