## Slide 1
Basic Principles of Process Calculations in Chemical Engineering (ChEg2106)
Prerequisites: No prerequisite for this course
Lecture 4: Material Balances without Chemical Reaction
Week 4
Lecturer: Adamu Esubalew (PhD, ChEg)
Addis Ababa, Ethiopia
1

## Slide 2: Lecture learning outcomes
At the end of the lecture, you will be able to:
identify the purposes of material balances in processes design
describe problem-solving techniques for material balances calculations, and
determine material balances without chemical reaction for steady state processes.
2

## Slide 3: Presentation outlines
Introduction to material balances
Problem-solving techniques for material balances without chemical reaction
Material balances without chemical reaction
Summary
3

## Slide 4: 4.1. Introduction to material balances
Material balances refer to determination of the quantity of materials present/flows in any physical and chemical processes.
Mass conservation law is used to determine quantity of material flows.
Conservation law states that mass is neither created nor destroyed.
The mass of any isolated system is constant.
Material balances are the prerequisite to solve both simple and complex chemical engineering problems.
4

## Slide 5: Cont’d
To perform material balance calculations, it is required to consider the key terms, such as system, system boundary, open system, closed system, isolated system, steady state and unsteady state.
System: It is an arbitrary portion or whole of a process considered for analysis.
System boundary: It is circumscribed the process itself to give attention the system to be isolated in each problem you work.
Open system: It is a system in which there are both material and energy transfer across system boundary.
5

## Slide 6: Cont’d
Closed system: It is a system in which is no material transfer across system boundary. But energy can transfer in the form of heat and work done across system boundary.
Isolated system: It is a system in which there is no both material and energy transfer across system boundary.
Unsteady state process: The value of process variables in the system changes with time.
Steady state process: The value of process variables in the system does not change with time.
6

## Slide 7: Cont’d
The use of material balances in a process allows you to calculate the values of the flows of species in the streams that enter and leave the plant equipment.
You may want to find out how much of each raw material is used and how much of each product (along with some wastes) is produced by the plant.
For process industries, material balances assist planning for process design, economic evaluation of proposed and existing process, process control and process optimization (Coulson & Richardson’s, 1999, pg. 35-57).
7

## Slide 8: 4.2. Problem-solving techniques for MBs without chem. rxn.
Material balances calculations require understanding of key problem-solving techniques.
Some of the key problem-solving techniques for material balances are the followings (Himmelblau, 2023, pg. 129-136):
Read the problem carefully and understand it,
Draw the process system diagram with system boundaries,
Write all given values and required unknowns on the diagram,
Determine the number of unknown variables and the number of independent equations to check that numbers of degree of freedom (NDF) is zero,
8

## Slide 9: Cont’d
Collect additional data, if needed,
Check all units are consistent by converting all units to the same consistent units,
State all your assumptions to the problem,
Identify and write the appropriate material balances equation,
Define all the symbols used in the material balances equation,
Solve the problem using appropriate equation, and
Analyze your final result and write your conclusion based on the results.
9

## Slide 10: 4.3. Material balances without chemical reaction
Material balances equation: It is an equation which is used to determine the quantity of materials transfer across system boundary, accumulation within the system, generation/ consumption in the system (Richard M. Felder, 2005, pg. 85).
The general material balances flow through a system is shown in Figure 4.1.
The dashed line denotes system boundary in which material balances can be written.
10
Figure 4.1. General material balances

## Slide 11: Cont’d
The general material balances equation is given by:
Rate of accumulation = rate of inputs - rate of outputs
± rate of generation/ consumption (4.1)
If a material balance is done with respect to total mass, the rate of generation/ consumption terms will be zero.
If a material balance is done with respect to elements, the rate of generation/consumption terms will be zero.
11

## Slide 12: Cont’d
If a material balance is done with respect to total moles without chemical reaction, the rate of generation/ and consumption terms will be zero.
If the rate of generation/ consumption is zero, the material balances equation (4.1) can be reduced to equation (4.2).
Rate of accumulation = rate of inputs - rate of outputs (4.2)
Material balances without chemical reaction can be a single system or multiple subsystems.
12

## Slide 13: Cont’d
4.3.1. Material balances without chemical reaction for a single system
Material balances without chemical reaction refers to the materials balances of physical processes, such as mixing, distillation, physical absorption, physical adsorption, evaporation and drying.
If there is no chemical reaction, the rate of generation/consumption term will be zero, and equation (4.2) will be used to determine the material balances for a single system.
If a process is steady state, then the rate of accumulation will be zero, and equation (4.2) will be reduced to equation (4.3).
Rate of inputs = Rate of outputs (4.3)
13

## Slide 14: Cont’d
Consider the following single system of material balances without chemical reaction, as depicted in Figure 4.2.
It is assumed that the system has three input streams and one output stream.
The feed streams may have many components (chemical compounds).
14
Process
R
Xir
F1
Xi1
F2
Xi2
F3
Xi3
Figure 4.2. Material balances without chemical reaction for a single system

## Slide 15: Cont’d
To determine material balances for Figure 4.2, it is assumed that the process is steady state.
The overall material balances and component balances are performed using equation (4.3).
Overall materials balance:
Rate of inputs = Rate of outputs
(4.4)
Where: F1, F2 and F3 are feed rates of streams 1, 2 and 3, respectively; and R is rate of output stream.
15

## Slide 16: Cont’d
(ii) Components materials balances:
Rate of inputs = Rate of outputs
(4.5)
Where: Xi1, Xi2 and Xi3 mass/mole fractions of species i in the feed streams 1, 2 and 3, respectively; and Xir is mass/mole fraction of species i in the output stream.
To solve equation (4.4) and equation (4.5), the number of unknowns and the number of independent equations should be equal, the numbers of degree of freedom should be zero.
16

## Slide 17: Activity 4.1
1. A liquid adhesive, which is used to make laminated boards, consists of a polymer dissolved in a solvent. The amount of polymer in the solution has to be carefully controlled for this application. An adhesive dealer receives an order for 8, 000 kg of adhesive solution containing 20% polymer by weight. An adhesive dealer has stocks of: (i) 2000 kg of 10% polymer solution, (ii) very large quantities of 40% polymer solution, and (iii) a pure solvent. Determine the mass of each of the stocks that must be blended together to fulfill the order.
17

## Slide 18: Cont’d
2. A solution composed of 50% ethanol (EtOH), 10% methanol (MeOH), and 40% water (H2O) is fed into a separator at the rate of 100 kg/hr that produces one stream at the rate of 60 kg/hr with the composition of 80% EtOH, 15% MeOH, and 5% H2O, and a second output stream of unknown composition and flow rate. Calculate the mass fractions of the three compounds in the second output stream and its flow rate in kg/hr. (Compositions are given in mass fraction).
18

## Slide 19: Cont’d
3. For crystallization operation, 5,000 kg of aqueous solution of sodium sulfate with concentration 30% is fed to a crystallizer. The solution is cooled to crystallize out sodium sulfate with a concentration of 75%, and the remaining solution (the mother liquor) is separated with concentration of 10% sodium sulfate. Calculate the mass of the final crystal sodium sulfate and mother liquor. (Compositions are given in mass fraction).
19

## Slide 20: Cont’d
# Q1, Answer:
Given : Three feed steams, and one output stream.
Feed 1 = 2, 000 kg with 10% polymer; Feed 2 = unknown quantity with 40 % polymer
Feed 3 = unknown quantity with a pure solvent; product = 8, 000 kg with 20 % polymer.
All fractions are in mass basis
Required: The mass of feed streams in 2 & 3.
Assumption: Mixing process is carried out at steady state condition.
20

## Slide 21: Cont’d
The mixing process flow diagram is depicted in Figure 4.3.
21
Figure 4.3. Mixing process flow for Activity 4.1 #Q1
Mixing process
R = 8, 000 kg
Xpr= 0.2
Xsr= 0.8
M1= 2,000 kg
Xp1= 0.1
Xs1= 0.9
M2= ?
Xp2= 0.4
Xs2= 0.6
M3=?
Xp3= 0
Xs3= 1

## Slide 22: Cont’d
Overall material balances:
The overall material balances is given by:
(4.6)
But M1= 2,000 kg, and R= 8, 000 kg
By substituting the values of M1 = 2, 000 kg, and R = 8, 000 kg into equation (4.6), we get:
(4.7)
Where: M1, M2, and M3 are mass of input stocks in streams 1, 2 and 3, respectively; and R is the mass of the output stream.
22

## Slide 23: Cont’d
(ii) Components material balances:
The components material balance is given by:
(4.8)
Where: Xi1, Xi2 and Xi3 are mass fractions of species i in the feed streams 1, 2 and 3, respectively; and Xir is mass fraction of species i in the output stream.
Component balance on polymer is given by:
(4.9)
23

## Slide 24: Cont’d
Where: Xp1, Xp2 and Xp3 are mass fractions of polymer in the feed streams 1, 2 and 3, respectively; and Xpr is mass fraction of polymer in the output stream.
Component balance on solvent is given by:
(4.10)
Where: Xs1, Xs2 and Xs3 are mass fractions of solvent in the feed streams 1, 2 and 3, respectively; and Xsr is mass fraction of solvent in the output stream.
24

## Slide 25: Cont’d
Since polymer is present only in the two streams of the feed stock, you can do component balance on polymer using equation (4.9).
25

## Slide 26: Cont’d
Now, you can calculate the mass in the feed stream 3 (M3), using equation (4.7)
The value of M2 is 3, 500 kg
By substituting the value of M2 = 3, 500 kg into equation (4.7), you can get the value of M3.
2, 500 kg
Therefore, the stocks of the feed streams should be 2, 000 kg, 3, 500 kg and 2, 500 kg for stream 1, 2 and 3, respectively.
26

## Slide 27: Cont’d
# Q2, Answer:
Given: Separation of ethanol, methanol and water mixtures
One input stream with total feed rate = 100 kg/ hr, and two output streams.
Mass fractions in the feed 0.5, 0.1 and 0.4, for EtOH, MeOH and H2O, respectively.
Top side flow rate is 60 kg/hr with 0.8, 0.15 and 0.05 for EtOH, MeOH and H2O.
Required: Bottom side output flow rate and the mass fractions of EtOH, MeOH and H2O
Assumption: Separation is carried out at steady state condition.
27

## Slide 28: Cont’d
The separation process flow diagram is shown in Figure 4.4.
28
Figure 4.4. Separation process flow diagram for Activity 4.1 #Q2
Separation
P = 60 kg/hr
Xpe = 0.8
Xpm = 0.15
Xpw = 0.05
F = 100 kg/hr
Xfe = 0.5
Xfm = 0.1
Xfw = 0.4
B = ?
XBe = ?
XBm = ?
XBw = ?

## Slide 29: Cont’d
To determine the four unknowns, you need four independent equations.
One independent equation is the overall material balance, and three independent equations are component material balances with respect to EtOH, MeOH and H2O.
Overall material balances:
The overall material balance is given by:
(4.11)
Where: F is mass flow rate of the input, P is mass flow rate of top side output stream, and B is mass flow rate of bottom side output stream.
29

## Slide 30: Cont’d
(ii) Components material balances:
Component material balance for ethanol is given by:
(4.12)
Component material balance for methanol is expressed by:
(4.13)
Component material balance for water is described by:
(4.14)
30

## Slide 31: Cont’d
Where: XFe, XFm & XFw are feed stream mass fractions of EtOH, MeOH and H2O, respectively; XPe, XPm & XPw are top side output stream mass fractions of EtOH, MeOH and H2O, respectively; and XBe, XBm & XBw are bottom side output stream mass fractions of EtOH, MeOH and H2O, respectively.
Using equation (4.11), the overall material balance is given by:
By substituting the values of F = 100 kg/ hr, and P = 60 kg/hr into equation (4.11), you get:
kg/hr
31

## Slide 32: Cont’d
To determine the mass fraction of ethanol in the bottom side output stream (XBe), you can use component balance of ethanol, equation (4.12):
Substitute the values of F = 100 kg/hr, P = 60 kg/hr, B = 40 kg/hr, XFe = 0.5 and XPe = 0.8
32

## Slide 33: Cont’d
To calculate the mass fraction of methanol in the bottom side output stream (XBm), use component balance of methanol, equation (4.13):
Substitute the values of F = 100 kg/hr, P = 60 kg/hr, B = 40 kg/hr, XFm = 0.1 and XPm = 0.15
33

## Slide 34: Cont’d
To calculate the mass fraction of water in the bottom side output stream (XBw), you can use component material balances of methanol, equation (4.14):
Substitute the values of F = 100 kg/hr, P = 60 kg/hr, B = 40 kg/hr, XFw = 0.4 and XPw = 0.05
34

## Slide 35: Cont’d
# Q3, Answer:
Given: Crystallization operation, and one stream feed with total quantity of 5, 000 kg, and two output streams (mother liquor and final crystal)
Mass fraction of sodium sulfate in the feed is 0.3.
Mass fractions of the final crystal and mother liquor are 0.75 and 0.10, respectively.
Required : Calculate the mass of final crystal and the mother liquor.
35

## Slide 36: Cont’d
Assumption: The crystallization operation is done at steady state condition; and water is a solvent with sodium sulfate solution
The crystallization process flow diagram is shown in Figure 4.5.
36
Figure 4.5. Crystallization process flow diagram Activity 4.1 #Q3
Crystallizer
M = ?
Xms = 0.10
Xmw = 0.90
R = ?
Xrs = 0.75
Xrw = 0.25
F = 5, 000 kg
XFs = 0.30
XFw = 0.70

## Slide 37: Cont’d
To calculate the two unknowns, you require two independent equations.
One independent equation is the overall material balances, and another one independent equation is the components material balances with respect to sodium sulfate or H2O.
The overall material balance is given by:
(4.15)
Where: F is mass of the input (feed) stream, M is mass of mother liquor (top side) output stream, and R is mass of final crystal of sodium sulfate (bottom side output) stream.
37

## Slide 38: Cont’d
Component balance for sodium sulfate is given by:
(4.16)
Where: XFs is mass fraction of sodium sulfate in the input (feed) stream, Xms is mass fraction of sodium sulfate in the mother liquor (top side) output stream, and Xrs is mass fraction of sodium sulfate in the final crystal of sodium sulfate (bottom side output) stream.
38

## Slide 39: Cont’d
By substituting the values of F = 5, 000 kg into equation (4.15), you get:
(4.17)
By substituting the values of F= 5, 000 kg, XFs= 0.30, Xms= 0.10, and Xrs= 0.75 in equation (4.16), you can get:
(4.18)
By substituting equation (4.17) into equation (4.18), you get:
39

## Slide 40: Cont’d
The mass of the final crystal sodium sulfate is calculated using equation (4.17).
The value of M is 3, 461.5 kg
Therefore, the mass of final crystal sodium sulfate and mother liquor are 1, 538.5 kg and 3, 461.5 kg, respectively.
40

## Slide 41: Cont’d
4.3.2. Material balances without chemical reaction for multiple subsystems
Physical operations can be carried out using multiple subsystems.
Material balances for multiple subsystems refers to a system has two or more subunits to be considered for material balances calculation (Richard M. Felder, 2005, pg. 104).
In real application unit operations and unit processes, multiple subsystems are interconnected.
To determine the material balances, you can apply the same techniques discussed so far for a single system.
41

## Slide 42: Cont’d
For multiple subsystems material balance:
consider the whole process flow sheet as a single unit, and
divide the flowsheet into subsystems to analyze one unit at a time.
If more than one piece of equipment or junction point is involved in the problem, you can write material balances for each piece of equipment and a balance around the whole process.
However, not all the balances you might write will be independent since the overall balance is nothing more than the sum of the balances about each piece of equipment.
42

## Slide 43: Cont’d
Consider the flow sheet of multiple subsystems which comprise of many interconnected equipment as shown in Figure 4.6.
43
Unit I
Unit II
Unit III
F
XFi
B
XBi
D
XDi
P
Xpi
R
Xri
S
Xsi
G
XGi
H
XHi
Figure 4.6 Process flow sheet of multiple subsystems

## Slide 44: Cont’d
Let’s draw a boundary line around the multiple subsystems to determine the overall materials balances and components balances as shown in Figure 4.7.
44
Unit I
Unit II
Unit III
F
XFi
B
XBi
D
XDi
P
Xpi
R
Xri
S
Xsi
G
XGi
H
XHi
Figure 4.7 Process flow sheet of multiple subsystems with system boundary

## Slide 45: Cont’d
From Figure 4.7, the overall material balance is given by:
(4.19)
Where: F is the quantity of material in the input for unit I; P, R and S are the quantity of material outputs in the top sides for unit I, II & III, respectively; and B and D are the quantity of material outputs in the bottom sides for unit II & III, respectively.
45

## Slide 46: Cont’d
The components material balance is expressed by:
(4.20)
Where: XFi is mass fraction of species i in the input of unit I; Xpi, Xri and Xsi are mass fractions of species i in the top sides of unit I, II & III, respectively; and XBi and XDi are mass fractions of species i in the bottom sides of unit II & III, respectively.
46

## Slide 47: Cont’d
To determine the material balances between each interconnected process equipment, let’s subdivide the process flow of Figure 4.7 into three subunits (I, II & III).
Figure 4.8 depicts the process flow diagram of unit I.
47
Unit I
F
XFi
P
Xpi
G
XGi
Figure 4.8 Process flow diagram of unit I

## Slide 48: Cont’d
Materials balance on unit I:
Overall materials balance is given by:
(4.21)
Where: F is quantity of input, and P & G are quantity of outputs.
The components material balance is expressed by:
(4.22)
Where: XFi is fraction of species i in the input, Xpi and XGi are fractions of species in the P and G output streams.
48

## Slide 49: Cont’d
Figure 4.9 shows the process flow diagram of unit II.
49
Unit II
B
XBi
R
Xri
G
XGi
H
XHi
Figure 4.9 Process flow diagram of unit II

## Slide 50: Cont’d
Materials balance on unit II:
Overall material balance is given by:
(4.23)
Where: G is quantity of input, and B, H & R are quantity of outputs.
The components balance is expressed by:
(4.24)
Where: XGi is fraction of species i in the input, XBi XHi, and Xri are fractions of species in the B, H and R output streams, respectively.
50

## Slide 51: Cont’d
For unit III, the process flow diagram is depicted in Figure 4.10.
51
Unit III
D
XDi
S
Xsi
H
XHi
Figure 4.10 Process flow diagram of unit III

## Slide 52: Cont’d
Materials balance on unit III:
Overall materials balances is written as:
(4.25)
Where: H is quantity of input, and D & S are quantity of outputs.
The component material balances is given by:
(4.26)
Where: XHi is fraction of species i in the input, and XDi & Xsi are fractions of species in the D and S output streams, respectively.
52

## Slide 53: Activity 4.2
1. In a petroleum refining industry, a distillation column separates 20,000 kg/hr. of a 50wt% benzene and 50wt% toluene mixture. The top product (D) recovered from the condenser at the top of the column contains 95wt% benzene and the bottom product (W) at the column contains 96wt% toluene. The vapor stream (V) enters to the condenser from the top of the column with a mass flow rate of 11,730 kg/hr. A portion of the product from the condenser is returned to the column as a reflux and the rest is withdrawn D. Determine: (a) the mass flow rates of D and W, (b) the mass flow rate of recycled reflux (R), and (c) the ratio of R to D.
53

## Slide 54: Cont’d
Answer:
Given: distillation column to separate benzene and toluene mixture.
Feed stream: F= 20, 000 kg/hr., XFB= 0.5, XFT= 0.5
Top product stream: D= ?, XDB= 0.95, XDT= 0.05; Vapor stream: V= 11,730 kg/hr.
Bottom product: B=?, XWB= 0.04, XWT= 0.96
Required: (a) D= ?, W=?, (b) R=? and (c) R/D =?
Assumption: The separation process is steady state.
.
54

## Slide 55: Cont’d
The process flow diagram with system boundary is shown in Figure 4.11.
55
Figure 4.11 Process flow diagram for Activity 4.2
Distillation column
F= 20, 000 kg/hr.
XFB = 0.5
XFT = 0.5
W= ?
XWB = 0.04
XWT = 0.96
Condenser
D = ?
XDB = 0.95
XDT = 0.05
V=11, 730 kg/hr.
R = ?

## Slide 56: Cont’d
(a) The flow rate of top product (D) & bottom product (W):
From Figure 4.11, the overall material balances can be determined using equation (4.27):
; F = 20, 000 kg/hr.
(4.27)
Where: F is mass flow rate of feed as input, D is mass flow rate of top product as output, and W is mass flow rate of bottom product as output.
In equation (4.27), there are two unknowns with one independent equation.
Now, you can find one independent equation from components material balance.
56

## Slide 57: Cont’d
You can do components balance on benzene or toluene.
Let’s do component balance on benzene.
(4.28)
Where: XFB is mass fraction of benzene in the input (feed), XDB is mass fraction of benzene in the top product, and XWB is mass fraction of benzene bottom product.
57

## Slide 58: Cont’d
By substituting the values of XFB= 0.5, XDB= 0.95 and XWB= 0.04 into equation (4.28), you can get:
(4.29)
To find the value of W, substitute equation (4.27) into equation (4.29).
kg/hr.
From equation(4.27), D = F-W = 20, 000-9,890 = 10, 110 kg/hr.
58

## Slide 59: Cont’d
(b) To calculate the amount of reflux rate (R), divide the process into two subunits, and consider the condenser part as shown in Figure 4.12.
Overall balance on condenser is given by: kg/hr.
(c) The reflux ratio over top product (R/D) = 1, 620/10,110 = 0.16
59
Condenser
D = 10, 110 kg/hr.
XDB = 0.95
XDT = 0.05
V=11, 730 kg/hr.
R = ?
Figure 4.12 Process flow diagram of condenser for Activity 4.2

## Slide 60: 4.4. Summary
Material balances without chemical reaction refers to physical process calculations of material inputs and outputs at steady state condition.
For process industries, material balances assist planning for process design, economic evaluation of proposed and existing process, process control and process optimization.
To determine material balances, the number of unknowns and number of independent equations must be equal, the numbers of degree of freedom must be zero.
The material balances calculation is performed using overall material balance and components balance.
60

## Slide 61: References
Basic Principles and Calculations in Chemical Engineering, Himmelblau, Pearson Education Inc, 9th edition, 2023.
Chemical Engineering Design, Volume 6, Coulson & Richardson’s, R. K. Sinnott, 3rd edition, 1999.
Elementary Principles of Chemical Processes, Richard M. Felder, John Wiley & Sons, 3rd edition, 2005.
61
Thank you!