## Slide 1
Basic Principles of Process Calculations in Chemical Engineering (ChEg2106)
Prerequisites: No prerequisite for this course
Lecture 12: Integrated Material and Energy Balances for Multiple Systems
Week 12
Lecturer: Adamu Esubalew (PhD, ChEg)
Addis Ababa, Ethiopia
1

## Slide 2: Lecture learning outcomes
At the end of the lecture, you will be able to:
identify the characteristics of multiple systems,
develop integrated material and energy balances equations for multiple systems without chemical reactions and with chemical reactions, and
determine material and energy balances for multiple systems without chemical reactions and with chemical reactions.
2

## Slide 3: Presentation outlines
Introduction to integrated material and energy balances for multiple systems
Integrated material and energy balances for multiple systems without chemical reactions
Integrated material and energy balances for multiple systems with chemical reactions
Summary
3

## Slide 4: 12.1. Introduction to IMEBs for multiple systems
Integrated material and energy balances (IMEBs) for multiple systems involve a comprehensive approach to analyze the flow of materials and energy within interconnected processes.
Integrated material and energy balances for multiple systems consider multiple systems as a whole rather than in isolation, allowing for a better understanding of interactions and dependencies of interconnections to account the exchange of materials and energy between different systems (Himmelblau, 2023, pg. 265-272).
The multiple systems can be interconnections of reactors, separators, and heat exchangers, which require integrated material and energy balances determination.
4

## Slide 5: Cont’d
Multiple systems have their own characteristics to be considered to determine integrated material and energy balances.
Some of the key characteristics multiple systems are:
Require holistic approach: Integrated material and energy balances for multiple systems follows holistic approach by considering multiple systems as a whole rather than in isolation.
Need to account multiple components: Interagted material and energy balances must consider multiple chemical species or components, each with its own properties and behaviors, and the heat of reactions associated with chemical reactions.
5

## Slide 6: Cont’d
Need software tools: Integrated material and energy balances are commonly complex to perform calculations manually, which requires relevant software tools to simulate the balances for complex calculations.
Data requirement: The inputs are required accurate data on flow rates, compositions, energy requirements, and operational conditions, which are essential for reliable integrated material and energy balances.
In this lecture, integrated material and energy balances for multiple systems without chemical reactions and with chemical reactions are discussed.
6

## Slide 7: 12.2 IMEBs for multiple systems without chemical reactions
To determine integrated material and energy balances without chemical reactions for multiple systems, consider the following multiple systems as shown in Figure 12.1(Coulson & Richardson’s, 1999, pg. 62).
7
Figure 12.1 Integrated material and energy balances for multiple systems
System I
System II
System III
v3
H3
v0
H0
v1
H1
v2
H2
h0
h3

## Slide 8: Cont’d
Where: the subscript “0” is the input for system I, II & III, and the subscripts “1, 2 & 3” are input and outputs of system I, II and III, respectively; and , , , , v and h are the rates of enthalpy, the heat addition, work done by the system, mass flow rate, velocity of fluid, and elevation of streams, respectively.
To determine integrated material and energy balances for multiple systems, you can consider the whole systems as a single system; and divide the multiple systems into three single systems.
8

## Slide 9: Cont’d
(A) Consider multiple systems as a single system:
Material balance equation: By considering the whole process as a single system, the material balances equation is given by:
(12.1)
Where: and are mass flow rates enter to system I, , and are mass flow rates enter to system II and system III, respectively, and is mass flow rate leaves from system III.
9

## Slide 10: Cont’d
Energy balance equation: Similarly, by considering the whole systems as single system, the energy balances equation is given by:
(12.2)
Where: is the rate of change in enthalpy, is the rate of change in kinetic energy, is the rate of potential energy, , and are the rates of heat added to system I, system II and system III, and , and are the rates of work done by system I, system II and system III, respectively (Richard M. Felder, 2005, pg. 322-324).
10

## Slide 11: Cont’d
(B) Dividing multiple systems into three single systems: The integrated material and energy balance equations for each system can be determined sequentially as follows:
System I: The integrated material and energy balances is depicted in Figure 12.2.
11
Figure 12.2 Integrated material and energy balances for system I
System I
v0
H0
v1
H1
h0
h1
v01
H01
h01

## Slide 12: Cont’d
Material balances equation: The material balances equation for system I is expressed by:
(12.3)
Where: and are mass flow rates in the input streams , and is mass flow rate in the output stream for system I.
Energy balances equation: The energy balances equation for system I is given by:
(12.4)
12

## Slide 13: Cont’d
Where: is the rate of change in enthalpy, is the rate of change in kinetic energy, is the rate of change in potential energy, is the rate of heat addition, and is the rate of work done by the system for system I.
The rate of change in enthalpy can be written as:
(12.5)
Where: is the rate of change in enthalpy, and are mass flow rate and specific enthalpy of the output stream, respectively, and , , and are mass flow rates and specific enthalpies in the input streams, respectively, for system I.
13

## Slide 14: Cont’d
The rate of change in kinetic energy can be written as:
] (12.6)
The rate of change in potential energy is also given by:
] (12.7)
Where: is the rate of change in kinetic energy, is the rate of change in potential energy, , and are mass flow rate, elevation and velocity of the output stream, respectively, and , , , and are mass flow rates, elevations and velocities in the input streams, respectively, for system I.
14

## Slide 15: Cont’d
System II: The integrated material and energy balances is shown in Figure 12.3.
15
Figure 12.3 Integrated material and energy balances for system II
System II
v1
H1
v2
H2
h1
h2
vo2
Ho2
h02

## Slide 16: Cont’d
Material balances equation: The material balances equation for system II is given by:
(12.8)
Where: and are mass flow rates in the input streams , and is mass flow rate in the output stream for system II.
Energy balances equation: The energy balances equation for system II is expressed by:
(12.9)
16

## Slide 17: Cont’d
Where: is the rate of change in enthalpy, is the rate of change in kinetic energy, is the rate of change in potential energy, is the rate of heat addition, and is the rate of work done by the system for system II.
The rate of change in enthalpy for system II can be written as:
(12.10)
Where: is the rate of change in enthalpy, and are mass flow rate and specific enthalpy of the output stream, respectively, and , , and are mass flow rates and specific enthalpies in the input stream, respectively, for system II.
17

## Slide 18: Cont’d
The rate of change in kinetic energy can be written as:
] (12.11)
The rate of change in potential energy can be written as:
] (12.12)
Where: is the rate of change in kinetic energy, is the rate of change in potential energy, , and are mass flow rate, elevation and velocity of the output stream, respectively, and , , , and are mass flow rates, elevations and velocities in the input streams, respectively, for system II.
18

## Slide 19: Cont’d
System III: The integrated material and energy balances is shown in Figure 12.4.
19
Figure 12.4 Integrated material and energy balances for system III
System III
v2
H2
v3
H3
h2
h3
vo3
Ho3
h03

## Slide 20: Cont’d
Material balances equation: The material balances equation for system III is given by:
(12.13)
Where: and are mass flow rates in the input streams , and is mass flow rate in the output stream for system III.
Energy balances equation: The energy balances equation for system III is expressed by:
(12.14)
20

## Slide 21: Cont’d
Where: is the rate of change in enthalpy, is the rate of change in kinetic energy, is the rate of change in potential energy, is the rate of heat addition, and is the rate of work done by the system for system III.
The rate of change in enthalpy for system III can be written as:
(12.15)
Where: is the rate of change in enthalpy, and are mass flow rate and specific enthalpy of the output stream, respectively, and , , and are mass flow rates and specific enthalpies in the input stream, respectively, for system III.
21

## Slide 22: Cont’d
The rate of change in kinetic energy for system III can be expressed by:
] (12.16)
The rate of change in potential energy for system III can be written as:
] (12.17)
Where: is the rate of change in kinetic energy, is the rate of change in potential energy, , and are mass flow rate, elevation and velocity of the output stream, respectively, and , , , , and are mass flow rates, elevations and velocities in the input streams, respectively, for system III.
22

## Slide 23: Activity 12.1
1. Water is supplied into multiple systems at temperature of 45oC with a mass flow rate of 700kg/s. In the process, 15% and 30% of the feed mass flow rate is discharged from system I and system II outlet streams, respectively, as shown in Figure 12.5. The supply energy rates into system I, II and III are 10,000kJ/s, 12,000kJ/s and 14, 000kJ/s, respectively. Assume that the specific heat capacity of water is 4.2kJ/kg.oC which is constant for all temperatures, and the reference temperature is 25oC. Determine: (a) the mass flow rates of each stream of system I, II & III, (b) the outlet temperatures from system I, II & III, and (c) the rate of overall change in enthalpy of multiple systems.
23

## Slide 24: Cont’d
The process flows sheet of Activity 12.1 is depicted in Figure 12.5.
24
H2II
T2II
H1
T1
System I
System II
System III
kg/s
H0
T0= 45oC
H2
T2
= 12, 000 kJ/s
H1I
T1I
H3
T3
Figure 12.5 Integrated material and energy balances for multiple systems

## Slide 25: Cont’d
Where: , Ho and To are mass flow rate, specific enthalpy and temperature of feed to system I, respectively; , , and are rates of heat addition to system I, II & III; , H1I and T1I are mass flow rate, specific enthalpy and temperature of water leaves from system I; , H1 and T1 are mass flow rate, specific enthalpy and temperature water of leaves from system I; , H2II and T2II are mass flow rate, specific enthalpy and temperature of water leaves from system II; , H2 and T2 are mass flow rate, specific enthalpy and temperature of water leaves from system II; and , H3 and T3 are mass flow rate, specific enthalpy and temperature of water leaves from system III, respectively.
25

## Slide 26: Cont’d
#Q1, Answer:
Given: Multiple systems without chemical reaction.
Input streams: kg/s, To= 45oC, kJ/s, kJ/s,
kJ/s
Output streams: kg/s, kg/s
Required: (a) the mass flow rates of each stream of system I, II & III, (b) the outlet temperatures from system I, II & III, and (c) the rate of overall change in enthalpy of multiple systems
26

## Slide 27: Cont’d
To determine integrated material and energy balances, you have to state your assumptions.
Assumptions:
The operation is carried out at steady state conditions.
There is no chemical reaction.
The specific heat capacity of water is constant in all temperatures.
The rates of change in kinetic energy, potential energy, and work done by the system all are negligible as compared with rates of heat addition and change in enthalpy.
27

## Slide 28: Cont’d
The process flows sheet for Activity 12.1 with boundary line is illustrated in Figure 12.6.
28
H2II
T2II
H1
T1
System I
System II
System III
kg/s
H0
T0= 45oC
H2
T2
= 12, 000 kJ/s
H1I
T1I
H3
T3
Figure 12.6 Integrated material and energy balances of multiple systems for Activity 12.1

## Slide 29: Cont’d
Overall material balances equation: The overall material balance equation is given by:
(12.18)
By rearranging equation (12.18), you can get:
(12.19)
By substituting the values of kg/s, kg/s and kg/s into equation (12.19), the of mass flow rate of water leaves from system III is calculated as:
kg/s
Hence, the mass flow rate of water leaves from system III is 385 kg/s.
29

## Slide 30: Cont’d
Overall energy balances equation: The overall energy balance equation is given by:
(12.20)
Where: is the rate of change in enthalpy, , and are the rates of heat added to system I, system II and system III, respectively.
By substituting the values of kJ/s, kJ/s and kJ/s into equation (12.20), the rate of change in enthalpy is calculated as:
kJ/s
Hence, the rate of overall change in enthalpy is 36, 000 kJ/s.
30

## Slide 31: Cont’d
System I: Integrated material and energy balances on system I for Activity 12.1 is depicted in Figure 12.7.
31
H1
T1
System I
kg/s
H0
T0= 45oC
kg/s
H1I
T1I
Figure 12.7 Integrated material and energy balances on system I for Activity 12.1

## Slide 32: Cont’d
Material balance equation: The material balance equation for system I is expressed by:
(12.21)
Where: , and are mass flow rates of water enters to system I, and leaves from it, respectively.
By substituting the values of kg/s and kg/s into equation (12.21), the mass flow rate of water leaves from system I and enters to system II () is determined as:
kg/s
32

## Slide 33: Cont’d
Energy balance equation: The energy balance equation for system I is expressed by:
(12.22)
But, H1 = H1I and T1= T1I since they are the same source.
(12.23)
(12.24)
Where: Cpw is specific heat capacity of water, T1 is outlet temperature of steam I and TR is reference temperature.
33

## Slide 34: Cont’d
By substituting equations (12.23& 12.24) into equation (12.22), and solving for the outlet temperature (T1), you can get:
(12.25)
By substituting the values of To= 45oC, kg/s, Cpw= 4.2 kJ/kg.oC and kJ/s into equation (12.25), the outlet temperature (T1) is calculated as:
oC
34

## Slide 35: Cont’d
System II: Integrated material and energy balances for system II for Activity 12.1 is depicted in Figure 12.8.
35
H2
T2
System II
kg/s
H1
T1= 48.4oC
kg/s
H2II
T2II
Figure 12.8 Integrated material and energy balances on system II for Activity 12.1

## Slide 36: Cont’d
Material balance equation: The material balance equation for system II is expressed by:
(12.26)
By substituting the values of kg/s and kg/s into equation (12.26), the mass flow rate of water leaves from system II and enters to system III () is determined as:
kg/s
36

## Slide 37: Cont’d
Energy balance equation: The energy balance equation for system II is expressed by:
(12.27)
But, H2 = H2II and T2= T2II since they are the same source.
(12.28)
(12.29)
Where: Cpw is specific heat capacity of water, T2 is outlet temperature of system II and TR is reference temperature.
37

## Slide 38: Cont’d
By substituting equations (12.28 & 12.29) into equation (12.27), and solving for the outlet temperature (T2), you can get:
(12.30)
By substituting the values of T1= 48.4oC, kg/s, Cpw= 4.2 kJ/kg.oC and kJ/s into equation (12.30), the outlet temperature (T2) is calculated as:
oC
38

## Slide 39: Cont’d
System III: Integrated material and energy balances for system III for Activity 12.1 is depicted in Figure 12.9.
39
H2
T3
System III
kg/s
H2
T2= 53.2oC
Figure 12.9 Integrated material and energy balances on system III for Activity 12.1

## Slide 40: Cont’d
Material balance equation: The material balance equation for system III is expressed by:
(12.31)
By substituting the values of kg/s into equation (12.31), the mass flow rate of water leaves from system III () is obtained as:
kg/s
Energy balance equation: The energy balance equation for system III is expressed by:
(12.32)
(12.33)
40

## Slide 41: Cont’d
(12.34)
By substituting equations (12.33 & 12.34) into equation (12.32), and solving for the outlet temperature (T3), you can get:
(12.35)
By substituting the values of T2= 53.2oC, kg/s, Cpw= 4.2 kJ/kg.oC and kJ/s into equation (12.35), the outlet temperature (T3) is calculated as:
oC
41

## Slide 42: 12.3. IMEBs for multiple systems with chemical reactions
To develop integrated material and energy balance equations, consider the following multiple systems with chemical reactions as shown in Figure 12.10.
42
Figure 12.10 Multiple systems with chemical reaction

## Slide 43: Cont’d
Where: Fio Fir, Fic, Fip and Fib are mole flow rates of species i enter to the reactor, leave from the reactor, leave from cooler and leave from separator in the top product and bottom product, respectively; and are rate of heat addition to the preheater and reactor, respectively; is work done by the reactor; To, T, Tr, Tc, Tp and Tb are temperatures enter to preheater, enter to the reactor, leave from the reactor, leave from cooler, and leave from separator to product and bottom product, respectively.
43

## Slide 44: Cont’d
Hio, Hi, Hir, Hic, Hip and Hib are specific enthalpies enter to preheater, enter to the reactor, leave from the reactor, leave from cooler, and leave from separator to top product and bottom product, respectively; and , , TR and Tcw are rate of heat removal by the cooler, mass flow rate of cooling water, input temperature of cooling water, and cooling water outlet temperature, respectively.
To develop integrated material and energy balance equations, first you have to state assumptions, and then you can consider the whole process as a single system, and divide the multiple systems into several single systems.
44

## Slide 45: Cont’d
Assumptions:
The whole process is operated at steady state condition.
The rates of the change in kinetic energy and potential energy are assumed negligible as compared with heat addition and heat of reaction.
There is no heat loss due to materials resistance.
Water at reference temperature is used as a coolant fluid.
Chemical reaction is only carried out in the reactor.
45

## Slide 46: Cont’d
A) Overall material and energy balances
By considering multiple systems as a single system, the material and energy balance equations are developed as follows:
Material balance equation: The overall material balance equation can be written as:
(12.36)
Where: Fip is the mole rate of species i in the top product, Fib is the mole rate of species i in the bottom product, Fio is the mole rate of species i in the feed, vi is stochiometric coefficient of species i, and  is extent of reaction.
46

## Slide 47: Cont’d
Energy balance equation: The overall energy balance equation is given by:
(12.37)
Where: and are rates of heat addition to preheater and reactor; is rate of work done by the reactor; Fio Fip and Fib are mole flow rates of species i enter to the reactor, leave from separator in top product and bottom product; Hio, Hip and Hib are specific enthalpies enter to preheater, and leave from separator to top product and bottom product, respectively; and is rate of heat removal by the cooler (Himmelblau, 2023, pg. 568-571).
47

## Slide 48: Cont’d
B) Integrated material and energy balances for each system
Preheater: Integrated material and energy balances on the preheater is shown Figure 12.11.
48
Figure 12.11 Integrated material and energy balances on the preheater

## Slide 49: Cont’d
Material balance equation: The material balance equation on the preheater is given by:
(12.38)
Energy balance equation: The energy balance equation on the preheater is expressed by:
(12.39)
Where: is rate of heat addition; Fio and Fi are the mole rates of species i in the input and output of the preheater, respectively; and Hio and Hi are the specific enthalpies of species i in the input and output streams of the preheater, respectively.
49

## Slide 50: Cont’d
Reactor: Integrated material and energy balances across reactor boundary line is shown Figure 12.12.
50
Figure 12.12 Integrated material and energy balances on the reactor

## Slide 51: Cont’d
Material balance equation: The material balance equation on the reactor can be written as:
(12.40)
Energy balance equation: The energy balance equation on the reactor can be written as:
(12.41)
Where: is rate of heat addition; is rate of work done; Fi and Fir are the mole rates of species i in the input and output of the reactor, respectively; vi is stochiometric coefficient of species i;  is extent of reaction; and Hi and Hir are the specific enthalpies of species i in the input and output streams of the reactor, respectively.
51

## Slide 52: Cont’d
Cooler: Integrated material and energy balance flows across cooler boundary line is depicted Figure 12.13.
52
Figure 12.13 Integrated material and energy balances on the cooler

## Slide 53: Cont’d
Material balance equation: The material balance equation on the cooler is expressed by:
(12.42)
Energy balance equation: The energy balance equation on the cooler is given by:
(12.43)
Where: is rate of heat removed by the cooler; Fir and Fic are the mole rates of species i in the input and output streams of the cooler, respectively; and Hir and Hic are the specific enthalpies of species i in the input and output streams of the cooler, respectively.
53

## Slide 54: Cont’d
The rate of heat removal by the cooler is given by:
(12.44)
Where: is rate of heat removed by the cooler; is mass flow rate of cooling water, Cpw is specific heat capacity of water, Tcw is temperature of cooling water after cooling operation, and TR is the input temperature of cooling water (reference temperature).
54

## Slide 55: Cont’d
Separator: Integrated material and energy balance flows across separator boundary line is illustrated Figure 12.14.
55
Figure 12.14 Integrated material and energy balances on the separator

## Slide 56: Cont’d
Material balance equation: The material balance equation on the separator is given by:
(12.45)
Energy balance equation: The energy balance equation on the separator is given by:
(12.46)
Where: Fic, Fip and Fib are the mole rates of species i in the input of separator, and output of the separator top product and bottom product, respectively; and Hic, Hip and Hib are the specific enthalpies of species i in the input of separator, and output of the separator top product and bottom product, respectively.
56

## Slide 57: Activity 12.2
1. The dehydrogenation of ethanol to form acetaldehyde is given by:
(g) (12.47)
The ethanol dehydrogenation reaction is carried out with the feed entering at 300oC. The feed contains 90% ethanol and the balance acetaldehyde and enters the reactor at a rate of 150 mol/s. To keep the temperature from dropping too much and thereby decreasing the reaction rate to an unacceptably low level, heat is transferred to the reactor. When the heat addition rate is 2,440kJ/s, the outlet temperature is 253oC. After chemical reaction, the outlet stream is passed through a cooler to recover heat using water as a coolant.
57

## Slide 58: Cont’d
Water is used as a coolant and enters to a cooler at 25oC, and the cooling water temperature is increased by 30oC. Calculate the change in enthalpy, the extent of reaction, the mole flow rates of each component in the reactor outlet stream, and mass flow rate of cooling water.
Additional data: The specific enthalpy of ethanol (H1F) at 300oC = -212. 19 kJ/mol, and the specific enthalpy of acetaldehyde (H2F) at 300oC = -147. 07 kJ/mol; and the specific enthalpy of ethanol (H1P) at 253oC = -216. 81 kJ/mol, the specific enthalpy of acetaldehyde (H2P) at 253oC = -150. 90 kJ/mol, and the specific enthalpy of hydrogen molecule (H3P) at 253oC = 6.595 kJ/mol (Richard M. Felder, 2005, pg. 458-460).
58

## Slide 59: Cont’d
#Q1, Answer:
Given: Chemical reaction with balanced stoichiometric equation:
(g)
Input stream: Feed is a mixture of ethanol and acetaldehyde with total feed rate of 150 mol/s, and 90% ethanol and 10% acetaldehyde at 300oC.
Heat added to the reactor 2, 440 kJ/s.
The specific enthalpy of ethanol (H1F) at 300oC = -212. 19 kJ/mol, and the specific enthalpy of acetaldehyde (H2F) at 300oC = -147. 07 kJ/mol.
59

## Slide 60: Cont’d
Reactor output stream: The outlet temperature for the reactor is 253oC. The specific enthalpy of ethanol (H1p) at 253oC = -216.81 kJ/mol, the specific enthalpy of acetaldehyde (H2p) at 253oC = -150.90 kJ/mol, and specific enthalpy of hydrogen molecule (H3p) at 253oC = 6.595 kJ/mol.
Cooler output stream: The specific enthalpy of ethanol (H1c) at 125oC = -108.4 kJ/mol, the specific enthalpy of acetaldehyde (H2c) at 125oC = -75.45 kJ/mol, and the specific enthalpy of hydrogen molecule (H3c) at 125oC = 3.280 kJ/mol.
Required: Calculate , , F and .
60

## Slide 61: Cont’d
Assumptions:
The reaction and cooling process is carried out at steady state condition.
The specific heat capacity of water (Cpw= 4.2 kJ/ kg.oC), which is constant.
It is assumed that the rates of the change in kinetic energy, potential energy, and work done by the system are neglected.
61

## Slide 62: Cont’d
The process flow diagram of integrated material and energy balances with chemical reaction is shown in Figure 12.15.
62
Figure 12.15 Integrated material and energy balances with reaction
Reactor
= 2, 440 kJ/s
H1p= -216.81 kJ/mol
H2p= -150.90 kJ/mol
H3p= 6.595 kJ/mol
Tp = 253oC
Fp = F1p + F2p + F3p
H1F= -212.19 kJ/mol
H2F= -147.07 kJ/mol
TF = 300oC
FF =150 mol/s
X1F= 0.90
X2F= 0.10
Cooler
H1c= -108.4 kJ/mol
H2c= -75.45 kJ/mol
H3c= 3.280 kJ/mol
Tc = 125oC
Fc = F1c + F2c + F3c
Tcw
TR

## Slide 63: Cont’d
Where: The subscripts “1, 2 and 3” refer to ethanol, acetaldehyde, and hydrogen molecule, respectively; the subscripts “F, p and c” refer to the feed stream, product stream and cooling stream, respectively; FF, FP and Fc are the mole flow rates for feed, product and cooling streams; TF, Tp and Tc are temperatures of feed, product and cooling streams; and HF, Hp and Hc are specific enthalpies in the feed, product and cooling streams, respectively.
63

## Slide 64: Cont’d
Material balance: The feed rate of ethanol: mol/s
The material balance equation of ethanol for the reactor is given by:
(12.48)
Where: F1P is the mole flow rate of ethanol in the product, and  is the extent of reaction.
The feed rate of acetaldehyde to the reactor: mol/s
The material balance equation of acetaldehyde for the reactor is given by:
(12.49)
Where: F2P is mole flow rate of acetaldehyde in the product, and  is the extent of reaction.
64

## Slide 65: Cont’d
The material balance equation for hydrogen molecule of the reactor is given by:
(12.50)
Where: F3P is mole flow rate of hydrogen molecule for product stream, and  is extent of reaction.
Energy balances: The energy balance on the reactor is given by:
(12.51)
Where: is rate of heat addition, and is the rate of change in enthalpy in the reactor.
It is given that the rate of heat addition is 2, 440 kJ/s.
 kJ/s
65

## Slide 66: Cont’d
The rate of change in enthalpy on the reactor can be written as:
(12.52)
The given values of the specific enthalpies, rate of heat addition, and mole flow rates are:
H1F= -212. 19 kJ/mol, H2F =-147. 07 kJ/mol, H3F = 0 (since no hydrogen molecule in the feed), H1P = -216. 81 kJ/mol, H2P = -150. 90 kJ/mol, and H3P = 6.595 kJ/mol, kJ/s,
F1F= 135 mol/s, and F2F= 15 mol/s
66

## Slide 67: Cont’d
By substituting the above values into equation (12.52), the energy balance equation becomes:
(12.53)
To determine the extent of reaction, you can substitute the material balance equations (12.48- 12.50) into energy balance equation (12.53).
mol/s
67

## Slide 68: Cont’d
Now, you can use the value of extent of reaction to calculate the mole flow rates of each component in the product stream of the reactor.
The mole flow rate of ethanol in the product stream (F1p) is calculated using equation (12.48) as: mol/s
The mole flow rate of acetaldehyde in the product is also determined using equation (12.49) as: mol/s
Similarly, the mole flow rate of hydrogen molecule in the product stream is determined using equation (12.50) as: mol/s
68

## Slide 69: Cont’d
To find the mass flow rate of cooling water required, you can determine integrated material and energy balance on the cooler as shown in Figure 12.16.
69
H1p= -216.81 kJ/mol
H2p= -150.90 kJ/mol
H3p= 6.595 kJ/mol
Tp = 253oC
Fp = F1p + F2p + F3p= 150 mol/s
Cooler
H1c= -108.4 kJ/mol
H2c= -75.45 kJ/mol
H3c= 3.280 kJ/mol
Tc = 125oC
Fc = F1c + F2c + F3c
Tcw
TR
Figure 12.16 Integrated material and energy balances on the cooler

## Slide 70: Cont’d
Material balances equation: Since there is no chemical reaction during cooling process, the mole rate of inputs is equal to the mole rate of outputs.
Ethanol balance: mol/s
Acetaldehyde balance: mol/s
Hydrogen molecule balance: mol/s
70

## Slide 71: Cont’d
Energy balances: The energy balance equation on the cooler is given by:
(12.54)
Where: is rate of heat addition, and is the rate of change in enthalpy in the cooler.
The rate of change in enthalpy through the cooler is expressed by:
kJ/s
From equation (12.54), you can get:
71

## Slide 72: Cont’d
The mass flow rate of cooling water is given by:
(12.55)
kJ/s, kJ/kg.oC, and T = Tcw-TR = 30oC
By substituting the above values into equation (12.55), you can get mass flow rate of cooling water as:
kg/s
72

## Slide 73: 12.4. Summary
Integrated material and energy balances for multiple systems involve a comprehensive approach to analyze the flow of materials and energy within interconnected processes.
The multiple systems can be interconnections of reactors, separators, and heat exchangers, which require integrated material and energy balances determination.
Careful review is required to avoid redundancy of equations when you develop integrated material and energy balance equations for multiple systems.
Integrated material and energy balances are commonly complex to perform calculations manually, which requires relevant software tools to solve balance equations.
73

## Slide 74: References
Basic Principles and Calculations in Chemical Engineering, Himmelblau, Pearson Education Inc, 9th edition, 2023.
Chemical Engineering Design, Volume 6, Coulson & Richardson’s, R. K. Sinnott, 3rd edition, 1999.
Elementary Principles of Chemical Processes, Richard M. Felder, John Wiley & Sons, 3rd edition, 2005.
74
Thank you!